## Slide 1: Faster Modular Exponentiation Using Double Precision Floating Point Arithmetic on the GPU
Niall Emmart, Fangyu Zheng, Charles Weems

## Slide 2: Talk Overview
Mod Exp is an important cryptographic primitive: RSA, digital signatures, prime generation, content centric networks, etc
Look at a simpler problem: big number multiplication
Computations can be done in the integer domain or floating point domain
Narrow Samples vs Wide Samples
Optimizations
Results
Question / Conjecture

## Slide 3: Big Num Multiplication – Narrow Samples
Given MP values A, and B, use floating point arithmetic for samples and column sums:
Ensure the column sums do not overflow the exact integer range.
Implies each samples uses less than half the floating point precision

## Slide 4: Big Num Multiplication – Wide Samples

## Slide 5: Computing a Dot-Product
Where a0 = 250, b0 = 250 and a1 = 1, b1 = 1
Desired result: H(sum) = 2100, L(sum) = 1

## Slide 6: Wide Samples
Use the full precision of the floating point value.
Well known fused-multiply-add technique can be used to compute high and low products of a sample as follows:
full_product(double a_sample, double b_sample) {
double hi, lo;
hi = __fma_rz(a_sample, b_sample, 0.0);
lo = __fma_rz(a_sample, b_sample, -hi);
return (hi, lo);
}

## Slide 7: Alignment Problem
Does not work well for computing dot products (or column sums):
Consider: a0 = 250, b0 = 250 and a1 = 1, b1 = 1
We have p0 = (2100, 0) and p1 = (1, 0)
Component-wise addition of p0 + p1 gives (2100, 0) not the desired (2100, 1)

## Slide 8: Alignment Problem -- Solution
Solution -- force the alignment of the high and low products:
Use 52 bit samples instead of 53
Add 2104 to high products and 252 to low products
full_product(double a_sample, double b_sample) {
double c1=2104, c2=2104+252, add;
hi = __fma_rz(a_sample, b_sample, c1); // high(a_samp*b_samp) + 2104
add = c2 – hi;
lo = __fma_rz(a_sample, b_sample, add); // low(a_samp*b_samp) + 252
return (hi, lo);
}

## Slide 9: Overflow Problem
Returning to our example: a0 = 250, b0 = 250 and a1 = 1, b1 = 1
We have p0 = (2104+2100, 252+0) and p1 = (2104+0, 252+1)
These are correctly aligned.
But we can’t use double precision for the sums – it will immediately overflow.

## Slide 10: A Slow Approach
full_product(double a_sample, double b_sample) {
double c1=2104, c2=2104+252, add;
hi = __fma_rz(a_sample, b_sample, c1);
add = c2 – hi;
lo = __fma_rz(a_sample, b_sample, add);
lo = lo - 252;
hi = (hi - 2104) * 2-52;
return ((uint64_t)hi, (uint64_t)lo);
}

## Slide 11: IEEE 754 – Double Precision Representation
Sign
bit
11 bit Exponent
with bias of 1023
52 bit mantissa, with implicit high bit (i.e., not stored in the bit representation).
If we store 2104+x, in a double (with rz rounding), where 0 ≤ x < 2104, then 2104 becomes the implicit bit and the 52-bit mantissa is exactly filled with .
Likewise, if we store 252 + y in a double, where 0 ≤ y < 252 then 252 becomes the implicit
bit and the 52-bit mantissa is exactly filled with y.

## Slide 12: Overflow Problem -- Solution
full_product(double a_sample, double b_sample) {
double c1 = 2104, c2 = 2104+252, sub;
uint64_t uhi, ulo, mask = 0xFFFFFFFFFFFFFull;
hi = __fma_rz(a_sample, b_sample, c1);
sub = c2 – hi;
lo = __fma_rz(a_sample, b_sample, sub);
uhi = to_u64(hi) & mask;
ulo = to_u64(lo) & mask;
return (uhi, ulo);
}

## Slide 13: Format Conversion – to_u64 function
uint64_t to_u64(double d) {
union {
double d;
uint64_t u64;
} converter;
converter.d=d;
return converter.u64;
}
Note: this is not equivalent to casting d as an unsigned integer: (uint64)d

## Slide 14: Returning to our example
Returning to our example: a0 = 250, b0 = 250 and a1 = 1, b1 = 1.
p0 = full_product(a0, b0)
p1 = full_product(a1, b1)
We have p0 = (248, 0) and p1 = (0, 1).
These can be added using component-wise addition, using unsigned 64-bit integers.

## Slide 15: Big Num Multiplication – Wide Samples

## Slide 16: MP Product Using Wide Samples
mp_product(double a_samples[], double b_samples[]) {
double c1 = 2104, c2 = 2104+252, sub;
uint64_t cols[2N] = {0}, mask = 0xFFFFFFFFFFFFFull;
for(i=0;i<N;i++) {
for(j=0;j<N;j++) {
hi = __fma_rz(a_sample[i], b_sample[j], c1);
sub = c2 – hi;
lo = __fma_rz(a_sample[i], b_sample[j], sub);
cols[i+j] += to_u64(lo) & mask;
cols[i+j+1] += to_u64(hi) & mask;
}
}
return cols;
}

## Slide 17: Optimization
Top 12 Bits
Top 12 bits are always constant. For high products, it’s 0x467, which is 104 + 1023 (the bias). For low
products it is always 0x433, which is 52 + 1023.
Since they are constant, we can add them to the column sums and by tracking the number of high and
low products, we can cancel them all out with a single subtractions.
The subtraction can even by avoided by initializing the column sum with the right magic value.

## Slide 18: MP Product – Optimized Version
mp_product(double a_samples[], double b_samples[]) {
double c1 = 2104, c2 = 2104+252, sub;
uint64_t cols[2*N];
// magic values to cancel high/low constants
for(i=0;i<N;i++) {
cols[i] = make_initial(i, i+1);
cols[2*N-1-i] = make_initial(i + 1, i);
}
for(i=0;i<N;i++)
for(j=0;j<N;j++) {
hi = __fma_rz(a_sample[i], b_sample[j], c1);
sub = c2 – hi;
lo = __fma_rz(a_sample[i], b_sample[j], sub);
cols[i+j] += to_u64(lo);
cols[i+j+1] += to_u64(hi);
}
return cols;
}

## Slide 19: Initial Value Routine
uint64_t make_initial(int high_count, int low_count) {
uint64_t value = 0x467*high_count + 0x433*low_count;
return –((value & 0xFFF)<<52);
}

## Slide 20: Mod Exp Implementation (lots of hand waving)
Parallel implementation with 4-8 GPU threads assigned to each Mod Exp instance
Uses a CIOS word-by-word Montgomery reduction
Take advantage of “free” bits to avoid Montgomery correction steps (See Orup [15] or Walter [16])
Modular exponentiation implemented with fixed window exponentiation

## Slide 21: Results
Performance of Modular Exponentiation on a GTX Titan Black GPU:

## Slide 22: Comparison to Prior Work

## Slide 23: Question / Conjecture / Future Work
Consider the case of A * B, where A and B are chains of doubles:
A = D0 -> D1 -> D2 -> … -> Dn-1
B = D0 -> D1 -> D2 -> … -> Dn-1
Can we beat the performance of the standard (53 bit) algorithm with normalization by using 52-bits samples, forcing Di -> Di+1 to be 52 bits apart and use the approach described in this paper?
Conjecture: Yes! We can do this in O(n2) steps

## Slide 24
Thank you!
Questions?