## Slide 1
Teaching Modules for
Steel Instruction
Beam Design
Developed by Scott Civjan
University of Massachusetts, Amherst

## Slide 2
FLEXURAL MEMBER/BEAM:
Member subjected to bending and shear.
Mb
Vb
Va
Ma
Notes: If also includes axial loads – handle as Beam Column – see Module #3
Typically horizontal members of a frame
Support gravity loads and distribute forces to columns
Also can provide column end restraint, distribute resistance to lateral loads

## Slide 3
Strength design requirements:
Mu  Mn (Ma  Mn/Ω) ASD
Vu  Vn (Va  Vn/Ω) ASD
Also check serviceability (under service loads):
Beam deflections
Floor vibrations
Notes: Note that subscript u= ultimate
n= nominal strength
Note that flexure typically controls strength design. Shear can control for shorter length “Deep Beams”
Longer spans and high live load make deflection and vibrations critical.
Generally design for critical condition independently, check others, revise as needed
Design is iterative.
Module will address each of these criteria separately (moment, shear, serviceability)

## Slide 4
Beam Members:
  Chapter F: Flexural Strength
  Chapter G: Shear Strength
  Chapter I: Composite Member Strength
  Part 3: Design Charts and Tables
  Chapter B: Local Buckling Classification

## Slide 5
Flexural Strength
Strength Limit States:
Plastic Moment Strength
Lateral Torsional Buckling
Local Buckling (Flange or web)
Notes: Each of these failure modes will be evaluated individually. The lowest strength will control design strength.

## Slide 6
Yield and Plastic Moments

## Slide 7
Moment can be related to stresses, , strains, , and curvature, .
Stress strain law -
Initially assume linearly elastic, no residual stresses
(for elastic only).
Plane sections remain plane -
Strain varies linearly over the height of the cross section (for elastic and inelastic range).
Assumptions:
Yield and Plastic Moments

## Slide 8
Strain
Stress
Fu
Fy
E
Esh
eY
.001 to .002
eu
.1 to .2
esh
.01 to .03
er
.2 to .3
Stress-strain law
Initially we will review behavior in this range
Assumed in Design
Elastic-Perfectly Plastic

## Slide 9
Plane sections remain plane.
9
Beam Theory
Yield and Plastic Moments
Notes: This allows for relationship between distance, strain, and stress through the cross section.
While variations will exist near boundaries, connections, etc. this is generally valid due to the ductile nature of steel.
9

## Slide 10
P = A = 0
Fi = A
Fi = 0
M = yA
M = yiFi
yi
dA
Centroid
Elastic Neutral Axis, ENA
Yield and Plastic Moments
Notes: For any shape we can set up equilibrium – the centroid is the elastic neutral axis (ENA).
This is the neutral axis during elastic loading for all shapes, but after yielding occurs it is only the neutral axis for sections loaded about an axis of symmetry.

## Slide 11
M
M
y
e
f
ymax
smax
ENA
11
Beam Theory
smax
Elastic Behavior:
Strain related to stress by Modulus of Elasticity, E
s = Ee
Yield and Plastic Moments
Notes: 11

## Slide 12
Beyond yield
Stress is constant
Strain is not related to stress
by Modulus of Elasticity E
Strain
Stress
Fy
E
eY
Now Consider what happens once some of the steel yields

## Slide 13
Increasing e
ey
Increasing s
Fy
Fy
Theoretically, reached at infinite strain.
13
Beam Theory
y
f
y
Beyond Elastic Behavior
Notes: The far right stress diagram, with essentially all of the section at yield stress, corresponds to the PLASTIC MOMENT (Mp). Due to ductile nature of steel, this can be reached in a typical section without fracture of the extreme fibers.
NOTE THAT stress=Mc/I IS NOT VALID
13

## Slide 14
Elastic Neutral Axis = Centroid
Plastic Neutral Axis –
If homogenous material (similar Fy), PNA divides Equal Areas, A1+A2/2.
For symmetric homogeneous sections, PNA = ENA = Centroid
14
Beam Theory
A1
A2
ENA
A1
y
x
A2/2
PNA
A1
A1
A2/2
x
yp
Yield and Plastic Moments
Notes: Use this slide to work an example for a symmetric shape
14

## Slide 15
15
Beam Theory
Yield Moment, My = (Ix/c)Fy = SxFy
Sx = Ix/c
c = y = distance to outer fiber
Ix = Moment of Inertia
Plastic Moment, Mp = ZxFy
Zx = AyA
For homogenous materials,
Zx = A iyi
Shape Factor = Mp/My
Yield and Plastic Moments
A1
A2
ENA
A1
y
x
A2/2
PNA
A1
A1
A2/2
x
yp
Notes: Use this slide to work an example for a symmetric shape
15

## Slide 16
Elastic Neutral Axis = Centroid
Plastic Neutral Axis ≠ Centroid
PNA divides equal forces in compression and tension.
If all similar grade of steel
PNA divides equal areas.
PNA
16
Beam Theory
A1
ENA
y
A2
A1
yp
A2
Yield and Plastic Moments
Notes: Use this slide to work an example of a non-symmetric shape
16

## Slide 17
17
Beam Theory
Plastic Moment, Mp = ZxFy
Zx = AyA = A iyi,
for similar material throughout the section.
Shape Factor = Mp/My
Yield Moment, My = (Ix/c)Fy = SxFy
Sx = Ix/c
c = y = distance to outer fiber
Ix = Moment of Inertia
PNA
A1
ENA
y
A2
A1
yp
A2
Yield and Plastic Moments
Notes: Use this slide to work an example of a non-symmetric shape
17

## Slide 18
With residual stresses, first yield actually occurs before My.
Therefore, all first yield
equations in the specification reference
0.7FySx
This indicates first yield 30% earlier than My.
For 50 ksi steel this indicates an expected residual stress of
(50 * 0.3) = 15 ksi.
Yield and Plastic Moments

## Slide 19
Moment
Mp
EI
f=curvature (1/in)
My
Mr
Including Residual Stresses
Consider what this does to the Moment-Curvature Relationship
Notes: Moment-curvature relationship is as shown for a beam
When Residual Stresses are considered, yield will occur prior to the yield moment My.
Yield initiates at Mr, with a decrease in stiffness at all points up until Mp is reached.
Note that the maximum strength is not changed, but the behavior leading up to this directly affects potential failure modes.

## Slide 20
Reduction in Stiffness affects the
failure modes and behavior prior to reaching Mp.
Actual service loads are typically held below or near to Mr
due to applied Load Factors (or Ω)
Yielding is not expected under normal service conditions.
In the case of overload the effects on strength are accounted for.

## Slide 21
Lateral Torsional Buckling
(LTB)

## Slide 22
LTB occurs along the length of the section.
Result is lateral movement of the compression flange and torsional twist of the cross section.
Compression flange tries to buckle as a column.
Tension flange tries to stay in place.
Lateral Torsional Buckling
Notes: Animations or demonstrations are very helpful in showing this failure mode.

## Slide 23
Lb is referred to as the unbraced length.
Braces restrain EITHER:
Lateral movement of compression flange or
Twisting in torsion.
Ma
Va
X
X
X
X
Lb
X’s denote lateral brace points.
Lateral Torsional Buckling
Mb
Vb

## Slide 24
Handout on Lateral Bracing
Lateralbeambracing.pdf

## Slide 25
FACTORS IN LTB STRENGTH
  Lb - the length between beam lateral bracing points.
  Cb - measure of how much of flange is at full compression within Lb.
  Fy and residual stresses (1st yield).
  Beam section properties - J, Cw, ry, Sx, and Zx.
Lateral Torsional Buckling
Notes: Where:
E= modulus of elasticity (29000 ksi)
G= Elastic Shear modulus (11500 ksi)
A= Area (in2)
Sx= elastic section modulus
Iy= moment of inertia about the y axis
J= St. Venants torsion constant (in4)
Cw= Warping torsion constant (in6)

## Slide 26
The following sections have inherent restraint against LTB
for typical shapes and sizes.
  W shape bent about its minor axis.
  Box section about either axis.
  HSS section about any axis.
For these cases LTB does not typically occur.
Lateral Torsional Buckling

## Slide 27
Local Buckling

## Slide 28
Handout on Plate Buckling
PlateBuckling.pdf

## Slide 29
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge
Failure is localized at areas of high stress
(Maximum Moment) or imperfections
Partial Restraint from Web

## Slide 30
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge
Failure is localized at areas of high stress
(Maximum Moment) or imperfections
Partial Restraint from Web

## Slide 31
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(Maximum Moment) or imperfections
Web is restrained by the flange at one edge, web in tension at other
Partial Restraint from Flange
Partial Restraint from
Web in Tension

## Slide 32
Local Buckling is related to Plate Buckling
Web is restrained by the flange at one edge, web in tension at other
Failure is localized at areas of high stress
(Maximum Moment) or imperfections
Partial Restraint from Flange
Partial Restraint from
Web in Tension

## Slide 33
If a web buckles, this is not necessarily a final failure mode. Significant post-buckling strength of the entire section may be possible (see advanced topics).
One can conceptually visualize that a cross section could be analyzed as if the buckled portion of the web is “missing” from the cross section.
Advanced analysis assumes that buckled sections are not effective, but overall section may still have additional strength in bending and shear.

## Slide 34
Local Web Buckling Concerns
Bending in the plane of the web;
  Reduces the ability of the web to carry its share of the bending moment (even in elastic range).
Support in vertical plane;
  Vertical stiffness of the web may be compromised to resist compression flange downward motion.
Shear buckling;
  Shear strength may be reduced.

## Slide 35
  Chapter F:
  Flexural Strength

## Slide 36
Fb = 0.90 (Wb = 1.67)
  Flexural Strength

## Slide 37
Specification assumes that the following failure modes have minimal interaction and can be checked independently from each other:
  Lateral Torsional Buckling(LTB)
  Flange Local Buckling (FLB)
  Shear
  Flexural Strength

## Slide 38
Local Buckling:
  Criteria in Table B4.1
  Strength in Chapter F: Flexure
  Strength in Chapter G: Shear
  Flexural Strength

## Slide 39
Local Buckling Criteria
Slenderness of the flange and web, l, are used as criteria to determine whether buckling would control in the elastic or inelastic range, otherwise the plastic moment can be obtained before local buckling occurs.
Criteria p and r are based on plate buckling theory.
For W-Shapes
FLB,  = bf /2tf pf = , rf =
WLB,  = h/tw pw = , rw =
  Flexural Strength

## Slide 40
  p “compact”
Mp is reached and maintained before local buckling.
fMn = fMp
p    r “non-compact”
Local buckling occurs in the inelastic range.
f0.7My ≤ fMn < fMp
 > r “slender element”
Local buckling occurs in the elastic range.
fMn < f0.7My
  Flexural Strength
  Local Buckling

## Slide 41
Mr = 0.7FySx
Mp = FyZx
lp
Equation F3-1 for FLB:
lr
l
Mn
Equation F3-2 for FLB:
or F4 and F5 (WLB)
Local Buckling Criteria
Doubly Symmetric I-Shaped Members
Note: WLB not shown. See Spec. sections F4 and F5.
(Straight Line) or F4 and F5 (WLB)

## Slide 42
Mr = 0.7FySx
Mp = FyZx
lp
Equation F3-1 for FLB:
lr
l
Mn
Equation F3-2 for FLB:
Local Buckling Criteria
Doubly Symmetric I-Shaped Members
42
Note: WLB not shown. See Spec. sections F4 and F5.
Rolled W-shape sections are dimensioned such that the webs are compact and flanges are compact in most cases. Therefore, the full plastic moment usually can be obtained prior to local buckling occurring.
Notes: 42

## Slide 43
The following slides assume:
  Compact sections
  Doubly symmetric members and channels
  Major axis Bending
  Section F2
  Flexural Strength
Notes: This corresponds to simply supported beams which include a floor slab. The majority of beams fall into this easy to design category.

## Slide 44
Only consider LTB as a potential failure mode prior to reaching the plastic moment.
LTB depends on unbraced length, Lb, and can occur in the elastic or inelastic range.
If the section is also fully braced against LTB,
Mn = Mp = FyZx Equation F2-1
When members are compact:
  Flexural Strength

## Slide 45
Mp = FyZx Equation F2-1
Mr = 0.7FySx
Lp = Equation F2-5
Lr = Equation F2-6
rts2 = Equation F2-7
ry =
For W shapes
c = 1 (Equation F2-8a)
ho = distance between flange centroids
When LTB is a possible failure mode:
Values of Mp, Mr, Lp and Lr are tabulated in Table 3-2

## Slide 46
Equation F2-2
Mr
Mp
Mn
Equation F2-3 and F2-4
Lb
Plastic LTB
Inelastic LTB
Elastic LTB
Lp
Lr
Lb
Lateral Brace
M = Constant (Cb=1)
Lateral Torsional Buckling
Strength for Compact
W-Shape Sections
X
X
Beam – AISC Manual 15th Ed

## Slide 47
If Lb > Lr,
Mn = FcrSx ≤ Mp Equation F2-3
Where Equation F2-4
If Lp < Lb  Lr,
Equation F2-2
Note that this is a straight line.
If Lb  Lp,
Mn = Mp
Assume Cb=1 for now

## Slide 48
Results are included only for:
W sections typical for beams
Fy = 50 ksi
Cb = 1
Plots of Mn versus Lb for Cb = 1.0 are tabulated,
Table 3-10
  Flexural Strength

## Slide 49
To compute Mn for any moment diagram,
Mn = Cb(Mn(Cb1))  Mp
Mn = Cb(Mn(Cb1))  Mp
(Mn(Cb1)) = Mn, assuming Cb = 1
Cb, Equation F1-1
  Flexural Strength

## Slide 50
Mmax = absolute value of maximum moment in unbraced section
MA = absolute value of moment at quarter point of unbraced section
MB = absolute value of moment at centerline of unbraced section
MC = absolute value of moment at three-quarter point of unbraced section
X
X
MA
MB
MC
Mmax
Shown is the section of the moment diagram between lateral braces.
  Flexural Strength
Notes: Note that Cb calculation results differ based on location of lateral bracing and shape of moment diagram

## Slide 51
X
X
X
X
X
Example
Consider a simple beam with differing lateral brace locations.
Note that the moment diagram is unchanged by lateral brace locations.
M
M
X – lateral brace location
  Flexural Strength
Notes: Note that Cb calculation results differ based on location of lateral bracing and shape of moment diagram

## Slide 52
Cb approximates an equivalent beam of constant moment.
X
X
Mmax
X
X
Mmax/Cb
M
M/2
M
M
M
Cb=1.0
Cb=1.25
Cb=1.67
Cb=2.3
M
  Flexural Strength
Notes: As the moment gradient increases, Cb increases, which also increases Mn
One can think of Cb transforming the maximum moment to an equivalent constant moment value for design purposes.

## Slide 53
Lateral Torsional Buckling
Strength for Compact W-Shape Sections
Effect of Cb
Mr
Mp
Mn
Lb
Lp
Lr
Cb=1
Increased by Cb
Cb>1
Limited by Mp

## Slide 54
Shear Strength

## Slide 55
Shear Strength
Failure modes:
Shear Yielding
Inelastic Shear Buckling
Elastic Shear Buckling

## Slide 56
Shear limit states for beams
Shear Yielding of the web:
Failure by excessive deformation.
Shear Buckling of the web:
Slender webs (large d/tw) may buckle prior to yielding.
Shear Strength

## Slide 57
Shear Stress,  = (VQ)/(Ib)
   = shear stress at any height on the cross section
  V = total shear force on the cross section
  Q = first moment about the centroidal axis of the area between the extreme fiber and where  is evaluated
  I = moment of inertia of the entire cross section
  b = width of the section at the location where  is evaluated
Shear Strength

## Slide 58
Handout on Shear Distribution
ShearCalculation.pdf
Shear Strength
Notes: This example shows why a W-shape can be designed independently for shear and moment, as the shear stresses are low in the flange, where the bending stresses are highest. Also note that for a simple span the maximum shear and moments occur at different locations along the span.

## Slide 59
Shear stresses generally are low in the flange area
(where moment stresses are highest).
For design, simplifying assumptions are made:
1) Shear and Moment stresses are independent.
2) Web carries the entire shear force.
3) Shear stress is simply the average web value.
i.e. web(avg) = V/Aweb = V/dtw
Shear Strength
Notes: Basis for the 1st is the distribution from the shear calculation handout.

## Slide 60
Yield defined by Mohr’s Circle
Yield defined by Mohr’s Circle
Shear Yield Criteria
Shear Strength

## Slide 61
Von Mises Yield defined by maximum distortion strain energy criteria (applicable to ductile materials):
For Fy = constant for load directions
Specification uses 0.6 Fy
Shear Yield Criteria
Shear Strength
Notes: For Von Mises criteria the energy of distortion is set equal to the failure for yielding in uniaxial tension. This results in shear yield criteria of approximately 0.6 the value of the tensile yield stress.

## Slide 62
Von Mises Failure Criterion
(Shear Yielding)
When average web shear stress V/Aweb = 0.6Fy
V = 0.6FyAweb
Shear Strength

## Slide 63
V
V
V
V
t
t
V
V
C
V
V
T
Shear Buckle
Shear buckling occurs due to diagonal compressive stresses.
Extent of shear buckling depends on h/tw of the web (web slenderness).
Shear Strength

## Slide 64
V
V
If shear buckling controls a beam section, the plate section which buckles can be “stiffened” with stiffeners. These are typically vertical plates welded to the web (and flange) to limit the area that can buckle. Horizontal stiffener plates are also possible, but less common.
No Stiffeners
Stiffener spacing = a
Potential buckling restrained by stiffeners
Potential buckling restrained by web slenderness
Shear Strength
Notes: Note that for shear stiffeners (as opposed to bearing type) the stiffener does not need to be welded to both flanges, which reduces the cost.

## Slide 65
V
V
When the web is slender, it is more susceptible to web shear buckling. However, there is additional shear strength beyond when the web buckles.
Web shear buckling is therefore not the final limit state.
The strength of a truss mechanism controls shear strength called “Tension Field Action.” Design for this is not covered in CEE434.
65
Beam Theory
Shear Strength
Compression can be carried by the stiffeners.
Tension can still be carried by the Web.
Shear Buckling of Web
Notes: Tension Field Action is a post buckling mechanism that is relied on to increase the overall shear strength. For very slender webs this post-buckling strength is significant.
This strength is often relied upon in built up beam sections.
Stiffeners must be properly designed to carry the compression forces – in addition to out of plane stiffness criteria for typical shear stiffener design.
65

## Slide 66
  Chapter G:
  Shear Strength

## Slide 67
Nominal Shear Strength
Vn = 0.6FyAwCv1 Equation G2-1
0.6Fy = Shear yield strength per Von Mises Failure Criteria
Aw = area of web = dtw
Cv1 = reduction factor for shear buckling
  Shear Strength

## Slide 68
Cv1 depends on slenderness of web and locations of shear stiffeners.
It is a function of kv.
Equation G2-5
  Shear Strength
a = clear distance between transverse stiffeners
h = clear distance between flanges minus fillet on a rolled shape
kv = 5.34 if no stiffeners are present or if a/h>3.0

## Slide 69
For a rolled I-shaped member
If
Then fv = 1.00 (W = 1.50)
Vn = 0.6FyAw (shear yielding) (Cv = 1.0)
  Shear Strength

## Slide 70
Otherwise, for other doubly symmetric shapes
If then Equation G2-4
If then Equation G2-3
fv = 0.9 (W =1.67)

## Slide 71
Equation G2-4 Cv1 reduction
0.6FyAw
Vn
h/tw
Shear Yielding
Shear Buckling
  Shear Strength

## Slide 72
  Chapter G:
  Shear Strength
  Transverse Stiffener Design
Advanced Beam: Shear - AISC Manual 15th Ed

## Slide 73
Shear Stiffener Design
All transverse stiffeners must provide sufficient out of plane stiffness to restrain web plate buckling
Research findings have shown that the stiffeners are loaded predominantly in bending due to the restraint they provide to the web, with only minor axial forces developing in the stiffeners. Stiffeners locally stabilize the web to allow for compression forces to be carried by the web. Therefore, additional stiffener moment of inertia is required. If Tension Field Action (TFA) is used a compression strut develops and balances the tension field, and results in an increase in stiffness requirements.
Advanced Beam: Shear - AISC Manual 15th Ed

## Slide 74
Detailing Requirements:
Can terminate short of the tension flange (unless bearing type)
Terminate web/stiffener weld between 4tw and 6tw from the fillet toe
Advanced Beam: Shear - AISC Manual 15th Ed
Ist is the required stiffness of the stiffener and is calculated about an axis in the web center for stiffener pairs, about the face in contact with the web for single stiffeners
Shear Stiffener Design
Notes: Typically design as double plate stiffeners (stiffener pairs).
The first detailing requirement is to save cost related to fit-up
The second is to avoid welds in the k-zone

## Slide 75
Requirements for stiffeners
Equation G2-12
Equation G2-13
Where
G2-12 limits the stiffness slenderness while the latter term in Equation G2-13 scales the required Ist to the amount of TFA required to meet the required shear strength Vr.
Advanced Beam: Shear - AISC Manual 15th Ed
Shear Stiffener Design
Notes: Force in the stiffener= Ps= (ttwa(sin))(sin)= (ttwa/2(1-cos2))= (ttwa/2)
this is then simplified by assuming a/h=1
=.5Fyw(1-Cv)atw(1-1/)= .15Fyw(1-Cv)atw
Then Ast=Ps/Fyst
an effective web area of 18tw(tw) can be subtracted from Ast
Any stiffener arrangement which meets all of the requirements is acceptable – often a minimum size based on available plate thickness is acceptable.

## Slide 76
Equation G2-14
Ist1= minimum moment of inertia required to develop full post buckling resistance of the stiffened web (capacity with TFA).
Equation G2-15
Ist2= minimum moment of inertia required to develop web shear buckling resistance (capacity without TFA).
Advanced Beam: Shear - AISC Manual 15th Ed
Shear Stiffener Design
Notes: Force in the stiffener= Ps= (ttwa(sin))(sin)= (ttwa/2(1-cos2))= (ttwa/2)
this is then simplified by assuming a/h=1
=.5Fyw(1-Cv)atw(1-1/)= .15Fyw(1-Cv)atw
Then Ast=Ps/Fyst
an effective web area of 18tw(tw) can be subtracted from Ast
Any stiffener arrangement which meets all of the requirements is acceptable – often a minimum size based on available plate thickness is acceptable.

## Slide 77
rst= the larger of Fyw/Fyst and 1.0
Vr= Required shear strength
Vc1= Available shear strength including TFA (per Section G2.2)
Vc2= Available shear strength without TFA
Advanced Beam: Shear - AISC Manual 15th Ed
NOTES: if TFA is neglected, Ist=Ist2
One can always conservatively design for Ist=Ist1
Shear Stiffener Design
Notes: Force in the stiffener= Ps= (ttwa(sin))(sin)= (ttwa/2(1-cos2))= (ttwa/2)
this is then simplified by assuming a/h=1
=.5Fyw(1-Cv)atw(1-1/)= .15Fyw(1-Cv)atw
Then Ast=Ps/Fyst
an effective web area of 18tw(tw) can be subtracted from Ast
Any stiffener arrangement which meets all of the requirements is acceptable – often a minimum size based on available plate thickness is acceptable.

## Slide 78
Beam Deflections

## Slide 79
Deflections :
  There are no serviceability requirements in AISC Specification.
  L.1 states limits “shall be chosen with due regard to the intended function of the structure” and “shall be evaluated using applicable load combinations.”

## Slide 80
Beam Deflections
Consider deflection for:
serviceability limit state
Camber calculations
Notes: Note that deflections are “serviceability” concern, so No Load factors should be used in calculations.
Camber= curvature applied to a beam during fabrication to allow it to be relatively straight (no deflection) when dead loads are applied (self weight, floor slab) – this allows for a flat floor of consistent depth in a completed structure. Note that this is not an exact process, so camber calculations to the nearest ½ inch are usually sufficient.

## Slide 81
Elastic behavior (service loads).
Limits set by project specifications.
Beam Deflections

## Slide 82
Typical limitation based on
Service Live Load Deflection
Typical criteria:
Max. Deflection, d= L/240, L/360, L/500, or L/1000
L = Span Length
Beam Deflections
Notes: Note that deflections are “serviceability” concern, so No Load factors should be used in calculations.

## Slide 83
Calculate deflection in beams from expected service dead load.
Result is a straight beam after construction.
Beam Deflections: Camber
Provide deformation in beam equal to a percentage of the dead load deflection and opposite in direction. It is important not to over-camber.
Specified on construction drawings.
Notes: Camber= curvature applied to a beam during fabrication to allow it to be relatively straight (no deflection) when dead loads are applied (self weight, floor slab) – this allows for a flat floor of consistent depth in a completed structure. Note that this is not an exact process, so camber calculations to the nearest ½ inch are usually sufficient.

## Slide 84
Beam without Camber
84
Beam Theory
Notes: 84

## Slide 85
Results in deflection in floor under Dead Load.
This can affect thickness of slab and fit of non-structural components.
d
85
Beam Theory
Notes: 85

## Slide 86
d
86
Beam Theory
d
Results in deflection in floor under Dead Load.
This can affect thickness of slab and fit of non-structural components.
Beam with Camber
Notes: 86

## Slide 87
87
Beam Theory
Results in deflection in floor under Dead Load.
This can affect thickness of slab and fit of non-structural components.
d
d
Cambered beam counteracts service dead load deflection.
Notes: 87

## Slide 88
Other topics including:
Composite Members
Slender Web Members
Beam Vibrations
Fatigue of Steel
Covered in CEE542…
Or you can download further slides (2010 manual) on these topics from http://www.aisc.org/content.aspx?id=24858