## Slide 1
Combined Load Member Design
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
Pa
Pb
Ma
Va
Mb
COMBINED FORCES:
Structural member subjected to axial load, bending and shear
Vb

## Slide 3
Combined Forces:
  Chapter H: Combined Forces
  Chapter C: Direct Analysis Method
  Chapter C: Other Analysis Requirements
  Appendix 7: Alternative Analysis Methods
  Appendix 8: Approximate 2nd Order Analysis
  Chapter B: Local Buckling Classification
  Part 6: Design Tables

## Slide 4
Combinations of flexural and axial forces need to be addressed in both analysis and design.
Analysis needs to consider second order effects (analysis based on final deformations).
Design needs to consider combinations of forces in a member.
COMBINED FORCES:

## Slide 5
Major Issues to Address:
Combination of multiple states of stress.
Second order load effects.
COMBINED FORCES:
Direct analysis versus traditional K methods.

## Slide 6
Combination of multiple states of stress:
Bending about the major and minor axis will combine to provide maximum stresses in the corner of a W shape.
Axial load will provide uniform stresses across the member and add to other maximum stresses.
s1=Mxcy/Ix
s3=P/A
s2=Mycx/Iy
(elastic range)

## Slide 7
Combination of multiple states of stress
Bending in each direction occurs simultaneously with associated shear stresses.
For elastic analysis one can superimpose stresses and arrive at a maximum value.
Once behavior becomes inelastic the resulting stresses are very difficult to calculate.
Actual design may include inelastic behavior and needs to account for residual stresses.

## Slide 8
Combination of multiple states of stress
Design provisions are simplified and rely on the inherent ductility of steel to redistribute stresses throughout the section.
The basic principle for design is an interaction equation which combines axial and bending forces with shear being checked independently.
Modes of failure from all independent modes are analyzed independently of other modes and forces. This does not capture complete behavior, but is sufficiently accurate for design purposes.

## Slide 9
DIRECT ANALYSIS
OR
“TRADITIONAL” METHODS
Analysis methods and design calculations are determined by the method used.
Direct Analysis applies additional “notional” loads and reduced member stiffness but uses K = 1 in column design.
Traditional method uses “notional” loads, calculated K values (alignment chart) in column design and nominal stiffness properties.

## Slide 10
Interaction Equations of Chapter H are applied for member design acceptance. Values used in these equations must be consistent with the analysis and design method used.
Direct Analysis Method (C1.1) or traditional methods (Appendix 7) may be used, but analysis and design must be consistent with the single approach chosen.
Combined Forces
Analysis and Design

## Slide 11
Doubly and Singly Symmetric Members:
  Flexure and Compression

## Slide 12
Combination of multiple states of stress:
Design provisions are simplified and rely on the inherent ductility of steel to redistribute forces throughout the section.
The basic principle for design is an interaction equation which combines forces from axial and bending loads. Shear is checked independently.
Modes of failure from all independent modes are analyzed independently of other modes and forces. This is not completely realistic, but is sufficiently accurate for design purposes.

## Slide 13
Equation H1-1b
Equation H1-1a
For
For
Doubly and Singly Symmetric Members:
Flexure and Compression

## Slide 14
Pr = required axial compressive strength from
2nd ORDER ANALYSIS
(from LRFD load combinations).
Pc = available design axial compressive strength per
LRFD (strength from Chapter E).
Mr = required flexural strength from
2nd ORDER ANALYSIS
(from LRFD load combinations).
Mc = available design flexural strength per
LRFD (strength from Chapter F).
x = strong axis bending
y = weak axis bending
Doubly and Singly Symmetric Members:
Flexure and Compression

## Slide 15
For uniaxial bending the interaction equations are depicted above (LRFD).
Uniaxial Flexural Load, Mu
Axial Load Pu
fcPn
fbMn
0.2fcPn
0.9fbMn
Pure axial or flexural load results in strength identical to Chapters E and F.

## Slide 16
Doubly and Singly Symmetric Members:
  Flexure and Tension

## Slide 17
The same equations are used for tension and compression.
(H1-1a and H1-1b)
Substitute:
Pr = required axial tensile strength
(from LRFD load combinations)
Pc = available design axial tensile strength per
LRFD (strength from Chapter D)
Additionally, for Mc
Cb can be increased per Section H1.2.
Lateral torsional buckling design strength increases due to tension.
Doubly and Singly Symmetric Members:
Flexure and Tension

## Slide 18
Analysis Requirements of AISC

## Slide 19
Second order analysis is required per C1.
Combined Forces
Analysis and Design
Geometric imperfections shall be considered.
Any rational method that accounts for both P-D and P-d is acceptable.
Second order analysis for LRFD uses load combinations.

## Slide 20
Typically computer analysis is used to calculate second order effects.
Combined Forces
Analysis and Design
P-d analysis can be neglected if requirements of Section C2.1(b) are met.
Many programs neglect P-d analysis.
Often not a significant effect, but this should be checked.

## Slide 21
Notional loads are applied to all load cases (Section C2.2b(1)) unless second order to first order drift ratio is ≤ 1.7. Then can apply notional loads only to gravity load combinations (Section C2-2b(d)).
Combined Forces
Analysis and Design
Initial imperfections must be considered, either through application of notional loads or direct modeling.
This last provision is applicable to the “traditional” method restrictions, therefore often requires the application of notional loads in fewer cases than the direct analysis method.

## Slide 22
Application of notional loads (Section C2-2b).
Ni = 0.002Yi
Ni = notional lateral load applied at level i
Yi = gravity load at level i from load combinations
Consider independently in two orthogonal directions.
This load accounts for assumed out-of-plumbness of 1/500, satisfying consideration of geometric imperfections in the analysis.
Combined Forces

## Slide 23
  Chapter C:
  Direct Analysis Method

## Slide 24
K = 1 for all design
Second order analysis (P-d and P-D) required, such as verified computer analysis or amplified first order analysis.
REQUIRED if D2nd Order/D1st Order > 1.5
(B2 > 1.5) (Section Appendix 7.2.1)
Analysis
Direct Analysis Method

## Slide 25
Stiffness adjustments are applied to all components that contribute to the stability of the structure (Section C2.3)
Stability is typically affected by flexural stiffness of members in moment frames and axial stiffness of braced frame components.
Direct Analysis Method
Reduce Stiffness EI* and EA* per Section C2.3:

## Slide 26
EI* = 0.8tbEI.
Required for all members that contribute to lateral stability of the structure (safe to include for all members).
E = modulus of elasticity
I = moment of inertia about axis of bending
tb = reduction factor for inelastic action
Direct Analysis Method
Reduce Stiffness EI* per Section C2.3:

## Slide 27
tb = Reduction Factor for Inelastic Action
for
for
Pr = required axial compressive strength
Py = FyA = member yield strength
a = 1.0 (LRFD), 1.6 (ASD)
Direct Analysis Method
Reduce Stiffness EI* per Section C2.3:
Equations C2-2a and C2-2b

## Slide 28
If an additional notional load of Ni = 0.001aYi is applied at all levels in all load combinations (even if Section C2.2b(d) applies),
tb = 1
per Section C2.3(c)
Direct Analysis Method
Reduce Stiffness EI* per Section C2.3:
Therefore, all stiffness could be adjusted similarly

## Slide 29
EA* = 0.8EA
E = modulus of elasticity
A = cross sectional member area
Required for all members that contribute to lateral stability of the structure (safe to include for all members).
Direct Analysis Method
Reduce Stiffness EA* per Section C2.3:

## Slide 30
  Chapter B:
  Local Buckling Criteria

## Slide 31
Local Buckling
Criteria Defined in Table B4.1
Since members are analyzed independently under flexural and axial loads, the local buckling provisions are checked separately for use in calculations related to each member type.
This does not directly address the combination of stresses which may make web local buckling less likely to occur for some load conditions.

## Slide 32
  2nd Order Effects Theory

## Slide 33
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Initially, consider a member subjected to flexure only.

## Slide 34
d0
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Initially, consider a member subjected to flexure only.
Application of load results in mid-span deflection d0,
from basic derivations.

## Slide 35
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Now consider the same member with Axial load P.
P
P

## Slide 36
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Axial force acting through deformations results in additional moment P(d0) at center of span.
d0

## Slide 37
Axial force acting through deformations results in additional moment P(d0) at center span.
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Additional moment then results in displacement d’.
P
P
37
d0
d’
Notes: 37

## Slide 38
Axial force acting through deformations results in additional moment P(d0) at center span.
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Additional moment then results in displacement d’.
P
P
38
d0
d’
Resulting in additional moment P(d’)
Notes: 38

## Slide 39
Axial force acting through deformations results in additional moment P(d0) at center span.
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Additional moment then results in displacement d’.
P
P
39
d0
d’
Resulting in additional moment P(d’)
Notes: 39

## Slide 40
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
This either results in an incremental failure, or stabilizes.
d > d0 and M > M0
M = M0 + Pd
but d depends on M…
where d0 and M0 are first order results based on original geometry.

## Slide 41
Second Order Effects
When considering a frame with loads applied at joints the same principles can be applied.
In these cases, we define joint deflections as D, with D0 being the first order joint deflection.

## Slide 42
Second Order Effects
P
P

## Slide 43
43
P
P
H
D0
Second Order Effects

## Slide 44
44
P
P
H
D0
D’
D
Second Order Effects

## Slide 45
Tension forces on a member tend to “straighten” the member. They do not introduce 2nd order effects.
Multiple states of stress are still present and need to be accounted for.
Tension in a member can also make lateral torsional buckling less likely to occur.
Tension forces and Flexure
Second Order Effects

## Slide 46
INDIVIDUAL MEMBERS
2nd Order Analysis Theory
Second Order Effects

## Slide 47
D0
H
Mmax= HL
Moment Diagram
L
Assuming deflections are in the shape of a sine curve
Second Order Effects

## Slide 48
D0
H
L
48
P
Mmax = HL + PD
D’
D
Assuming deflections are in the shape of a sine curve
Moment Diagram
Second Order Effects
Notes: 48

## Slide 49
D0
H
L
49
P
D’
D
, due to PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 49

## Slide 50
D0
H
L
50
P
D’
D
, due to PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 50

## Slide 51
D0
H
L
51
P
D’
D
, due to PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 51

## Slide 52
D0
H
L
52
P
D’
D
, due to PD
Since
, and
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 52

## Slide 53
D0
H
L
53
P
D’
D
, due to PD
Since
and
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 53

## Slide 54
Assuming deflections are in the shape of a sine curve
D0
H
L
54
P
D’
D
Mmax = HL + PD = M0 + PD
Second Order Effects
Notes: 54

## Slide 55
D0
H
L
55
P
D’
D
Mmax = HL + PD = M0 + PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 55

## Slide 56
D0
H
L
56
P
D’
D
Mmax = HL + PD = M0 + PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 56

## Slide 57
D0
H
L
57
P
D’
D
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 57

## Slide 58
D0
H
L
58
P
D’
D
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 58

## Slide 59
D0
H
L
59
P
D’
D
Assuming deflections are in the shape of a sine curve
For design Cm is usually taken equal to 1 for this condition (translation of member ends), calculated for the condition where deflections are within a member length (P-d).
Second Order Effects
Notes: 59

## Slide 60
H+PD/L
L
60
D
Note that the maximum moment is similar to this case:
Mmax = HL + PD
Moment Diagram
Second Order Effects
Notes: 60

## Slide 61
H+PD/L
L
61
D
Note that the maximum moment is similar to this case:
However, the shape of the moment diagram is slightly altered,
now assumed to be a straight line.
Previous case moment
Mmax = HL + PD
Moment Diagram
Second Order Effects
Notes: 61

## Slide 62
H+PD/L
L
62
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 62

## Slide 63
H+PD/L
L
63
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 63

## Slide 64
H+PD/L
L
64
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 64

## Slide 65
H+PD/L
L
65
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 65

## Slide 66
H+PD/L
L
66
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 66

## Slide 67
H+PD/L
L
67
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 67

## Slide 68
H+PD/L
L
68
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 68

## Slide 69
P
P
P
2H
H
H
D0
D’
D = (Amplification Factor)D0
The previous theory is applicable to deflections and moments within a single member.
General equations are similar.
69
D0
H
L
D’
D

## Slide 70
Amplification factors approach infinity as P approaches PE.
Axial Force, P
Amplification Factor
1.0
Pe
Second Order Effects

## Slide 71
Transverse Load on Beam
Mid Span Deflection, d
P = 0 No amplification of M or d
P1 > 0 Amplification of M and d
P2 = 2xP1 Amplification of M and d is GREATER than P1 results times 2
71
Therefore, can not superimpose results from different P values.
Second Order Effects
Notes: 71

## Slide 72
MEMBERS WITHIN STRUCTURE
Second Order Effects

## Slide 73
H
L
P4
P3
P2
P1
73
Note that in a full structure all displacements within a story are similar.
Second Order Effects
Notes: 73

## Slide 74
Note that in a full structure all displacements within a story are similar.
H
L
P4
P3
P2
P1
74
D
D
Second Order Effects
Notes: 74

## Slide 75
H
L
75
D
D
Note that in a full structure all displacements within a story are similar.
P4
P3
P2
P1
Second Order Effects
Notes: 75

## Slide 76
H
L
76
P4
P3
P2
P1
This concept is directly applicable to the case of “Leaner Columns” as discussed in the Compression Member module.
Second Order Effects
Notes: 76

## Slide 77
H
L
77
D
D
P4
P3
P2
P1
This concept is directly applicable to the case of “Leaner Columns” as discussed in the Compression Member module.
Second Order Effects
Notes: 77

## Slide 78
NOTIONAL LOADS

## Slide 79
Notional loads are a function of the gravity load being applied.
Notional loads are applied as a lateral load at each floor level in the direction that adds to the destabilizing effects of the load combination being considered.
Notional loads can account for geometric imperfections, inelasticity of members, and other non-ideal conditions.
NOTIONAL LOADS
Notional loads can be thought of as representing an initial out-of-plumbness in each story of the structure of 1/500 times the story height.

## Slide 80
Recall that a vertical load acting through a displacement, D, is similar to the application of a horizontal load PD/L.
Therefore, a notional load can be considered the equivalent effect of an assumed geometric imperfection, D.
H+PD/L
L
D
H
L
P
D
NOTIONAL LOADS

## Slide 81
MODELING ISSUES

## Slide 82
Second Order Effects
Final deflections and moments can be calculated in several different ways.
Closed form mathematical solutions:
Derivations exist for standard results, but very difficult, if not impossible, for a full structure.
Approximate Methods:
Amplification factor applied to first order displacement and moments by simple method
OR
approximate computer methods will provide results within a given tolerance.

## Slide 83
Amplified First Order Analysis
Computer Analysis
Exact Closed-Form Solution
2nd order analysis is any method that accounts for P-D and P-d effects.
Second Order Effects

## Slide 84
Exact solutions for P-d and P-D can be derived for simple structures.
Exact Closed-Form Solution
For full structures typically encountered in design the process is generally too tedious to perform.

## Slide 85
Most structural analysis programs will include some form of “second order” analysis.
To satisfy a “rigorous 2nd order analysis” a program must include both P-D and P-d analysis, or the designer must verify that P-d effects are minimal in the structure.
Computers use approximate solutions rather than exact closed form solutions, and iterate until a specified error tolerance is reached.
Computer Analysis

## Slide 86
Verify that load combinations include second order effects. Some programs analyze individual load cases only. Load case results are factored and summed to produce load combinations, but are not re-analyzed.
Designers must verify that second order effects are correctly handled by the programs being used.
Therefore, moments resulting from lateral loads in one load case may not be correctly amplified by axial load in a separate load case when combined in a load combination.
Computer Analysis

## Slide 87
Verify computer programs correctly analyze load combinations.
87
H
P
P
+
Load Case 2
Load Case 1
Computer Analysis

## Slide 88
Verify computer programs correctly analyze load combinations.
88
P
P
H
Compare 2nd order analysis from the load combination and load case 3. If results are identical, the program correctly includes 2nd order analysis in load combinations.
Load Combination (LC1+LC2)
OR
Load Case 3
H
P
P
+
Load Case 2
Load Case 1
Computer Analysis

## Slide 89
Designers must verify that second order effects are correctly handled by the programs being used.
89
Computer Analysis

## Slide 90
Most programs only include P-D. If P-d effects are significant the designer can use multiple elements to provide equivalent P-D effects within the original element.
Designers must verify that second order effects are correctly handled by the programs being used
To determine the capabilities of a specific program compare first and second order analysis results for known load cases – typically a flagpole (P-D) and simple beam (P-d) with axial and lateral loads applied. (Figures C-C2.2 and C-C2.3)
Computer Analysis

## Slide 91
Computer Analysis
P
P
H
Some computer programs do not analyze P-d effects such as the case shown.
d

## Slide 92
92
P
P
H
Some computer programs do not analyze P-d effects such as the case shown.
d
P
P
H
Provide additional joints in the member.
Member shown is now made up of 4 shorter members.
Computer Analysis

## Slide 93
93
P
P
H
Some computer programs do not analyze P-d effects such as the case shown.
d
P
P
H
Provide additional joints in the member
(Member shown is now made up of 4 shorter members)
D1
D1
D2
P-d analysis of the overall member is now analyzed as P-D analysis of each individual member, which most programs will be able to analyze.
Such an analysis is only required for members which will have significant P-d effects
Computer Analysis

## Slide 94
Braced frames with pinned member connections:
If loads applied at the nodes, members are subjected to axial forces only.
Combined Forces
Beams and girders may be subjected to combined forces, but designers should take care in understanding whether analysis results represent compressive forces present in the steel section or carried by the floor slab.

## Slide 95
Moment frames with fixed member connections:
Most if not all members will be subjected to a combination of axial forces, flexure and shear.
Combined Forces

## Slide 96
  Appendix 8:
  Approximate Second- Order Analysis

## Slide 97
Amplified First Order Analysis
Amplification of First-Order Elastic Analysis
This method is typically used in the following situations:
Appendix 8
To analyze and design simple structures being performed by hand calculations.
To verify second order results in computer analyses.
To determine the significance of P-d effects (B1 factor).
Basis for the factors is in 2nd order analysis theory slides

## Slide 98
Mr = B1Mnt + B2Mlt Equation A-8-1
Mr = second order required flexural strength
B1 = amplification factor to account for second order effects caused by displacements along member length (P-d effects).
Mnt = first order moment, assuming no lateral translation of frame (from load combinations).
B2 = amplification factor to account for second order effects caused by displacements of member ends (P-D effects).
Mlt = first order moment caused by lateral translation of frame (from load combinations).
Amplified First Order Analysis

## Slide 99
99
Amplified First Order Analysis
Pr = Pnt + B2Plt Equation A-8-2
Pr = second order required axial strength.
Pnt = first order axial force, assuming no lateral translation of frame (from load combinations).
B2 = amplification factor to account for second order effects caused by displacements of member ends (P-D effects).
Plt = first order axial force caused by lateral translation of frame (from load combinations).
Notes: 99

## Slide 100
Equation A-8-3
Note that:
in the plane of bending being considered for moment amplification.
Lc1=K1 L= 1L or less since there is no end translation.
a=1 for LRFD design
a=1.6 for ASD design
Amplified First Order Analysis

## Slide 101
For cases where loads are present transverse to the member:
y from Table C-A-8.1
For cases where member has end moment only (no transverse loads applied):
Cm = 0.6 - 0.4(M1/M2) Equation A-8-4
M1 = smaller first order end moment
M2 = larger first order end moment
Amplified First Order Analysis

## Slide 102
(largest possible value)
(smallest possible value)
M1
M1
M1
M2=M1
M2=-M1
Amplified First Order Analysis

## Slide 103
or
Equations A-8-6 through A-8-8
Note that:
in the plane of bending being considered for moment amplification.
K2 ≥ 1 as calculated for end translation.
a=1 for LRFD design
a=1.6 for ASD design
Amplified First Order Analysis

## Slide 104
Amplified First Order Analysis

## Slide 105
105
Amplified First Order Analysis
Combined Forces will cause Mnt and Mlt in a structure.

## Slide 106
106
To determine Mnt and Pnt, restrain lateral movement at each story.
Amplified First Order Analysis

## Slide 107
107
To determine Mnt and Pnt, restrain lateral movement at each story.
Amplified First Order Analysis

## Slide 108
108
To determine Mnt and Pnt, restrain lateral movement at each story.
Amplified First Order Analysis
Resulting reactions at each story are required to resist the lateral translation of the structure.

## Slide 109
109
To determine Mnt and Pnt, restrain lateral movement at each story.
Amplified First Order Analysis
Resulting reactions at each story are required to resist the lateral translation of the structure.
Resulting Moments and Axial Forces are Mnt and Pnt respectively.

## Slide 110
To determine Mlt and Plt, apply the resulting reaction at each story.
110
Amplified First Order Analysis

## Slide 111
To determine Mlt and Plt, apply the resulting reaction at each story.
111
Amplified First Order Analysis
R3
R2
R1

## Slide 112
To determine Mlt and Plt, apply the resulting reaction at each story.
112
Amplified First Order Analysis
R3
R2
R1
Resulting moments and axial forces are Mlt and Plt respectively.

## Slide 113
DIRECT ANALYSIS METHOD
COMPARISON TO
TRADITIONAL (K FACTOR) METHOD

## Slide 114
DIRECT ANALYSIS METHOD
Analysis of entire structure interaction.
Additional lateral “Notional” loads.
No K values required.
Reduced stiffness of structure.
Notes: Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.

## Slide 115
Moment, M
Axial Force, P
Initially consider a “traditional” analysis
115
DIRECT ANALYSIS METHOD
Notes: 115

## Slide 116
Moment, M
Axial Force, P
Initially consider a “traditional” analysis
116
PnKL
Py
Axial strength is defined as PnKL which includes K factors (Py indicates crushing).
DIRECT ANALYSIS METHOD
Notes: 116

## Slide 117
Moment, M
Axial Force, P
Initially consider a “traditional” analysis
117
PnKL
Py
Axial strength is defined as PnKL which includes K factors (Py indicates crushing).
Bending Strength is defined as Mn, assumed here to be Mp for a laterally braced member.
Mp
DIRECT ANALYSIS METHOD
Notes: 117

## Slide 118
Moment, M
Axial Force, P
118
PnKL
Py
Mp
Pu
Mu
Elastic 2nd Order
Traditional design accounts for interaction by calibrating the member design to column curves.
DIRECT ANALYSIS METHOD
Notes: 118

## Slide 119
Moment, M
Axial Force, P
119
PnKL
Py
Mp
Pu
Mu
Elastic 2nd Order
Traditional design accounts for interaction by calibrating the member design to column curves.
Actual Response
Actual response produces a higher internal moment in the member. This is accounted for in calibrating the member check, but does not get transferred into adjacent members and connections.
DIRECT ANALYSIS METHOD
Notes: 119

## Slide 120
Moment, M
Axial Force, P
120
PnKL
Py
Mp
Pu
Mu
Elastic 2nd Order
Actual Response
DIRECT ANALYSIS METHOD
Notes: 120

## Slide 121
Moment, M
Axial Force, P
121
Now consider the “Direct” analysis
DIRECT ANALYSIS METHOD
Notes: 121

## Slide 122
Moment, M
Axial Force, P
122
Py
Now consider the “Direct” analysis
PnL
Axial strength is defined as PnL which assumes K=1 for all cases.
DIRECT ANALYSIS METHOD
Notes: 122

## Slide 123
Moment, M
Axial Force, P
123
Py
Now consider the “Direct” analysis
PnL
Axial strength is defined as PnL which assumes K=1 for all cases.
Mp
Bending strength is defined as Mn, assumed here to be Mp for a laterally braced member.
DIRECT ANALYSIS METHOD
Notes: 123

## Slide 124
Moment, M
Axial Force, P
124
Py
Now consider the “Direct” analysis
PnL
Axial strength is defined as PnL which assumes K=1 for all cases.
Mp
Bending strength is defined as Mn, assumed here to be Mp for a laterally braced member.
PnKL
Therefore, design curve is shifted upwards from traditional assumptions.
DIRECT ANALYSIS METHOD
Notes: 124

## Slide 125
Moment, M
Axial Force, P
125
Py
PnL
Mp
Pu
Mu
Elastic 2nd order (direct analysis includes notional loads and reduced stiffness).
Direct analysis accounts for interaction by including additional lateral “notional” loads and reducing the frame stiffness thus calibrating the member design to K = 1 analysis.
DIRECT ANALYSIS METHOD
Notes: 125

## Slide 126
Moment, M
Axial Force, P
126
Py
PnL
Mp
Pu
Mu
Elastic 2nd order (direct analysis includes notional loads and reduced stiffness).
Actual Response
Actual response then should match the internal moment, transferring this moment into adjacent members and connections during analysis.
DIRECT ANALYSIS METHOD
Direct analysis accounts for interaction by including additional lateral “notional” loads and reducing the frame stiffness thus calibrating the member design to K = 1 analysis.
Notes: 126

## Slide 127
Moment, M
Axial Force, P
DIRECT ANALYSIS METHOD
127
Py
PnL
Mp
Pu
Mu
Elastic 2nd order (direct analysis includes notional loads and reduced stiffness).
Actual Response
Notes: 127

## Slide 128
Direct Analysis and Traditional methods are valid for design.
DIRECT ANALYSIS METHOD
The Direct Analysis method has been calibrated for typical building structures. Unusual structures (such as a cantilever with compression and bending) may require additional calibration.
Each is reliant on calibration to match the response curves shown on previous slides.

## Slide 129
DIRECT ANALYSIS METHOD
Analysis and Calibration
With proper calibration design strength approaches the actual response.
Calibration consists of a combination of notional load values and reduction in member stiffness.
Analysis is referenced to K = 1 member capacities.