## Slide 1
Compression Member Design
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
COMPRESSION MEMBER/COLUMN:
Structural member subjected to axial load
P
P
Notes: Note that “column” is used in these slides interchangeably for “compression member”. This is not technically correct, but was adopted based on nomenclature in existing modules. Members are designed for the type of force in the member and a “column” in a structure could have compression or tension in the member depending on the load conditions. However, compression members are typically controlled by compression while the connections may require additional attention to tension loads.
If also includes flexural loads – handle as Combined Load – see Module #3
Typically vertical members of a frame, such as columns, braces, truss members

## Slide 3
Compression Members:
  Chapter E: Compression Strength
  Chapter I: Composite Member Strength
  Part 4: Design Charts and Tables
  Chapter C: Analysis Issues

## Slide 4
Strength design requirements:
Pu  Pn (Pa  Pn/Ω)ASD
Where  = 0.9 for compression
(Ω = 1.67)ASD
Notes: Note that subscript u= ultimate foREVISE FOR ASD/LRFD
Note that flexure typically controls strength design. Shear can control for shorter length “Deep Beams”
Generally design for critical condition independently, check others, revise as needed
Design is iterative.
Module will address each of these criteria separately (moment, shear, serviceability)

## Slide 5
Axial Strength
Strength Limit States:
Squash Load
Global Buckling
Local Buckling
Notes: Each of these limit states will be evaluated individually. The lowest strength will control design strength.
Define buckling is the loss of compressive load carrying capacity resulting from a change in the geometry of the member, this differs somewhat from a classical approach of defining buckling as a bifurcation point, but as we will see a true bifurcation point is generally not realized in an actual member.
Global buckling will typically limit strength. For very short “stub” columns, or fully braced sections (such as buckling restrained bracing) reaching the “squash load” can control. Local buckling can control members with slender elements (flange or web)

## Slide 6
Global Buckling
Local Flange Buckling
Local Web Buckling
Notes: Each of these failure modes will be evaluated individually. The lowest strength will control design strength.
Define buckling is the loss of compressive load carrying capacity resulting from a change in the geometry of the member, this differs somewhat from a classical approach of defining buckling as a bifurcation point, but as we will see a true bifurcation point is generally not realized in an actual member.
Global buckling will typically limit strength. For very short “stub” columns, or fully braced sections (such as buckling restrained bracing) crushing can control. Local buckling can control members with slender elements (flange or web)

## Slide 7
INDIVIDUAL COLUMN
Notes: Initially it’s easiest to describe behavior of an individual column, then introduce the role and analysis of a column within an entire structure. The full structure can be conceptualized as varying the end conditions of individual columns.

## Slide 8
Squash Load
Fully Yielded Cross Section

## Slide 9
When a short, stocky column is loaded the strength is limited by the yielding of the entire cross section.
Absence of residual stress, all fibers of cross-section yield simultaneously at P/A=Fy.
D
P=FyA
eyL0
P
P
D
L0
Notes: Crushing is often called the “squash load”, the load at which the entire cross section would yield.

## Slide 10
Results in a reduction in the effective stiffness of the cross section, but the ultimate squash load is unchanged.
Reduction in effective stiffness can influence onset of buckling.
RESIDUAL STRESSES

## Slide 11
D
P=FyA
eyL0
No Residual Stress
11
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
RESIDUAL STRESSES
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
11

## Slide 12
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
12
P=(Fy-Fres)A
1
No Residual Stress
= Yielded
Steel
1
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
12

## Slide 13
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
13
P=(Fy-Fres)A
1
= Yielded
Steel
2
No Residual Stress
1
2
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
13

## Slide 14
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
14
P=(Fy-Fres)A
1
= Yielded
Steel
1
2
2
3
3
No Residual Stress
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
14

## Slide 15
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
P=(Fy-Fres)A
1
= Yielded
Steel
1
2
2
3
3
Effects of Residual Stress
4
15
4
No Residual Stress
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
15

## Slide 16
Euler Buckling

## Slide 17
Assumptions:
Column is pin-ended.
Column is initially perfectly straight.
Load is at centroid.
Material is linearly elastic (no yielding).
Member bends about principal axis (no twisting).
Plane sections remain Plane.
Small Deflection Theory.
Euler Buckling
Notes: A handout from any structural analysis text is worthwhile to show the derivation of the Euler Buckling Equation.

## Slide 18
e
s
E
D
P
Stable Equilibrium
Bifurcation Point
D
Euler Buckling
P
Notes: At the bifurcation point the member is mathematically indifferent between carrying additional load with no deflection or deflecting with no additional load strength. However, any actual member will have some perturbation (slight out of straightness or imperfect end conditions, etc.) which will make additional load impossible. It is also important to note that while the load deflection plots are typically shown as above, the theory is only valid for small deflections. Therefore the plot does not accurately describe actual column behavior.

## Slide 19
Dependant on Imin and L2.
Independent of Fy.
L
PE
Minor axis buckling
For similar unbraced length in each direction,
“minor axis” (Iy in a W-shape) will control strength.
19
Major axis buckling
Euler Buckling
Notes: Euler Buckling plot of strength versus column length for a W-shape – note that each axis has a different strength – the lowest controls. Often a demonstration of buckling of an I-shape foam beam or slender ruler is effective. Students intuitively understand the controlling buckling axis-this plot provides a descriptive justification.
19

## Slide 20
PE =
divide by A, PE/A = , then with r2 = I/A,
PE/A = FE =
FE = Euler (elastic) buckling stress
L/r = slenderness ratio
Re-write in terms of stress:
Euler Buckling

## Slide 21
Buckling controlled by largest value of L/r.
Most slender section buckles first.
L/r
FE
Fy
Euler Buckling
Notes: For a given column length, the maximum value of L/r will occur when r is a minimum.
For a given column shape, the maximum value of L/r will occur when L is a maximum

## Slide 22
EULER ASSUMPTIONS
(ACTUAL BEHAVIOR)

## Slide 23
0 = initial mid-span deflection of column
Initial Crookedness/Out of Straight
P
P
M = PDo
Do
Do
Notes: First, what are the effects of a column that is not perfectly straight as expected by the Euler Buckling derivation? ASTM limits are noted to show that these are expected in an actual shape. The ASTM limits may change in the future, but the concept is the same regardless of the limiting value. An initial displacement D0, causes an initial moment along the length of the section, Pd. This is greatest at the location of maximum deflection. Elastic theory then predicts the solid line in the plot to the right. Actual behavior, shown as the dashed line, is due to the additional effects of inelastic behavior. Yielding occurs from a combination of stresses due to moment and axial loads.

## Slide 24
D
P
Do= 0
Do
Initial Crookedness/Out of Straight

## Slide 25
D
P
Do= 0
Do
Elastic theory
25
Initial Crookedness/Out of Straight

## Slide 26
D
P
Do= 0
Do
Elastic theory
26
Actual Behavior
Initial Crookedness/Out of Straight
Notes: 26

## Slide 27
Buckling is not instantaneous.
ASTM limits of 0 = L/1000 or 0.25” in 20 feet
Typical values are 0 = L/1500 or 0.15” in 20 feet
Additional stresses due to bending of the column,
P/A  Mc/I.
Assuming elastic material theory (never yields),
P approaches PE.
Actually, some strength loss
small 0 => small loss in strengths
large 0 => strength loss can be substantial
Initial Crookedness/Out of Straight
Notes: The first of these (along with the ductility of steel shapes) usually allows for some warning prior to a column failure. It also means that a column limited by “buckling” does not exhibit the classical instantaneaous buckling “failure” at a bifurcation point.

## Slide 28
D
P
e
L
D
Load Eccentricity
28
D
P
Do= 0
Elastic theory
Notes: An initial load eccentricity, e, causes an initial moment along the length of the section, (Pe at the top). This is a similar effect to that of an initial out-of-straightness, namely the introduction of a moment in addition to the purely axial loading. Elastic theory then predicts the solid line in the plot to the right. Actual behavior, shown as the dashed line, is due to the additional effects of inelastic behavior. Yielding occurs from a combination of stresses due to moment and axial loads.
28

## Slide 29
D
P
e
L
D
Load Eccentricity
29
D
P
Do= 0
Elastic theory
Actual Behavior
Notes: An initial load eccentricity, e, causes an initial moment along the length of the section, (Pe at the top). This is a similar effect to that of an initial out-of-straightness, namely the introduction of a moment in addition to the purely axial loading. Elastic theory then predicts the solid line in the plot to the right. Actual behavior, shown as the dashed line, is due to the additional effects of inelastic behavior. Yielding occurs from a combination of stresses due to moment and axial loads.
29

## Slide 30
If moment is “significant” section must be designed as a member subjected to combined loads.
Buckling is not instantaneous.
Additional stresses due to bending of the column,
P/A  Mc/I.
Assuming elastic material theory (never yields),
P approaches PE.
Actually, some strength loss
small e => small loss in strengths
large e => strength loss can be substantial
Load Eccentricity
Notes: Note that “significant” moment is difficult to define. Most computer software design all members as beam-columns. The latter slides on columns address analysis methods where sections are analyzed as beam-columns for all cases. It is good to have students start thinking about the effects of moment on axial member design so they understand the concepts when beam-columns are introduced.

## Slide 31
Similar to pin-pin, with L’ = L/2.
Load Strength =
4 times as large.
EXAMPLE
KL
Set up equilibrium and solve similarly to Euler buckling derivation.
Determine a “K-factor.”
End Restraint (Fixed)
Notes: A derivation of the above example is provided in many structural analysis texts subsequent to the Euler Buckling strength derivation, and is found similarly. Charts of effective lengths and K-factors can be found in steel design texts and the AISC code as well.

## Slide 32
Length of equivalent pin ended column with similar elastic buckling load,
Effective Length = KL
End Restraint (Fixed)
Distance between points of inflection in the buckled shape.

## Slide 33
Handout on K-factors
EquivalentLength.pdf

## Slide 34
Fy
ET= Tangent Modulus
E
(Fy-Fres)
e
s
Test Results from an Axially Loaded Stub Column
Inelastic Material Effects
Notes: Inelastic material effects occur whenever axial stress in any portion of the cross section exceeds the first yield of the material (including residual stresses). This also compounds effects of out of straightness and load eccentricity, as the bending moment term introduced also results in longitudinal stresses.

## Slide 35
KL/r
Inelastic Material Effects
s
35
Elastic Behavior
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
35

## Slide 36
KL/r
s
36
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
36

## Slide 37
KL/r
s
37
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
37

## Slide 38
Elastic Buckling: ET = E
No yielding prior to buckling
Fe  Fy-Fres(max)
Fe = predicts buckling (EULER BUCKLING)
Two classes of buckling:
Inelastic Buckling:
Some yielding/loss of stiffness prior to buckling
Fe > Fy-Fres(max)
Fc - predicts buckling (INELASTIC BUCKLING)
Inelastic Material Effects

## Slide 39
Fy
KL/r
Experimental Data
Overall Column Strength
Notes: In general, the differences observed in testing of columns from Euler Buckling predicted capacities are as follows: Columns of low slenderness ratios are governed by inelastic buckling, and limited by crushing capacities. Columns of high slenderness ratios are limited by out of straightness effects. Columns of intermediate slenderness ratios see a combination of these effects.

## Slide 40
Fy
KL/r
Experimental Data
Inelastic Material effects
Including Residual Stresses
Out of Straightness
Overall Column Strength
40
Notes: In general, the differences observed in testing of columns from Euler Buckling predicted capacities are as follows: Columns of low slenderness ratios are governed by inelastic buckling, and limited by crushing capacities. Columns of high slenderness ratios are limited by out of straightness effects. Columns of intermediate slenderness ratios see a combination of these effects.
40

## Slide 41
Major factors determining strength:
1) Slenderness (L/r).
2) End restraint (K factors).
3) Initial crookedness or load eccentricity.
4) Prior yielding or residual stresses.
Overall Column Strength
The latter 2 items are highly variable between specimens.

## Slide 42
  Chapter E:
  Compression Strength

## Slide 43
fc= 0.90 (Wc= 1.67)
Compression Strength

## Slide 44
Specification considers the following conditions:
  Flexural Buckling
  Torsional Buckling
  Flexural-Torsional Buckling
Compression Strength
Notes: Note that for W-shape and tube members, only global flexural buckling needs to be checked

## Slide 45
  Compressive Strength

## Slide 46
The following slides assume:
  Non-slender flange and web sections
  Doubly symmetric members
Compression Strength
Notes: This corresponds to simply supported beams which include a floor slab. The majority of beams fall into this easy to design category.

## Slide 47
Since members are non-slender and doubly symmetric,
flexural (global) buckling is the most likely potential failure mode prior to reaching the squash load.
Buckling strength depends on the slenderness of the section, defined as Lc/r.
Lc= KL = effective length of the member
The strength is defined as
Pn= FcrAg Equation E3-1
Compression Strength
Notes: Equation E3-1 defines the strength as an effective critical stress times the gross area of the cross section.
Fcr is therefore limited to Fy, which would indicate the squash load.

## Slide 48
Fe = elastic (Euler) buckling stress, Equation E3-4
If , then Fcr = 0.877Fe Equation E3-3
This defines the “elastic” buckling limit
with a reduction factor, 0.877, times the theoretical limit.
If , then . Equation E3-2
This defines the “inelastic” buckling limit.

## Slide 49
Lc/r
Inelastic Material Effects
s
49
Elastic Behavior
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
49

## Slide 50
s
50
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Lc/r
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
50

## Slide 51
s
51
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Lc/r
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
51

## Slide 52
s
52
Fy
Inelastic
Elastic
Inelastic Material Effects
0.44Fy
Lc/r
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
52

## Slide 53
Design Aids
Table 4-14
fcFcr as a function of Lc/r
Tables 4-1 to 4-13
fcPn as a function of Lcy
Useful for all shapes.
Larger Lc/r value controls.
Can be applied to Lcx by dividing Lcy by rx/ry.

## Slide 54
Slenderness Criteria
Notes: Note KL/r=slenderness parameter
This criteria is mostly based on erection and shipping concerns rather than safety issues.

## Slide 55
Per Section E.2
Recommended to provide Lc/r less than 200

## Slide 56
LOCAL BUCKLING

## Slide 57
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge.
Failure is localized at areas of high stress
(maximum moment) or imperfections.

## Slide 58
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge.
Failure is localized at areas of high stress
(maximum moment) or imperfections.
58
Notes: 58

## Slide 59
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge.
59
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Notes: 59

## Slide 60
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flanges.

## Slide 61
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flanges.
61
Notes: 61

## Slide 62
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flanges.
62
Notes: 62

## Slide 63
Local Buckling:
  Criteria in Table B4.1a
  Strength in Chapter E: Members with Slender Elements

## Slide 64
Local Buckling Criteria
Slenderness of the flange and web, l, are used as criteria to determine whether local buckling might control in the elastic or inelastic range, otherwise the global buckling criteria controls.
Criteria r are based on plate buckling theory.
For W-Shapes
FLB,  = bf /2tf rf =
WLB,  = h/tw rw =
Notes: Depends on 2 variables:1)Width to thickness ratio of flange and/or web and 2)Fy
Values are more stringent from those provided for beams, as the entire section is under full compression, and therefore less likely to provide restraint to the adjacent sections. In a W-shape beam bent about the major axis, only part of the web is in compression, and the value is minimal near the centroid, allowing the web to provide additional restraint to the flanges. Also, the web in such a beam is only partially under compression, so is much less likely to buckle than in a compressive member.

## Slide 65
 > r “slender element”
Failure by local buckling occurs.
Covered in Section E7
Many rolled W-shape sections are dimensioned such that the full global criteria controls.
Local Buckling
Notes: In general practically all W-shapes are non-slender as compression members, so this is covered as an advanced topic only.
May control if high Fy, welded shapes, shapes not generally used for compression (such as angles, WT, etc.)

## Slide 66
  Section E7:
  Compression Strength
  Members with Slender Elements

## Slide 67
THE FOLLOWING SLIDES CONSIDER SLENDER FLANGES AND SLENDER WEBS
NOT COMMON FOR W-SHAPES!!

## Slide 68
Pn = FcrAe Equation E7-1
Fcr = Calculated from Section E3 or E4.
Ae = Summation of the effective cross section areas based on reduced effective widths be, de or he or as defined by Equations E7-6 or E7-7. These reduced areas are based on sections not being effective at carrying load due to local buckling.
Compression Strength – Slender Sections

## Slide 69
For then be = b Equation E7-2
Compression Strength – Slender Sections
be = effective flange width (unstiffened element)
de = effective T-section height
he = effective web height (stiffened element)
For Slender Elements Excluding Round HSS
For then
See definitions in AISC Manual Equation E7-3

## Slide 70
For then Ae = A Equation E7-6
Compression Strength – Slender Sections
be = effective flange width (unstiffened element)
de = effective T-section height
he = effective web height (stiffened element)
For Slender Round HSS
For
then Equation E7-7

## Slide 71
FULL STRUCTURE BEHAVIOR
Notes: Column within a full structure will first be described as affecting the end conditions of a single column. Next the approach of full structure behavior including nominal forces (Direct Analysis Method) is introduced. This is covered in more detail in the Beam-Column design module.

## Slide 72
ALIGNMENT CHART
OR
DIRECT ANALYSIS METHODS
Notes: The instructor must decide how they wish to proceed here – both methods are presented and the instructor can select one or the other as their primary method.
The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.
Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.
Ideally both methods would be introduced, with an assignment comparing results for students to determine acceptability of the notional load values. Alignment chart procedures are often simpler for students to grasp conceptually while Direct Analysis methods easier for them to apply in a design.

## Slide 73
Does not redistribute restraining moments into girders/beams.
ALIGNMENT CHART
“Traditional Method”
Determine effective length, KL, for each column.
Basis for design similar to individual columns.
Notes: The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.

## Slide 74
DIRECT ANALYSIS METHOD
Analysis of entire structure interaction.
Include lateral “Notional” loads.
All members must be evaluated under combined axial and flexural load.
No K values required.
Reduce stiffness of structure.
Notes: Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.

## Slide 75
ALIGNMENT CHART METHOD
IS USED FOR THE FOLLOWING SLIDES
Notes: The instructor must decide how they wish to proceed here – both methods are presented and the instructor can select one or the other as their primary method.
The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.
Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.
Ideally both methods would be introduced, with an assignment comparing results for students to determine acceptability of the notional load values. Alignment chart procedures are often simpler for students to grasp conceptually while Direct Analysis methods easier for them to apply in a design.

## Slide 76
ALIGNMENT CHART
“Traditional Method”
Determine effective length, KL, for each column.
Basis for design similar to individual columns.
Does not redistribute restraining moments into girders/beams.
Notes: The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.

## Slide 77
K-FACTORS FOR END CONSTRAINTS
No Joint Translation Allowed – Sidesway Inhibited
0.5  K  1.0
Joint Translation Allowed – Sidesway Uninhibited
1.0  K  

## Slide 78
K-FACTORS FOR END CONSTRAINTS
Behavior of individual column unchanged
(Frame merely provides end conditions).
Two categories,
Braced Frames, 0.5  K  1.0
Sway Frames, K ≥ 1.0

## Slide 79
Floors do not translate relative to one another in-plane.
Typically, members are pin connected to save cost.
Sidesway Prevented

## Slide 80
Assume girder/beam infinitely rigid or flexible compared to columns to bound results.
K=0.7
K=0.5
K=1
K=0.7
Sidesway Prevented

## Slide 81
Shear Wall
Idealized
Equivalent
Sidesway Prevented
Notes: Note that even a brace or shear wall braces all attached nodes within the story if they are connected – and therefore act as bracing to linked columns.

## Slide 82
Shear Wall
Idealized
Equivalent
82
Sidesway Prevented
Notes: Note that even a brace or shear wall braces all attached nodes within the story if they are connected – and therefore act as bracing to linked columns.
82

## Slide 83
Shear Wall
Idealized
Equivalent
83
Sidesway Prevented
Notes: Note that even a brace or shear wall braces all attached nodes within the story if they are connected – and therefore act as bracing to linked columns.
83

## Slide 84
Typically, members are pin-connected to save cost (K = 1).
If members include fixity at connections,
Alignment Chart Method to account for rotational restraint (K < 1).
Typical design will assume K = 1 as a conservative upper bound (actual K ≈ 0.8 not much difference from K = 1 in design).
Sidesway Prevented

## Slide 85
Floors can translate relative to one another in-plane.
Enough members are fixed to provide stability.
Number of moment frames chosen to provide reasonable force distribution and redundancy.
Sway Frame

## Slide 86
Assume girder/beam infinitely rigid or flexible compared to columns to bound results.
K=2
K=1
K = ∞
K=2
Sway Frame

## Slide 87
Moment Frame
87
Sway Frame
Notes: Note that even a single moment frame braces all attached nodes within the story if they are connected – though the rest of the structure is just “along for the ride”.
87

## Slide 88
88
Moment Frame
Sway Frame
Notes: Note that even a single moment frame braces all attached nodes within the story if they are connected – though the rest of the structure is just “along for the ride”.
88

## Slide 89
89
Moment Frame
Sway Frame
Notes: Note that even a single moment frame braces all attached nodes within the story if they are connected – though the rest of the structure is just “along for the ride”.
89

## Slide 90
Calculate “G” at the top and bottom of the column (GA and GB).
G is inversely proportional to the degree of rotational restraint at column ends.
I = moment of inertia of the members
L = length of the member between joints
Alignment Charts

## Slide 91
Alignment Charts
Separate Charts for Sidesway Inhibited and Uninhibited
Sidesway Inhibited
(Braced Frame)
Sidesway UnInhibited
(Sway Frame)
91

## Slide 92
Alignment Charts
Separate Charts for Sidesway Inhibited and Uninhibited
Sidesway Inhibited
(Braced Frame)
Sidesway UnInhibited
(Sway Frame)
92
Gtop
X
Gbottom
X
Gtop
X
Gbottom
X

## Slide 93
Alignment Charts
Separate Charts for Sidesway Inhibited and Uninhibited
Sidesway Inhibited
(Braced Frame)
Sidesway UnInhibited
(Sway Frame)
93
Gtop
X
Gbottom
X
K
K
Gtop
X
Gbottom
X

## Slide 94
Use the IN-PLANE stiffness Ix if in major axis direction, Iy if in minor axis.
Girders/Beams are typically bending about Ix when column restraint is considered.
Only include members RIGIDLY ATTACHED (pin ended members are not included in G calculations).
If column base is “pinned” – theoretical G = ∞. AISC recommends use of 10.
If column base is “fixed” – theoretical G = 0. AISC recommends use of 1.
Alignment Charts

## Slide 95
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.
Alignment Charts

## Slide 96
Let’s evaluate the assumptions.
Alignment Charts

## Slide 97
97
Alignment Charts
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.

## Slide 98
If the column behavior is inelastic,
Yielding decreases stiffness of the column.
Relative joint restraint of the girders increases.
G therefore decreases, as does K.
Decrease is typically small.
Conservative to ignore effects.
Can account for effects by using a
stiffness reduction factor, t, times G.
(SRF Table 4-13)
Alignment Charts

## Slide 99
99
Alignment Charts
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.

## Slide 100
These conditions can be directly accounted for, but are generally avoided in design.
Partial restraint of connections and non-uniform members effectively change the rotational stiffness at the connections.
Only include members RIGIDLY ATTACHED (pin ended members are not included in G calculations).
Alignment Charts

## Slide 101
101
Alignment Charts
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.

## Slide 102
Calculation of G accounts for rotational stiffness restraint at each joint based on assumed bending.
For other conditions include a correction factor “m” to account for actual rotational stiffness of the girder at the joint.
Alignment Charts

## Slide 103
Far end pinned
Bending Stiffness =
Bending Stiffness =
Bending Stiffness =
Sidesway Inhibited (Braced)
Assumption: single curvature bending of girder.
Far end fixed
Alignment Charts
m = (3EI/L)/(2EI/L) = 1.5
m = (4EI/L)/(2EI/L) = 2

## Slide 104
Far end pinned
Sidesway Uninhibited (Sway)
Assumption: reverse curvature bending of girder.
Far end fixed
Bending Stiffness =
Bending Stiffness =
Bending Stiffness =
Alignment Charts
m = (3EI/L)/(6EI/L) = 1/2
m = (4EI/L)/(6EI/L) = 2/3

## Slide 105
105
Alignment Charts
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.

## Slide 106
Design typically checks each story independently, based on these assumptions.
In general, columns are chosen to be a similar size for more than one story. For each column section this results in sections with extra strength in upper floors, and close to their strength in lower floors.
Actual conditions can be directly accounted for, but are generally ignored in design.
Alignment Charts

## Slide 107
107
Alignment Charts
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.

## Slide 108
This case will be addressed first, with the concept valid for general conditions as well.
In a story not all columns will be loaded to their full strength.
Some are ready to buckle, while others have additional strength.
An extreme case of this is a “leaner” column.
Alignment Charts

## Slide 109
“LEANER” COLUMNS

## Slide 110
Leaner Columns
For this structure note that the right columns are pinned at each connection, and provide no bending restraint.
Theoretically G at top and bottom is infinite.
110
Moment Frame
Leaner Columns
Notes: 110

## Slide 111
Theoretically the column has an infinite KL.
Therefore, the strength should be zero.
For Leaner Columns:
G top= Infinity
G bottom= Infinity
Therefore K= Infinity
KL= Infinite
So the column has no strength according to the alignment chart
Leaner Columns

## Slide 112
Moment
Frame
Leaner Columns
Consider only applying a small load to the right columns
112
Leaner Columns
Notes: 112

## Slide 113
Moment
Frame
Surely a small load could be applied without causing instability! (Due to connection to the rest of the structure)
Leaner Columns
Consider only applying a small load to the right columns
Leaner Columns

## Slide 114
PA
K = infinity
fPn = zero
PA
K < infinity
fPn > zero
Actual Condition
Chart
Provided that the moment frame is not loaded to its full strength, it can provide some lateral restraint to the leaner columns. This is indicated by the spring in the figure above.
Leaner Columns

## Slide 115
P
Note that the result of a vertical force trying to translate through displacement, D, is a lateral load of value PD/H applied to the system.
D
PD/H
H
PD/H
P
Leaner Columns

## Slide 116
leaner
1
2
3
4
P1
P2
P3
P4
ΣP = ΣPe
ΣP = P1+P2+P3+P4
ΣPe = P1e+P2e+P3e+P4e=P1e+P4e
In the elastic range, the “Sum of Forces” concept states that the total column capacities can be re-distributed
Leaner Columns

## Slide 117
leaner
1
2
3
4
P1
P2
P3
P4
If P2 = P2e
Reach failure even if
ΣP < ΣPe
However, the total load on a leaner column still must not exceed the non-sway strength.
Leaner Columns

## Slide 118
A system of columns for each story should be considered.
Actual design considers inelastic behavior of the sections, but the basic concept is the same.
The strength of the story is the load which would cause all columns to sway.
The strength of an individual column is the load which would cause it to buckle in the non-sway mode (K=1).
Leaner Columns

## Slide 119
EXAMPLE DEMONSTRATION –
SEE YURA VIDEOS

## Slide 120
Once the limit against lateral buckling and lateral restraint is reached, the entire story will exhibit sidesway buckling.
In general, each story is a system of columns which are loaded to varying degrees of their limiting strength.
Those with additional strength can provide lateral support to those which are at their sidesway buckling strength.
Alignment Chart

## Slide 121
Alignment Chart
121
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Shear deformations are neglected.

## Slide 122
Axial load reduces bending stiffness of a section.
In girders, account for this with reduction factor on EI/L.
Alignment Chart

## Slide 123
If bending load dominates, consider the member a “girder” with reduced rotational stiffness at the joint (axial load reduction).
If axial load dominates, consider member a “column” with extra strength to prevent the story from buckling (sum of forces approach).
It is helpful to think in terms of members controlled by axial force or bending, rather than “girders” and “columns.”
Alignment Chart

## Slide 124
Alignment Chart Issues
Notes: Note KL/r=slenderness parameter
This criteria is mostly based on erection and shipping concerns rather than safety issues.

## Slide 125
To account for inelastic column effects,
stiffness reduction factors, ta,
used to reduce EI of the columns.
Stiffness Reduction Factors
Table 4-13
Alignment Chart

## Slide 126
If beams have significant axial load,
they provide less rotational restraint.
1-Q/Qcr
Q = axial load
Qcr = axial in-plane buckling strength with K=1
Reduce rotational stiffness component (EI/L) of beams with modification,
This is also valid for “columns” at a joint (multiple stories), which carry minimal axial load compared to their strengths.
Alignment Chart

## Slide 127
To account for story buckling concept, all columns must reach their capacity to allow for story failure.
Revise K to account for story effects.
Alignment Chart
Kn2 = K factor directly from the alignment chart
Pr = Load on the column (factored for LRFD)
K2 from Equation C-A-7-8

## Slide 128
DIRECT ANALYSIS METHOD
IS USED FOR THE FOLLOWING SLIDES

## Slide 129
DIRECT ANALYSIS METHOD
Analysis of entire structure interaction.
Include lateral “Notional” loads.
No K values required.
Reduce stiffness of structure.
Notes: Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.

## Slide 130
DIRECT ANALYSIS METHOD
Further evaluation of this method is included in the module on “Combined Forces.”