## Slide 1
TENSION MEMBER Design
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
TENSION MEMBER:
Structural member subjected to tensile axial load.
P
P
Notes: Typically hangers, braces, truss members. Also components of connections and other members.

## Slide 3
Strength design requirements:
Pu  Pn (Pa  Pn/Ω)ASD
Where  varies depending on failure mode.

## Slide 4
Tensile Strength
Strength Limit States:
Yielding on Gross Area
Rupture on Net Area
Block Shear
Bearing or Tear-out at Bolts
Notes: Each of these failure modes will be evaluated individually. The lowest strength will control design strength.

## Slide 5
Yielding on Gross Area, Ag

## Slide 6
When a member is loaded the strength is limited by the yielding of the entire cross section.
D
P=FyA
eyL0
L0
Yield on Gross Area
Notes: Note that residual stress does not affect tension member strength, as ultimate load is not affected and loss of stiffness is not a major factor in tension (as opposed to compression where buckling failure modes are affected).

## Slide 7
When a member is loaded the strength is limited by the yielding of the entire cross section.
D
P=FyA
eyL0
L
Yield on Gross Area
P
P
D
Notes: Note that residual stress does not affect tension member strength, as ultimate load is not affected and loss of stiffness is not a major factor in tension (as opposed to compression where buckling failure modes are affected).

## Slide 8
However, consider how this is affected by the stress-strain conditions.
Consider L0=100 inch long tension member.
Yield on Gross Area

## Slide 9
eu
.1 to .2
Strain
Stress
Fu
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
9
Tension Theory
Yield on Gross Area

## Slide 10
eu
.1 to .2
Strain
Stress
Fu
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
10
Tension Theory
Δy = 0.0015(100) = 0.15”
Yield on Gross Area

## Slide 11
eu
.1 to .2
Strain
Stress
Fu
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
11
Tension Theory
Δy = 0.0015(100) = 0.15”
Δsh = 0.02(100) = 2”
Yield on Gross Area

## Slide 12
eu
.1 to .2
Strain
Stress
Fu
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
12
Tension Theory
Δy = 0.0015(100) = 0.15”
Δsh = 0.02(100) = 2”
Δu = 0.15(100) = 15”
Yield on Gross Area

## Slide 13
Consider L0 = 100 inch long tension member.
Excessive deformations defines “Failure” for tension member yielding.
Limit to FyAg.
ΔYield = approx. 0.0015(100) = 0.15”
ΔOnset of Strain Hardening = approx. 0.02(100) = 2”
ΔPeak Load = approx. 0.15(100) = 15”
Yield on Gross Area

## Slide 14
Rupture on Effective Net Area, Ae

## Slide 15
If holes are included in the cross section less area resists the tension force.
Bolt holes are larger than the bolt diameter.
In addition, processes of punching holes can damage the steel around the perimeter.
Rupture on Effective Net Area

## Slide 16
Design typically uses average stress values.
This assumption relies on the inherent ductility of steel.
Pn
Rupture on Effective Net Area

## Slide 17
Design typically uses average stress values.
This assumption relies on the inherent ductility of steel.
Pn
17
Tension Theory
Initial stresses will typically include stress concentrations due to higher strains at these locations.
Rupture on Effective Net Area
Notes: 17

## Slide 18
Design typically uses average stress values.
This assumption relies on the inherent ductility of steel.
Pn
18
Tension Theory
Highest strain locations yield, then elongate along plastic plateau while adjacent stresses increase with additional strain.
Rupture on Effective Net Area
Notes: 18

## Slide 19
Design typically uses average stress values.
This assumption relies on the inherent ductility of steel.
Pn
19
Tension Theory
Eventually at very high strains the ductility of steel results in full yielding of the cross section.
Rupture on Effective Net Area
Notes: 19

## Slide 20
Design typically uses average stress values.
This assumption relies on the inherent ductility of steel.
Pn
20
Tension Theory
Therefore average stresses are typically used in design.
Rupture on Effective Net Area
Notes: 20

## Slide 21
Similarly, bolts and surrounding material will yield prior to rupture due to the inherent ductility of steel.
Therefore assume each bolt transfers equal force .
21
Tension Theory
Pn
Rupture on Effective Net Area
Notes: 21

## Slide 22
Shear Lag affects members where:
Only a portion of the cross section is connected,
Connection does not have sufficient length.
Rupture on Effective Net Area

## Slide 23
Cross Section
Net area reduced by hole area
1
2
3
Bolt line
23
Tension Theory
Pn
The plate will fail in the line with the highest force (for similar number of bolts in each line).
Each bolt line shown transfers 1/3 of the total force.
Rupture on Effective Net Area
Notes: 23

## Slide 24
The plate will fail in the line with the highest force (for similar number of bolts in each line).
Cross Section
Net area reduced by hole area
Each bolt line shown transfers 1/3 of the total force.
1
2
3
Bolt line
24
Tension Theory
Pn
Pn
Pn
Rupture on Effective Net Area
Notes: 24

## Slide 25
Cross Section
Net area reduced by hole area
1
2
3
Bolt line
25
Tension Theory
Pn
Pn
2/3Pn
Pn/6
Pn/6
The plate will fail in the line with the highest force (for similar number of bolts in each line).
Each bolt line shown transfers 1/3 of the total force.
Rupture on Effective Net Area
Notes: 25

## Slide 26
Cross Section
Net area reduced by hole area
1
2
3
Bolt line
26
Tension Theory
Pn
Pu
Pu
Pn
1/3Pn
Pn/6
Pn/6
Pn/6
Pn/6
The plate will fail in the line with the highest force (for similar number of bolts in each line).
Each bolt line shown transfers 1/3 of the total force.
Rupture on Effective Net Area
Notes: 26

## Slide 27
Cross Section
Net area reduced by hole area
1
2
3
Bolt line
27
Tension Theory
Pn
The plate will fail in the line with the highest force (for similar number of bolts in each line).
Each bolt line shown transfers 1/3 of the total force.
Pn
0
Pn/6
Pn/6
Pn/6
Pn/6
Pn/6
Pn/6
Rupture on Effective Net Area
Notes: 27

## Slide 28
Pn
Pn
0
1/3
Pn
2/3
Pn
Cross Section
Net area reduced by hole area
Force in plate
Bolt line 1 resists Pn in the plate.
Bolt line 2 resists 2/3Pn in the plate.
Bolt line 3 resists 1/3Pn in the plate.
1
2
3
Bolt line
The plate will fail in the line with the highest force (for similar number of bolts in each line).
Each bolt line shown transfers 1/3 of the total force.
Rupture on Effective Net Area

## Slide 29
Consider how this is affected by the stress-strain conditions.
Consider L0=1 inch diameter holes.
Pn
1 inch
Rupture on Effective Net Area

## Slide 30
eu
.1 to .2
Strain
Stress
Fu
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
30
Tension Theory
Rupture on Effective Net Area

## Slide 31
eu
.1 to .2
Strain
Stress
Fy =
50 ksi
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
31
Tension Theory
Fu
Δ = 0.0015(1) = 0.0015”
Rupture on Effective Net Area

## Slide 32
eu
.1 to .2
Strain
Stress
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
32
Tension Theory
Δ = 0.02(1) = 0.02”
Fu
Δ = 0.0015(1) = 0.0015”
Rupture on Effective Net Area

## Slide 33
eu
.1 to .2
Strain
Stress
Fy
E
Esh
ey
.001 to .002
esh
.01 to .03
er
.2 to .3
eu
.1 to .2
33
Tension Theory
Δsh = 0.02(1) = 0.02”
Δu = 0.15(1) = 0.15”
Fu
Δy = 0.0015(1) = 0.0015”
Rupture on Effective Net Area

## Slide 34
Consider L0=1 inch hole diameter.
Failure at net area can achieve Fu
so long as ductility is available.
ΔYield = approx. 0.0015(1) = 0.0015”
ΔOnset of Strain Hardening = approx. 0.02(1) = 0.02”
ΔPeak Load = approx. 0.15(1) = 0.15”
34
Tension Theory
Rupture on Effective Net Area
Notes: 34

## Slide 35
For a plate with a typical bolt pattern the rupture plane is shown.
Yield on Ag would occur along the length of the member.
Both failure modes depend on cross-sectional areas.
Pn
Rupture failure across section at lead bolts.
Yield failure (elongation) occurs along the length of the member.
Rupture on Effective Net Area

## Slide 36
What if holes are not in a line perpendicular to the load?
Additional strength depends on:
Geometric length increase
Combination of tension and shear stresses
Combined effect makes a direct calculation difficult.
Need to include additional length/area of failure plane due to non-perpendicular path.
g
s
Pn
Rupture on Effective Net Area

## Slide 37
Pn
As the force is transferred from each bolt it spreads through the tension member. This is sometimes called the “flow of forces”
Note that the forces from the left 4 bolts act on the full cross section at the failure plane (bolt line nearest load application).
Boundary of force transfer into the plate from each bolt.
Rupture on Effective Net Area

## Slide 38
Pn
At the rupture plane (right bolts) forces have not engaged the entire plate.
Now consider a much wider plate.
Rupture on Effective Net Area
Notes: Describing this in terms of an extremely wide plate in sheet metal, or tin foil, will allow students to intuitively grasp the concept.

## Slide 39
Pn
At rupture plane (right bolts) forces have not engaged the entire plate.
39
Tension Theory
Rupture Plane
Now consider a much wider plate.
Rupture on Effective Net Area
Notes: Describing this in terms of an extremely wide plate in sheet metal, or tin foil, will allow students to intuitively grasp the concept.
39

## Slide 40
Pn
At the rupture plane (right bolts) forces have not engaged the entire plate.
40
Tension Theory
Rupture Plane
Now consider a much wider plate.
Portion of member carrying no tension.
Rupture on Effective Net Area
Notes: Describing this in terms of an extremely wide plate in sheet metal, or tin foil, will allow students to intuitively grasp the concept.
40

## Slide 41
Pn
At the rupture plane (right bolts) forces have not engaged the entire plate.
41
Tension Theory
Portion of member carrying no tension.
Effective length of rupture plane
Rupture Plane
Now consider a much wider plate.
Rupture on Effective Net Area
Notes: Describing this in terms of an extremely wide plate in sheet metal, or tin foil, will allow students to intuitively grasp the concept.
41

## Slide 42
lw= width of Whitmore Section
This concept describes the Whitmore Section.
Pn
42
Tension Theory
Rupture on Effective Net Area
30o
30o
Notes: Describing this in terms of an extremely wide plate in sheet metal, or tin foil, will allow students to intuitively grasp the concept.
42

## Slide 43
Accounts for distance required for stresses to distribute from connectors into the full cross section.
Only a portion of the cross section is connected.
Connection does not have sufficient length.
Largest influence when
Shear Lag
Rupture on Effective Net Area

## Slide 44
Shear Lag
44
Tension Theory
Ae = Effective Net Area
An = Net Area
Ae ≠ An Due to Shear Lag
Rupture on Effective Net Area
Notes: 44

## Slide 45
Pn
l= Length of Connection
45
Tension Theory
Rupture on Effective Net Area
Notes: 45

## Slide 46
l= Length of Connection
46
Tension Theory
Rupture Plane
Pn
Rupture on Effective Net Area
Notes: 46

## Slide 47
l= Length of Connection
47
Tension Theory
RupturePlane
Distribution of Forces Through Section
Pn
Rupture on Effective Net Area
Notes: 47

## Slide 48
Section Carrying Tension Forces
l= Length of Connection
48
Tension Theory
RupturePlane
Distribution of Forces Through Section
Pn
Rupture on Effective Net Area
Notes: 48

## Slide 49
49
Tension Theory
Area not Effective in Tension Due to Shear Lag
Effective Net Area in Tension
Shear lag less influential when l is long, or if outstanding leg has minimal area or eccentricity
Pn
Rupture on Effective Net Area
Notes: 49

## Slide 50
Block Shear

## Slide 51
State of Combined Yielding and Rupture
Block Shear
Failure Planes
Failure Tears Out Block of Steel
Block defined by:
Center line of holes
Edge of welds
At least one each in tension and shear.

## Slide 52
Block Shear
Typical Examples in Tension Members:
Angle Connected on One Leg
W-Shape Flange Connection
Plate Connection

## Slide 53
Pn
Angle Bolted to Plate
Pn
Block Shear
Notes: Note that angle tension plane goes towards the free edge rather than up into the other leg, as this would be less resistance.
Similarly the Plate would fail vertically towards the closest edge.

## Slide 54
Pn
Angle Bolted to Plate
Pn
54
Tension Theory
Tension plane on Angle
Shear plane on Plate
Tension plane on Plate
(Shorter Dimension Controls if Fy and t are the same)
Shear plane on Angle
Block Shear
Notes: Note that angle tension plane goes towards the free edge rather than up into the other leg, as this would be less resistance.
Similarly the Plate would fail vertically towards the closest edge.
54

## Slide 55
Block Failure from Angle
Block Shear
Pn
Angle Bolted to Plate
Block Failure From Plate
Pn
Notes: Block shear could occur on either the angle or the plate – lowest failure mode strength of all controls

## Slide 56
Pn
First look at the W-Shape, then the plate
Flange of W-Shape Bolted to Plate
Block Shear

## Slide 57
Pn
Tension planes on W-Shape
Shear planes on W-Shape
First look at the W-Shape, then the plate
57
Tension Theory
Block Shear
Flange of W-Shape Bolted to Plate
Notes: 57

## Slide 58
Pn
Block Failure in W-Shape
First look at the W-Shape, then the plate
Block Shear
Flange of W-Shape Bolted to Plate

## Slide 59
Pn
Pn
Flange of W-Shape Bolted to Plate
Block Shear
Notes: Here 2 possible plate block shear modes could occur, the lower strength would control.

## Slide 60
Pn
Pn
Shear planes on Plate
Tension plane on Plate
Shear planes on Plate
Tension planes on Plate
60
Tension Theory
Flange of W-Shape Bolted to Plate
Block Shear
Notes: Here 2 possible plate block shear modes could occur, the lower strength would control.
60

## Slide 61
Pn
Block Failure in Plate
Pn
Block Failure in Plate
Flange of W-Shape Bolted to Plate
Block Shear

## Slide 62
Pn
Angle or Plate Welded to Plate
Weld around the perimeter
Two Block Shear Failures to Check
Block Shear
Notes: Two possible block shear failures can be described by the perimeter of the welds – that with the lower strength would control.

## Slide 63
Pn
Pn
63
Tension Theory
Block Shear
Angle or Plate Welded to Plate
Notes: Two possible block shear failures can be described by the perimeter of the welds – that with the lower strength would control.
63

## Slide 64
Pn
Pn
Tension plane on Plate
Shear planes on Plate
Tension plane on Plate
Shear plane on Plate
64
Tension Theory
Block Shear
Angle or Plate Welded to Plate
Notes: Two possible block shear failures can be described by the perimeter of the welds – that with the lower strength would control.
64

## Slide 65
Pn
Pn
Block Failure From Plate
65
Tension Theory
Block Shear
Angle or Plate Welded to Plate
Notes: Two possible block shear failures can be described by the perimeter of the welds – that with the lower strength would control.
65

## Slide 66
Bearing at Bolt Holes

## Slide 67
Bolts bear into material around hole.
Direct bearing can deform the bolt hole an excessive amount and be limited by direct bearing capacity.
If the clear space to adjacent hole or edge distance is small, capacity may be limited by tearing out a section of base material at the bolt.
Bearing at Bolt Holes

## Slide 68
Bearing at Bolt Holes
Pn
Bolt
Bolt induces bearing stresses on the base material.

## Slide 69
Pn
Bolt
Which can result in excessive deformation of the bolt hole,
Bearing at Bolt Holes

## Slide 70
Pn
Bolt
When bearing stresses act on bolts that are near the edge of the material (Lc dimension is small).
Lc
Lc= clear distance, in the direction of load, between the edge of the hole and the edge of the adjacent hole or the edge of the material.
Bearing at Bolt Holes

## Slide 71
Pn
A block of material can tear out to the plate edge due to bearing.
Bearing at Bolt Holes
Notes: Note, this is differentiated from block shear since there is no tension plane for the failure.

## Slide 72
Pn
Bolt
Similarly, when bearing stresses act on bolts that are closely spaced (Lc dimension is small).
Lc
Bearing at Bolt Holes

## Slide 73
Pn
A block of material can tear out between the bolt holes due to bearing stresses.
Bearing at Bolt Holes
Notes: Note, this is differentiated from block shear since there is no tension plane for the failure.

## Slide 74
Tension Member
AISC Manual – 15th Edition
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 75
Tension Members:
  Chapter B: Gross and Net Areas
  Chapter D: Tension Member Strength
  Chapter J: Block Shear
  Part 5: Design Charts and Tables

## Slide 76
Gross and Net Areas:
  Criteria in Section B4.3
  Strength criteria in Chapter D: Design of Members for Tension

## Slide 77
Yield on Gross Area
Ft = 0.90 (Wt = 1.67)
Rupture on Effective Net Area
Ft = 0.75 (Wt = 2.00)
Block Shear
Ft = 0.75 (Wt = 2.00)

## Slide 78
Yield on Gross Area

## Slide 79
Pn = FyAg Equation D2-1
Yield on Gross Area
Ft = 0.90 (Wt = 1.67)
Ag = Gross Area
Total cross-sectional area in the plane perpendicular to tensile stresses.

## Slide 80
Rupture on Effective Net Area

## Slide 81
Ae = Effective Net Area
Accounts for any holes or openings, potential failure planes not perpendicular to the tensile stresses, and effects of shear lag.
Pn = FuAe Equation D2-2
ft = 0.75 (Wt = 2.00)
Rupture on Effective Net Area

## Slide 82
An = Net Area = Net Width x thickness
Modify gross area (Ag) to account for the following:
Holes or openings
Potential failure planes not perpendicular to the tensile stresses.
Rupture on Effective Net Area

## Slide 83
Diagonal hole pattern:
Net Width = Gross Width + Σs2/4g – width of all holes
Section B4.3b
s = longitudinal center-to-center spacing of holes (pitch)
g = transverse center-to-center spacing between fastener lines (gage)
g
s
Pu
Rupture on Effective Net Area

## Slide 84
Holes or openings
Section B4.3b
Use1/16” greater bolt hole width than nominal hole dimension shown in Table J3.3.
Accounts for potential damage in fabrication.
Rupture on Effective Net Area

## Slide 85
When considering angles:
Find gage (g) in Table 1-7A of Manual,
“Workable Gages in Angle Legs”
unless otherwise noted.
Rupture on Effective Net Area

## Slide 86
An = Net Area
An = Ag- ∑(dn+1/16)t + ∑(s2/(4g))t
dn = nominal hole diameter
t = thickness of tension member
Other terms defined on previous slides
Rupture on Effective Net Area

## Slide 87
Ae = Effective Net Area
Modify net area (An) to account for shear lag.
Or value per Table D3.1
Ae = AnU Equation D3-1
U = shear lag factor reduction
= eccentricity of connection
l = length where force transfer occurs (distance parallel to applied tension force along bolts or weld)
Rupture on Effective Net Area

## Slide 88
Block Shear

## Slide 89
Block Shear
Block Shear Rupture Strength (Equation J4-5),
ft = 0.75 (Wt = 2.00)
Agv = gross area subject to shear
Anv = net area subject to shear
Ant = net area subject to tension
Ubs = 1 or 0.5 (1 for most tension members, see Figure C-J4.2)

## Slide 90
Block Shear
Block Shear Rupture Strength (Equation J4-5),
Agv = gross area subject to shear
Anv = net area subject to shear
Ant = net area subject to tension
Ubs = 1 or 0.5 (1 for most tension members, see Figure C-J4.2)
Smaller of two values will control
90
ft = 0.75 (Wt = 2.00)
Notes: 90

## Slide 91
Bearing and Tearout at Bolt Holes

## Slide 92
Bearing and Tearout at Bolt Holes
ft = 0.75 (Wt = 2.00)
t = thickness of connected material
d = nominal bolt diameter
Fu = specified minimum tensile strength of the connected material
For standard, oversized, and short-slotted holes, or long slotted holes with slots parallel to the direction of loading:
for Bearing (Equation J3-6a)

## Slide 93
Bearing and Tearout at Bolt Holes
ft = 0.75 (Wt = 2.00)
lc = clear distance, in the direction of force, between the edge of hole and the edge of adjacent hole or edge of the material.
t = thickness of connected material
Fu = specified minimum tensile strength of the connected material
For standard, oversized, and short-slotted holes, or long slotted holes with slots parallel to the direction of loading:
for Tearout (Equation J3-6c)

## Slide 94
For standard, oversized, and short-slotted holes, or long slotted holes with slots parallel to the direction of loading, but when deformation of the bolt hole is not a design consideration:
for Bearing (Equation J3-6b)
for Tearout (Equation J3-6d)
For long-slotted holes with slot perpendicular to the direction of force:
for Bearing (Equation J3-6e)
for Tearout (Equation J3-6f)
Bearing and Tearout at Bolt Holes

## Slide 95
Design Aids
Tension - AISC Manual 15th Ed

## Slide 96
Tables 5-1 to 5-8
List available yield and rupture strength for typical sections.
Use care!
These tables assume Ae = 0.700Ag to 0.952Ag.
You must check this is met in the member and connections!
Design Aids

## Slide 97
Design Aids
Table 7-4 provides bearing and tearout strength at bolt holes based on bolt spacing.
These tables check bearing and tearout.
Note that edge distance, Le and bolt spacing, s are measured to the centers of bolt holes, rather than the edges of the bolt holes.
The bearing side of the equation controls when s ≥ sfull or Le ≥ Lefull. sfull and Lefull are the bolt spacing and edge distance, respectively, for full bearing strength.
Table 7-5 provides bearing and tearout strength at bolt holes based on edge distance.