## Slide 1: FAULT TOLERANT SYSTEMS http://www.ecs.umass.edu/ece/koren/FaultTolerantSystems Part 2 – Canonical Structures Chapter 2 – Hardware Fault Tolerance

## Slide 2: Failure Rate
Rate at which a component suffers faults
Depends on age, ambient temperature, voltage or physical shocks that it suffers, and technology
Dependence on age is usually captured by the bathtub curve:

## Slide 3: Bathtub Curve
Young component – high failure rate
  Good chance that some defective units slipped through manufacturing quality control and were released
Later - bad units weeded out – remaining units have a fairly constant failure rate
As component becomes very old, aging effects cause the failure rate to rise again

## Slide 4: Empirical Formula for  - Failure Rate
 = L Q (C1 T V + C2 E)
  L: Learning factor, (how mature the technology is)
  Q: Manufacturing process Quality factor (0.25 to 20.00)
  T: Temperature factor, (from 0.1 to 1000), proportional to exp(-Ea/kT) where Ea is the activation energy in electron-volts associated with the technology, k is the Boltzmann constant and T is the temperature in Kelvin
  V: Voltage stress factor for CMOS devices (from 1 to 10 depending on the supply voltage and the temperature); does not apply to other technologies (set to 1)
  E: Environment shock factor: from about 0.4 (air-conditioned environment), to 13.0 (harsh environment - e.g., space, cars)
  C1, C2: Complexity factors; functions of number of gates on the chip and number of pins in the package
  Further details: MIL-HDBK-217E handbook

## Slide 5: Reliability and MTTF of a Single Component (Module)
Module operational at time t=0
Remains operational until it is hit by a failure
All failures are permanent
T - lifetime of module - time until it fails
T is a random variable
f(t) - density function of T
F(t) - cumulative distribution function of T

## Slide 6: Probabilistic Interpretation of f(t) and F(t)
F(t) - probability that the component will fail at or before time t
  F(t) = Prob {T  t}
f(t) – not a probability, but the momentary rate of probability of failure at time t
  f(t)dt = Prob {t  T  t+dt}
Like any density function (defined for t  0)
f(t)  0 (for all t  0) and
The functions F and f are related through
  and

## Slide 7: Reliability and Failure (Hazard) Rate
The reliability of a single module - R(t)
  R(t) = Prob {T>t} = 1- F(t)
The conditional probability that the module will fail at time t, given it has not failed before, is
Prob {t  T  t+dt | T  t} = Prob {t T t+dt} / Prob{T  t} = f(t)dt / (1-F(t))
The failure rate (or hazard rate) of a component at time t, (t), is defined as
  (t) = f(t)/(1- F(t))
Since dR(t)/dt = - f(t), we get (t) = -1/R(t) • dR(t)/dt

## Slide 8: Constant Failure Rate
If the module has a failure rate which is constant over time -
  (t) = 
  dR(t) / dt = -  R(t) ; R(0)=1
The solution of this differential equation is
A module has a constant failure rate if and only if T, the lifetime of the module, has an exponential distribution

## Slide 9: Mean Time to Failure (MTTF)
MTTF - expected value of the lifetime T
Two ways of calculating MTTF
First way:
Second way:
If the failure rate is a constant 

## Slide 10: Weibull Distribution - Introduction
Most calculations of reliability assume that a module has a constant failure rate  (or equivalently - an exponential distribution for the module lifetime T)
There are cases in which this simplifying assumption is inappropriate
Example - during the ‘’infant mortality” and ‘’wear-out” phases of the bathtub curve
Weibull distribution for the lifetime T can be used instead

## Slide 11: Weibull distribution - Equation
The Weibull distribution has two parameters,  and 
The density function of the component lifetime T:
The failure rate for the Weibull distribution is
(t) is decreasing with time for <1, increasing with time for >1, constant for =1, appropriate for infant mortality, wearout and middle phases, respectively

## Slide 12: Reliability and MTTF for Weibull Distribution
Reliability for Weibull distribution is
MTTF for Weibull distribution is
( (x) is the Gamma function )
The special case  = 1 is the exponential distribution with a constant failure rate 

## Slide 13: Hardware Failure Mechanisms
Common CMOS failures mechanisms:
(1) Electromigration: Atoms in the metal interconnect migrating away – thinning of wires
Median time to failure
  -constant, J – current density, 1<m<2, activation energy (depends on interconnect material), T- absolute temperature, k- Boltzmann’s constant

## Slide 14: CMOS Failure Mechanisms
(2) Stress Migration: Metal wires and Silicon substrate expand at different rates causing migration of atoms from wires
  -constant,  - 2<m<9, activation energy (depends on interconnect material), T- absolute temperature, k- Boltzmann’s constant

## Slide 15: CMOS Failure Mechanisms
(3) Negative Bias Temperature Instability – With increased temperature, electric charge is trapped causing increase of threshold voltage and delay
Beyond a certain delay the circuit fails
(4) Hot Carrier Injection - Charge carriers accelerated by high electric field and a fraction of these are injected into the gate oxide slowing down the transistor
For n-channel devices (similar expression for p-channel):
  - constant, - substrate current, w - transistor width, activation energy, 2<m<4, k- Boltzmann constant, T - temperature

## Slide 16: CMOS Failure Mechanisms
(5) Time-Dependent Dielectric Breakdown – electrical defects (traps) in the gate oxide increase leakage current and may result in a breakdown of the dielectric film.
  - constant, V - voltage, T - absolute temperature (K), k - Boltzmann’s constant, a=78; b=-0.008; X=0.76eV, Y=-66.8eVK, Z=-0.37×10-4eV/K
Putting It Together: Assume constant failure rate ; =; R(t)=exp(-t)
But: (i) failure mechanisms are not independent; (ii) hard to get accurate values for all parameters; (iii) constant environment (e.g., temperature) assumed

## Slide 17: Varying Failure Rates
If failure rates vary (e.g., due to temperature change), reliability can not be calculated using R(t)=exp(-t)
Suppose is a function of temperature T: (T) and T changes as a function of time t: T(t)
Partition the interval [0,t] into small intervals of length ∆
Probability of no failure during the j-th interval, given that it was functional at the beginning of that interval, is π(j) = exp(-(Tj) ∆)
Probability of no failure until end of j-th interval is
Common-mode failures: multiple circuits (i) operate in same harsh environment (e.g., massive radiation) may produce identical erroneous outputs, or (ii) have a common power supply that experiences a surge
Can be protected against by using design diversity - logic or circuit diversity

## Slide 18: Canonical Structures
A canonical structure is constructed out of N individual modules
The basic canonical structures are
  A series system
  A parallel system
  A mixed system
We will assume statistical independence between failures in the individual modules

## Slide 19: Reliability of a Series System
A series system - set of modules so that the failure of any one module causes the entire system to fail
Reliability of a series system - Rs(t) - product of reliabilities of its N modules
Ri(t) is the reliability of module i

## Slide 20: Series System – Modules Have Constant Failure Rates
Every module i has a constant failure rate i
s =i is the constant failure rate of the series system
Mean Time To Failure of a series system -

## Slide 21: Reliability of a Parallel System
A Parallel System - a set of modules connected so that all the modules must fail before the system fails
Reliability of a parallel system -
is the reliability of module i

## Slide 22: Parallel System – Modules have Constant Failure Rates
Module i has a constant failure rate, i
Example - a parallel system with two modules
MTTF of a parallel system with the same 

## Slide 23: Non Series/Parallel Systems
Each path represents a configuration allowing the system to operate successfully, e.g., ADF
The reliability can be calculated by expanding about a single module i :
Rsystem=Ri Prob{System works | i is fault-free} +(1-Ri) Prob{System works | i is faulty}
Draw two new diagrams: in (a) module i is operational; in (b) module i is faulty
Module i is selected so that the two new diagrams are closer to simple series/parallel structures

## Slide 24: Expanding about C
The process of expanding can be repeated until the resulting diagrams are of the series/parallel type
Figure (a) needs further expansion about E
Figure (a) should not be viewed as a parallel connection of A and B, connected serially to D and E in parallel. Such a diagram will have the path BCDF which is not a valid path
(a)
(b)

## Slide 25: Expanding about C and E
Rsystem=RC Prob {System works | C is operational} +(1-RC) RF [1-(1-RA RD)(1-RB RE)]
Expanding about E yields
Prob {System works | C is operational}= RE RF [1-(1-RA)(1-RB)] +(1-RE)RA RD RF
Substituting results in
Rsystem=RC [RE RF(RA+RB-RA RB)+(1-RE) RA RD RF] +(1-RC) [RF(RA RD+RB RE-RA RD RB RE)]
Example: RA=RB=RC=RD=RE=RF=R
Rsystem=R (R -3R +R+2)
2
3
3
(a)
(b)

## Slide 26: Upper Bound on Reliability
If structure is too complicated - derive upper and lower bounds on Rsystem
An upper bound - Rsystem  1 -  (1-Rpath_i)
  Rpath_i - reliability of modules in series along path i
  Assuming all paths are in parallel
Example - the paths are ADF, BEF and ACEF
Rsystem  1 -(1-RA RD RF)(1-RB RE RF)(1-RA RC RE RF)
If RA=RB=RC=RD=RE=RF=R then
Upper bound can be used to derive the exact expression: perform multiplication and replace every occurrence of by

## Slide 27: Lower Bound on Reliability
A lower bound is calculated based on minimal cut sets of the system diagram
A minimal cut set: a minimal list of modules such that the removal (due to a fault) of all modules will cause a working system to fail
Minimal cut sets: F, AB, AE, DE and BCD
The lower bound is
Rsystem   (1-Qcut_i)
  Qcut_i - probability that the minimal cut i is faulty (i.e., all its modules are faulty)
Example - RA=RB=RC=RD=RE=RF=R

## Slide 28: Upper Bound on Reliability
If structure is too complicated - derive upper and lower bounds on Rsystem
An upper bound - Rsystem  1 -  (1-Rpath_i)
  Rpath_i - reliability of modules in series along path i
  Assuming all paths are in parallel
Example - the paths are ADF, BEF and ACEF
Rsystem  1 -(1-RA RD RF)(1-RB RE RF)(1-RA RC RE RF)
If RA=RB=RC=RD=RE=RF=R then
Upper bound can be used to derive the exact expression: perform multiplication and replace every occurrence of by

## Slide 29: Lower Bound on Reliability
A lower bound is calculated based on minimal cut sets of the system diagram
A minimal cut set: a minimal list of modules such that the removal (due to a fault) of all modules will cause a working system to fail
Minimal cut sets: F, AB, AE, DE and BCD
The lower bound is
Rsystem   (1-Qcut_i)
  Qcut_i - probability that the minimal cut i is faulty (i.e., all its modules are faulty)
Example - RA=RB=RC=RD=RE=RF=R

## Slide 30: Example – Comparison of Bounds
Example - RA=RB=RC=RD=RE=RF=R
Lower bound here is a very good estimate for a high-reliability system