## Slide 1: Functional Verification of Arithmetic Circuits
Maciej Ciesielski
Department of Electrical & Computer Engineering
University of Massachusetts, Amherst
ciesiel@ecs.umass.edu

## Slide 2: Outline
Introduction
  Hardware verification methods, focus on arithmetic verification
Basics
  Boolean techniques: BDD
  Word-level canonical: BMD, TED
  Equivalence checking, SAT
Bit-vector and word-level techniques
  SMT, ILP models
Computer algebra methods
  Arithmetic bit level
  Data-flow based approach
  Other algebraic methods
Extended bibliography

## Slide 3
Arithmetic Verification Part I
Basics
Canonical Diagrams, SAT

## Slide 4: Hardware Verification
Variety of formal techniques
  Model checking, property checking
  Equivalence checking
  Theorem proving
Solution methods
  Canonical diagrams (Boolean, word-level)
  SAT (satisfiability)
  SMT (satisfiability modulo theories)
  Integer Linear Programming (ILP) methods
  Computer Algebra approach

## Slide 5: Formal Verification Techniques
Theorem proving,
  Deductive reasoning with axioms, rules to prove correctness
  Term-rewriting, no guarantee it will terminate
  Complex, heavy user interaction and domain knowledge
  Systems: ACL, PVS, HOL,
Model checking
  Automatic technique to prove correctness of concurrent systems
  Use temporal logic specification, CTL, etc. to describe properties
  Practical tools become available, popular in industry
Equivalence checking
  Check if two designs are equivalent
  Solved for combinational circuits
    Except arithmetic circuits and datapaths
    Difficult problem for sequential systems
Functional verification (our focus: arithmetic circuits)
  Special case of equivalence checking and property checking
ICCD 2015
Arithmetic Verification - Tutorial
5

## Slide 6: Functional Verification
Determined by functional specification
  Input-output (I/O) relationship
  Our focus: combinational integer arithmetic circuits
How is functional specification given?
    By writing a formula that describes I/O relationship
      Easy for logic circuits (write a Boolean formula)
      What about arithmetic circuits?
      Different ways to provide “specification”
    By providing reference design with desired function
      e.g. standard “text-book” multiplier
      Checking equivalence with the reference design

## Slide 7: Combinational Equivalence Checking
Functional Approach
  Transform output functions of combinational circuits into a unique (canonical) representation
  Two circuits are equivalent if their representations are identical
  Efficient canonical representations:
    BDD, BMD, TED.
Structural
  Identify structurally similar internal points
  Prove internal points (cut-points) equivalent
ICCD 2015
Arithmetic Verification - Tutorial
7

## Slide 8: Canonical Representations
Boolean Representations (f: B → B)
  BDDs, ZBDDs, etc.
Moment Diagrams (f: B → Z)
  BMDs, K*BMDs, etc.
  Canonical DAGs for Polynomials (f: Z → Z)
  Taylor Expansion Diagrams (TEDs)
  Horner Decision Diagrams (HDDs)
Arithmetic verification needs representation for f: Z2m → Z2m
  Modular arithmetic
ICCD 2015
Arithmetic Verification - Tutorial
8

## Slide 9: Binary Decision Diagrams (BDD)
Based on recursive Shannon expansion [Bryant DAC’85]
  f = x fx + x’ fx’
Compact data structure for Boolean logic
  can represents sets of objects (states) encoded as Boolean functions
Canonical representation
  Reduced, ordered BDDs (ROBDD) are canonical
  Essential for verification
    Equivalence checking
    SAT

## Slide 10: Application to Verification - EC
Equivalence Checking (EC) of combinational circuits
Canonicity property of BDDs:
  if F and G are equivalent, their BDDs are identical (for the same ordering of variables)
1
0
a
b
c
F = a’bc + abc +ab’c
G = ac +bc
1
0
a
b
c

1
0
a
b
c
G
F
ICCD 2015
Arithmetic Verification - Tutorial
10

## Slide 11: Application to Verification - SAT
General SAT
  Find a set of satisfying assignments
Functional test generation
  SAT, Boolean satisfiability analysis
  to test for H = 1 (0), find a path in the BDD to terminal 1 (0)
  the path, expressed in function variables, gives a satisfying solution (test vector)
ab
ab’c
H
0
1
a
b
c
Problem: size explosion
ICCD 2015
Arithmetic Verification - Tutorial
11

## Slide 12: Large BDDs
Maps: B → B, very low-grain
  Can be prohibitively large for arithmetic circuits (multipliers, etc.)

## Slide 13: Partitioned BDDs
Circuits for which BDD can be constructed
  Represent multiple-output circuits as shared BDDs
  BDDs must be identical (with same variable order)
Circuits whose BDDs are too large
  Cannot construct BDDs, memory problem
  Use partitioned BDD method
    decompose circuit into smaller pieces, each as BDD
    check equivalence of internal points (cut-point method)
ICCD 2015
Arithmetic Verification - Tutorial
13

## Slide 14: Word-level Canonical Diagrams - BMD
BMD for 4-bit Multiplier (bit-level) [Bryant TCAD’95]
    Map: B → Z (binary to integers)
*BMD
Devised for word-level operations, arithmetic designs
Based on modified Shannon expansion (positive Davio)
  f = x fx + x’ fx’ = x fx + (1-x) fx’
  = fx’ + x (fx - fx’ ) = fx’ + x fx
where fx’ = fx=0 is zero moment
f  x = (fx - fx’ ) is first moment, first derivative
Additive and multiplicative weights on edges (*BMD)
ICCD 2015
Arithmetic Verification - Tutorial
14

## Slide 15: *BMD - Construction
Unsigned integer: X = 8x3 + 4x2 + 2x1 + x0
X x3=1 = 8 + 4x2 + 2x1 + x0
Xx3=0 = 4x2 + 2x1 + x0
Xx3 = 8
x3
8
x2
x1
x0
4
2
1
0
BMD
1
0
x0
x1
x2
1
2
4
x3
8
*BMD
Multiplicative edges
ICCD 2015
Arithmetic Verification - Tutorial
15

## Slide 16: *BMD – Word-Level Representation
Efficiently modeling symbolic word-level operators
4
1
0
x0
x1
x2
1
2
4
y0
y1
y2
2
1
1
0
x0
x1
x2
y0
y1
y2
1
2
4
2
4
1
X+Y
X Y
ICCD 2015
Arithmetic Verification - Tutorial
16

## Slide 17: Taylor Expansion Diagram (TED)
Canonical representation of multi-variate polynomials of arbitrary degree [Ciesielski-TComp’06]
  f: Integer  Integer
  More word-level than BMD
  When input are Boolean: TED  BMD
TED is not a decision diagram
  Cannot solve SAT
  Too high-grain
  Cannot express output bits as
  function of word-level inputs
X + Y
1
0
X
Y
X Y
1
0
X
Y

## Slide 18: TED – a few Examples
1
x0
x1
x2
x3
2
4
1
0
1
x0
x1
x2
1
1
1
4
4
8
16
16
64
1
1
AC+BC +1
= A(B+C)+1
1
0
B
C
A
1
A2+AB +2BC
1
0
B
C
A
B
1
2
Useful for finding factored forms
ICCD 2015
Arithmetic Verification - Tutorial
18

## Slide 19: TED – Application to EC
Resource sharing
  TED can prove their equivalence
Z = sel(A*B) + (1-sel)(C*D)
= sel(A*B - C*D) + CD

## Slide 20: Applications to RTL Verification
Equivalence checking with TEDs
  word-level and Boolean variables
A
B
s2
0
1
F2
bk
ak
*
*
-
D
B
A
s1
1
0
F1
D
ak
bk
>
+
*
-
F1 = s1(A+B)(A-B) + (1-s1)D
s1 = (ak > bk) = ak (1-bk)
F2 = (1-s2) (A2-B2) + s2 D
s2 = ak’  bk = 1 - ak + ak bk
A = [an-1, …,ak,…,a0] = [Ahi,ak,Alo], B = [bn-1, …,bk,…,b0] = [Bhi,bk,Blo]
20

## Slide 21: RTL Equivalence Checking
1
ak
0
Ahi
D
ak
bk
bk
Bhi
Alo
Blo
0
1
22k+2
2k+2
^2
-2k+2
2k
2k
-22k+2
1
-1
-1
1
F1 = F2
^2
= power edge
B
A
s1
1
0
F1
D
ak
bk
>
+
*
-
A
B
s2
0
1
F2
bk
ak
*
*
-
D
ICCD 2015
Arithmetic Verification - Tutorial
21

## Slide 22: Equivalence Checking with SAT
Equivalence checking using SAT [GRASP, zChaff, MiniSAT]
  Create a “miter” at the outputs
  Check for unSAT (if always evaluates to 0)
  The most popular way to solve equivalence checking (EC)
unSAT
CL2

## Slide 23: Property Checking using SAT
Same concept can be applied to property checking
  Need to conjunct the system spec (S) with the complement of the property (p)
  Invoke a SAT solver
    unSAT if system S satisfies property p
p
S

## Slide 24: Miter for Cut-point based EC
Use cut-points to partition the Miter
Use SAT to solve the problem: is the output of Miter unSAT ?
= 0?
f1
f2
f3
v1
v2
= 0?
= 0?
f1
f2
f3
v2
v1
x
Cut-point guessing
  Compute signature with random simulation
  Sort signatures + select cut-points
  Iteratively verify and refine cut-points
  Verify outputs

## Slide 25: Boolean Satisfiability (SAT)
Well known Constraint Satisfaction Problem.
Given a propositional formula Ψ, determine if there exist a variable assignment such as Ψ evaluates to true.
  If it exist, Ψ is called satisfiable
  If not, Ψ is called unsatifiable
  SAT problems are hard (NP complete)
Most SAT solvers uses Conjunctive Normal Form (CNF) to represent the propositional formula
  Conjunction of clauses
  Each clause is a disjunction of literals

## Slide 26: CNF for Gate-level Circuits
Converting gate-level circuit into CNF formula

## Slide 27: Theorem Provers

## Slide 28: Theorem Prover: Example

## Slide 29: Theorem Prover: Example

## Slide 30
Arithmetic Verification Part II
Word-level Models SMT, ILP methods

## Slide 31: SMT for bit-vector Operation
SMT-LIB
Bit-vector operations
  variables extended to bit-vectors
X1 = AND (a0 , b0)
X1 – a0b0 = 0
gate netlist
A = B
A ≠ B

## Slide 32: SMT for bit-vector Operation
SMT-LIB
Bit-vector operation
  variables extended to bit-vectors
Z – (A+B)
M – (A*B)
A > B

## Slide 33: SMT vs SAT
SMT extends SAT solving by adding extensions (theories)
    Core theory (Boolean)
    Ints theory
    Reals theory
    Reals_Ints theory
    ArraysEx theory
    Fixed_Size_BitVectors theory, etc.
Properties
  Decidable: An effective procedure exists to check if a formula is a member of a theory T
  Often Quantifier-free
An SMT solver can solve a SAT problem, but not vice-versa
  Application:
    Software Model Checking, RTL Design, Analog

## Slide 34: DPLL(T)
In a nutshell
  DPLL(X)
    Very similar to a SAT solver, enumerates Boolean model
    Not allowed: pure literal, blocked clause elimination, ...
    Required: incremental addition of clauses
    Desirable: partial model detection
  T-Solver
    Checks consistency of conjunctions of literals
    Computes theory propagations
    Produces explanations of inconsistency / T-propagation
    Should be incremental and backtractable

## Slide 35: SMT modeling without Reference
Full adder using SMT: a+b+c = 2Cout+S
  {+, -, 2} are bit-vector operations
XOR
XOR
AND
AND
Fspec

## Slide 36: Functional Test Generation
Deterministic test pattern generation
  Formulate a SAT problem for a complex combinational design
  Solve SAT: find a set of satisfying assignment
modulo example(
A, B, C, x, a, b, out
);
input [?:0] A,B,C;
input a,b,x;
output out;
assign sel = (A+B)<(B*C);
assign out = (sel)? (a&b) : x;
endmodule
A=?
0
1
<
+
*
out
B=?
C=?
a=?
b=?
x=?
extract

## Slide 37: Types of Operators
A
B
C
s
0
1
Mixed-level blocks
  MUX
<
c
A
B
  comparators
  shifters, etc
a
b
c
Boolean logic (bit-level)
  logic gates
+ --
* /
A
B
C
Arithmetic blocks
  (symbolic, word-level operators)
  ADD, SUB
  MULT, DIV

## Slide 38: Modeling Arithmetic Datapaths
Map entire design to CNF (miniSAT, GRASP, zCHAFF,…)
  Any generic CNF-based solver can be used
  Representation is large, structural information is lost
Map Boolean logic onto CNF, arithmetic operators onto linear equations (HSAT)
  Inconsistent domains, explicit backtracking needed
Represent both domains in a unified format (LPSAT)
  Solve Mixed Integer Linear Program (MILP)
  Scalable with design size
  Constraint propagation implicitly passed to MILP solver
First, assume infinite precision
  No overflows, arbitrarily large bit-width
ATPG is also used

## Slide 39: Arithmetic and Mixed Operators
<
s
D
E
X
Y
Z
s
1
0
+ --
* /
A
B
C
C = A + B
A, B  2n-1
Z – X – L (1-s)  0
X – Z – L (1-s)  0
Z – Y – L s  0
Y – Z – L s  0
D - E - L (1-s) < 0
D - E + L s  0
D, E  2n-1
X, Y  2n-1
s = {0,1}
s = {0,1}
L = 2n-1
n = number of bits

## Slide 40: LP: Linearizing the Multiplier
Expand operand A
  A = A0 + 2 A1 + … + 2 n-1 An-1
Keep operand B as one variable
Represent result in terms of partial products Pi
*
A
B
C = A*B
B
P0 = A0 B
P1 = A1 B
Pn-1=An-1B
………..
An-1
A0
Ai

C = P0 + 2 P1 + … + 2 n-1 Pn-1
for i = 1, …, n-1:
  Pi – L Ai  0
  Pi – B + L(1-Ai)  0
  0  Pi  B
where L = 2n-1

## Slide 41: LP Modeling of Boolean Logic
c
a
c = 1 - a
a
b
c
a
b
c
c  a
c  b
c  a + b
c  1
c  a
c  b
c  a+b-1
c  0
a, b, c = {0, 1}

## Slide 42: MILP Solvers - Efficiency Issues
Efficiency depends on the number of integer variables
  Only IO signals defined as binary variables
  All internal signals left as continuous, automatically adjusted to integer
Implicit branch & bound, backtracking
  Impose ordering of variables to branch on
  Put decision variables first
binary
binary
…
…
continuous

## Slide 43: LPSAT - Example
Y[k]  A[k], C[k]
Y[k]  A[k] + C[k] – 1
Y[k]  0
A[..] , C[..] ,Y[..] = bit vectors
s = decision variable (0,1)
A,B,C,D,E,X,Z = continuous variables
D = A + B
E = B * C (linearized)
0  A,B,C  2n-1
D - E - L (1-s) < 0 D - E + L s  0
Z – X – L (1-s)  0
X – Z – L (1-s)  0
Z – Y – L s  0
Y – Z – L s  0
<
*
Z
X
Y[..]
<
s
+
A
B
D
*
C
E
A[..]
C[..]
1
0
1
0
+

## Slide 44: Improving ILP Modeling
ILP model for RTL design
+
A
B
<
6
C
s
Solve the problem for A=5, B=3 in n=3 bits
  ILP solution (incorrect):
    C = 8; s = (8 < 6) = 0
  Correct solution in 3 bits:
    C = 8 mod 23 = 0; s = (0 < 6) = 1
  Note: adding constraint C  7 will make it infeasible
  Need to properly model modulo semantics
    Add a slack variable  to adjust the variable size

## Slide 45: Modeling Modulo Semantic
Correctly models modulo semantics [Brinkman VLSI’02]
+
A
B
<
6
C
s
  Now the solution is correct:
  C = 0;  = 1; s = (0 < 6) = 1

## Slide 46: ILP Model for RTL Design
Complete RTL model

## Slide 47: Arithmetic Verification Part III Algebraic Approach

## Slide 48: Arithmetic Verification
HA
HA
HA
HA
S
C
S
C
C
C
S
S
Functional verification of arithmetic circuits
  Verify function implemented by arithmetic circuit
  Use algebraic approach
Why is it important
  Arithmetic circuits are difficult
  to verify on bit-level
  Avoid “bit blasting”
  (flattening to bit-level)

## Slide 49: Arithmetic Verification
We should be able to answer questions:
  Does the circuit meet the specification ?
  What function does this circuit implement ?
  If it does not meet the specification
    Demonstrate error, show bug trace
    Find the bug (debugging, difficult)
How to approach it:
with Computer Algebra

## Slide 50: Computer Algebra Methods
Arithmetic Bit-level (ABL) representation
[Wienand’08, Pavlenko’11]
Also applied to Galois Fields (GF) [Kalla’14, Tcomp’15]
  Circuit specification Fspec and implementation B
  represented by polynomials
  Check if implementation B satisfies specification Fspec
  Done by reducing Fspec modulo B
Methods differ in ways they accomplish the reduction

## Slide 51: Computer Algebra - Basics
  Represent specification and implementation as polynomials, Fspec and B in Z2n.
Example: multiplier Z = X*Y
  Fspec = Z - X * Y
  B = set of polynomials in Z2n representing circuit elements:
    y = INV(x): (y + 1 – x )
    q1 = AND (a, b): (q1 – a b)
    q2 = OR(a, b): (q2 – a – b + ab)
    q3 = XOR(a, b): (q3 – a – b + 2ab)
    {C,S} = HA(a, b): (2C + S – a – b)
    {C,S} = FA(a, b, c): (2C + S – a – b – c)
  Each satisfies the local function if poly = 0

## Slide 52: Computer Algebra - reduction
Goal: reduce Fspec modulo B:
Systematic methods exist to perform this reduction
  If r = 0, the circuit is correct
  If r ≠ 0, circuit may still be correct but B needs to be a canonical basis (Groebner basis) to determine if r = 0
  Groebner basis
    Difficult to compute, computationally complex
  In gate-level circuit, B is already Groebner basis
    But it must also include polynomials <x2-x> for all Boolean signals x in the circuit (i.e., x = 0, 1)
Fspec
r

## Slide 53: Reducing Fspec modulo B
  Reduce Fspec modulo B by a series of polynomial divisions
B
poly (PI)
poly (PO)
Fspec =
Sigout
0 ?
Sigin
-
Implementation

## Slide 54: Example (STABLE)
Example: 2-bit adder
  Fspec = a0 + b0 + 2a1 + 2b1 – 4r2 – 2r1 – r0
  B = list of polynomials describing gates

## Slide 55: Polynomial Division (1)
a0 + b0 + 2a1 + 2b1 – 4r2 – 2r1 – r0
= – (a0 + b0 – 2a0b0) + r0 + b0 + 2a1 + 2b1 – 4r2 – 2r1 – r0
= 2a0b0 + 2a1 + 2b1 – 4r2 – 2r1
= – 2(a0b0) + 2c + 2a0b0 + 2a1 + 2b1 – 4r2 – 2r1
= 2c + 2a1 + 2b1 – 4r2 – 2r1
= – 2(a1 + b1 – 2a1b1) +2d + 2c + 2a1 + 2b1 – 4r2 – 2r1
= 4a1b1 +2d + 2c – 4r2 – 2r1
= – 2(c +d – 2cd) + 2r1 + 4a1b1 +2d + 2c – 4r2 – 2r1
= 4cd + 4a1b1 – 4r2
= – 4(cd) + 4f + 2cd+ 4a1b1 – 4r2
= 4f + 4a1b1 – 4r2
= – 4(a1b1) + 4e + 4f + 4a1b1 – 4r2
= 4e + 4f – 4r2
= – 4(e + f – ef) + 4r2 + 4e + 4f – 4r2
= 4ef
Divide polynomial Fspec =

## Slide 56: Polynomial Division (2)
Continue dividing polynomial 4ef
4ef
= 4e(cd)
= 4(a1b1)(cd)
= 4(a1b1) (a0b0) (a1 + b1 – 2a1b1)
= 4(a1b1) (a1 + b1 – 2a1b1) (a0b0)
= 4(a1b1a1 + a1b1b1 – 2a1b1a1b1) (a0b0)
= 4(0) (a0b0)
= 4ef = 0
This means that Fspec mod B = 0 , hence the circuit correctly implements a 2-bit adder.

## Slide 58: Data Flow Approach
Treat computation as flow of data
[Basith-FMCAD’11, Ciesielski-HVC’13,]
Based on observation that :
  In an arithmetic circuit an integer flow across the circuit is the same at any point (cut) in the circuit
    Cut: set of signals separating PIs from POs
  Write equations to represent the flow for a cut
  Functional correctness can be done by proving that the flow at PIs = flow at the POs.
Define input and output signatures of the network
Prove functionality by checking if input signature can be transformed into output signature
(or vice-versa)
  ABL networks (HA based, linear)
  Gate-level networks (nonlinear)

## Slide 59: Arithmetic Network Model
Represent design as network of HAs and FAs (if possible)
Half-Adder (HA)
  Binary inputs ( a, b)
  Binary outputs ( S, C)
a + b = 2C + S
Full-Adder (FA)
  Binary inputs ( a, b , cin)
  Binary outputs ( S, C)
a + b + cin = 2C + S

## Slide 60: Input & Output Signatures
Input signature: Functionality provided by user (spec)
SigIn = x1 + x2 + x3 + x4 + x5 + x6 + x7
Output signature: Binary encoding of outputs
Sigout = 4S2 + 2S1 + S0
Transform
Sigin into Sigout
to verify function
Transform
Sigout into Sigin
to extract function
Or

## Slide 61: Data Flow Model – Basic Concept
Sigin transformed into Sigout by a series of rewriting steps (~Gaussian elimination)
Replace input part of the FA equation
  by the output part
Sigin = x1 +x2 +x3 + x4 +x5 +x6 + x7 (PI)
→ (2 x11 + x12) + x4 +x5 +x6 + x7
→ (2 x11 + x12) + (2 x13 +x14) + x7
Continue:
2 x11 + 2 x13 + x12 + x14 + x7
→ 2 x11 + 2 x13 + (2 x15 + x10)
→ 2 (2 x8 + x9) + x10 = 4S2 + 2S2 + S0 (PO)
This proves that circuit implements a 7-3 compactor
cut1
cut2
a + b + c = 2 C + S

## Slide 62: Gate-level Arithmetic Circuits
Functional correctness can be shown by
  Forward rewriting (PI  PO) or
  Backward rewriting (PO  PI)
Algebraic model:
Forward rewriting
  Polynomial division (reduction),
  Replacing input expression by outputs
  HA: (a + b) / (a + b - 2C - S) = 2C + S
Backward rewriting
  Replacing gate output by the expression in its inputs (expansion)
  e.g., OR gate: z = a + b - a*b
polynomial: (a + b - 2C - S)
equation: a + b = 2C + S
a
b
z

## Slide 63: Forward Rewriting
Example: 2-bit adder
Problem: RE ≠ Ø
  <x2-x> was not used
  Can we reduce it to zero?
f1
f0
f2
f3
Problem: RE = 4ef, but … it reduces to 0
4
1
2
2
4
1
1
2
2

## Slide 64: Backward Rewriting
f1
f0
f2
f3
f0 = 4(a1b1) + 2(a0b0) + 2(a1+ b1 - 2a1b1)
+ (a0 + b0 - 2a0b0)
- 4(a1b1)(a0b0)(a1 + b1 -2a1b1)
= 2a1+ 2b1 + a0 + b0
It matches the specification:
 circuit is correct
Replace gate output by its equation
  Backward symbolic simulation
  No RE ! It will never be generated
  But … the expression can explode

## Slide 65: Function Extraction - summary
Important features
  Backward rewriting = function extraction !
Different than standard symbolic simulation
  Proof of functional correctness is done by propagating cut expressions for all the signals, from POs, rather than from individual outputs
  Cancellation happen during the process (example: HA)
    Consider cut = 2C+S, with C = ab; S = a + b -2ab
    If done separately: first replace C = ab, then replace a, b by other signals, up to certain level, so that cut =
    2 f(x) g(y) + f(x) + f(y) – 2ab
    It cannot be simplified until a, b are substituted.
    But if S is replaced immediately after C, then
    cut = 2ab + a + b -2ab = a + b
    proving that 2C+S = a + b
a + b = 2C + S

## Slide 66: Backward Rewriting - issues
No residual expression !
  But the cut expression can explode (fat belly issue)
  Choice and ordering of cuts during rewriting affects performance
Issues:
  Minimize the “fat belly”, the size of largest expression (memory)
  Handling complex gates
  Provide cuts in AOI gate

## Slide 67: Experimental Results
Effect of ordering of cuts and including some useful redundancy (vanishing polynomials) on the size of cut expressions
4-bit serial squarer

## Slide 68: Experimental Results
Performance of the backward rewriting process
  Combinational and sequential (bounded model) circuits
4-bit serial squarer

## Slide 69: Experimental Results
Multiplier design - comparisons with other methods
Performance for original and synthesized designs

## Slide 70: Summary and Conclusions
Forward rewriting is simple to implement
  No memory explosion, but ..
  Generates RE to be verified (typically using backward rewriting)
  Need to compute weights (not easy for non-linear ckts)
Backward rewriting is more reliable (no RE)
  But … may explode
  Can be used for function extraction:
    the computed signature gives the specification
Combining rewriting in both directions
  Can be used for debugging
  The difference between computed signatures tells which gate should be replaced [isvlsi-2015]
Solving the problem for highly bit-optimized circuits
  Remains difficult
  Very large fat belly, memory explosion problem

## Slide 71: Arithmetic Verification Bibliography

## Slide 72: Algebraic
[Basith-FMCAD'11] B., Mohamed Abdul, T. Ahmad, A. Rossi, and M. Ciesielski. "Algebraic approach to arithmetic design verification." FMCAD 2011.
[Ciesielski-HVC'13] M. Ciesielski, W. Brown, and A. Rossi."Arithmetic Bit-level Verification using Network Flow Model." HVC, 2013. 327-343.
[Ciesielski-ISVLSI'14] Ciesielski, M., Brown, W., Liu, D., and Rossi, A. "Function extraction from arithmetic bit-level circuits." ISVLSI, 2014.
[Ciesielski-DAC'15] "Verification of Gate-level Arithmetic Circuits by Function Extraction." DAC,2015
[Wienand-CAV'08] Wienand, Oliver, et al. "An algebraic approach for proving data correctness in arithmetic data paths.” CAV, 2008.
[Pavlenko-DATE'11] Pavlenko, E., Wedler, M., Stoffel, D., Kunz, W., Dreyer, A., Seelisch, F., and Greuel, G. M. "STABLE: A new QF-BV SMT solver for hard verification problems combining Boolean reasoning with computer algebra." DATE, 2011.
[Marx-ICCAD'13] Marx, O., Wedler, M., Stoffel, D., Kunz, W., and Dreyer, A. "Proof logging for computer algebra based SMT solving." ICCAD,2013

## Slide 73: Algebraic, cont’d
[Shekhar-ICCAD'05] Shekhar, N., Kalla, P., Enescu, F., and Gopalakrishnan, S. "Equivalence verification of polynomial datapaths with fixed-size bit-vectors using finite ring algebra." ICCAD,2005
[Shekhar-ICCD'05] Shekhar, N., Kalla, P., Enescu, F., and Gopalakrishnan, S. "Exploiting vanishing polynomials for equivalence verification of fixed-size arithmetic datapaths." ICCD, 2005.
[Pruss-DAC'14] Pruss, T., Kalla, P., and Enescu, F. "Equivalence verification of large galois field arithmetic circuits using word-level abstraction via gröbner bases." DAC,2014
[Lv-TCAD'14] Lv, J., Kalla, P., and Enescu, F. "Efficient gröbner basis reductions for formal verification of galois field arithmetic circuits." Trans. on CAD, 2014.
[Lv-DATE'12] Lv, J., Kalla, P., and Enescu, F. "Efficient gröbner basis reductions for formal verification of galois field multipliers." DATE,2012.
[Sun-DATE’15] Sun, X., Kalla, P., Pruss, T., & Enescu, F. (2015, March). Formal verification of sequential Galois field arithmetic circuits using algebraic geometry. DATE, 2015.
[Kroening-2008] Kroening, Daniel, and Ofer Strichman. Decision procedures: an algorithmic point of view. Springer Science & Business Media, 2008.

## Slide 74: Algebraic, cont’d
[Cox-1992] Cox, David, John Little, and Donal O'shea. Ideals, varieties, and algorithms. Vol. 3. New York: Springer, 1992.
[Tim-TCAD’15] Tim Pruss, Priyank Kalla and Florian Enescu. Accepted, to appear in IEEE Trans. on CAD, 2015

## Slide 75: ILP
[Brinkmann-VLSID'02], Raik, and Rolf Drechsler. "RTL-datapath verification using integer linear programming." VLSID,2002
[Zeng-DATE'01] Zeng, Z., Kalla, P., and Ciesielski, M."LPSAT: a unified approach to RTL satisfiability." DATE, 2001.
[Fallah-DAC'1998] Fallah, F., Devadas, S., and Keutzer, K. "Functional vector generation for HDL models using linear programming and 3-satisfiability." DAC,1998.
[Huan-TCAD’01] Huan, C. Y., & Cheng, K. T. (2001). Using word-level ATPG and modular arithmetic constraint-solving techniques for assertion property checking. Trans. on CAD, 20(3), 381-391.

## Slide 76: Abstraction
[Johannsen-CAV'01] Johannsen, P. "BOOSTER: Speeding up RTL property checking of digital designs by word-level abstraction." CAV, 2001.
[Jain-TCAD'08] "Word-level predicate-abstraction and refinement techniques for verifying RTL verilog." Trans. on CAD, 2008.
[Kroening-ICCAD'07] Kroening, D., and Seshia, S. A. "Formal verification at higher levels of abstraction." ICCAD, 2007.
[Andraus-DAC'04] Andraus, Z. S., and Sakallah, K. A. "Automatic abstraction and verification of verilog models." DAC, 2004.
[Brady-MEMOCODE'10] Brady, B., Bryant, R. E., Seshia, S., and O'leary, J. W. "ATLAS: automatic term-level abstraction of RTL designs." MEMOCODE, 2010.
[Andraus-ASPDAC'06] Andraus, Z. S., Liffiton, M. H., and Sakallah, K. A. "Refinement strategies for verification methods based on datapath abstraction." ASP-DAC, 2006.

## Slide 77: Theorem Provers
[Sawada-FMCAD'11] Sawada, J., Sandon, P., Paruthi, V., Baumgartner, J., Case, M., and Mony, H. "Hybrid verification of a hardware modular reduction engine." FMCAD, 2011.
[Sawada-FMCAD'06] Sawada, J., and Reeber, E. ”ACL2SIX: A hint used to integrate a theorem prover and an automated verification tool." FMCAD, 2006.
[Russinoff-IMACS'05] Russinoff, D., Kaufmann, M., Smith, E., and Sumners, R. "Formal verification of floating-point RTL at AMD using the ACL2 theorem prover." IMACS, 2005.
[Harrison-2006] Harrison, J. "Floating-point verification using theorem proving." Formal Methods for Hardware Verification, 2006. 211-242.
[Brock-FMCAD'1996] Brock, B., Kaufmann, M., and Moore, J. S. “ACL2 theorems about commercial microprocessors." FMCAD, 1996.
[Hartmanis-2006] Hartmanis, A. C. D. H. J., Henzinger, T., Leighton, J. H. N. J. T., and Nivat, M. "Texts in Theoretical Computer Science An EATCS Series." (2006). Springer.
[Vasudevan-TCAD’07] Vasudevan, S., Viswanath, V., Sumners, R. W., & Abraham, J. Automatic verification of arithmetic circuits in RTL using stepwise refinement of term rewriting systems. Trans on CAD. 56(10), 1401-1414.
[Kapur-FMSD’1998] Kapur, D., & Subramaniam, M. (1998). Mechanical verification of adder circuits using rewrite rule laboratory. Formal Methods in System Design, 13(2), 127-158.

## Slide 78: Industry, floating-point
[Aharoni-ARITH'05] Aharoni, M., Asaf, S., Maharik, R., Nehama, I., Nikulshin, I., and Ziv, A. "Solving constraints on the invisible bits of the intermediate result for floating-point verification." Computer Arithmetic, 2005.
[Jacobi-DATE'05] Jacobi, C., Weber, K., Paruthi, V., and Baumgartner, J. “Automatic formal verification of fused-multiply-add FPUs." DATE, 2005.
[Krautz-DAC'14] Krautz, U., Paruthi, V., Arunagiri, A., Kumar, S., Pujar, S., and Babinsky, T. "Automatic Verification of Floating Point Units." DAC, 2014.
[Guralnik-TC'11] Guralnik, E., Aharoni, M., Birnbaum, A. J., and Koyfman, A. "Simulation-based verification of floating-point division." Trans. on Computers, 2011.

## Slide 79: ABC, Simulation graph
[Brayton-CAV'10] Brayton, R., and Mishchenko, A. "ABC: An academic industrial-strength verification tool." CAV, 2010.
[Mishchenko-2010]. Mishchenko, A. "ABC: A system for sequential synthesis and verification." URL http://www. eecs. berkeley.edu/alanmi/abc
[Soeken-FMCAD'15] Soeken, M., Sterin, B., Drechsler, R., and Brayton, R. "Simulation Graphs for Reverse Engineering." FMCAD, 2015.

## Slide 80: Canonical Diagrams
[Bryant-TC'1986] Bryant, R. E. "Graph-based algorithms for boolean function manipulation." TC, 100.8 (1986): 677-691.
[Bryant-DAC'1995] Bryant, R. E., and Chen, Y. A. "Verification of arithmetic circuits with binary moment diagrams." DAC, 1995.
[Chen-ICCAD'1997] Chen, Y. A., and Bryant, R. E. "PHDD: An efficient graph representation for floating point circuit verification." ICCAD, 1997.
[Drechsler-ISMVL'1997]. Drechsler, R., Keim, M., and Becker, B. "Sympathy-MV: Fast Exact Minimization of Fixed Polarity Multi-Valued Linear Expressions." ISMVL, 1997.
[Ciesielski-TCAD'06] Ciesielski, M., Kalla, P., and Askar, S. "Taylor expansion diagrams: A canonical representation for verification of data flow designs." Trans on Computers, 55.9 (2006): 1188-1201.
[Ciesielski] Ciesielski, M., Gomez-Prado, D., Ren, Q., Guillot, J., & Boutillon, E. “Optimization of data-flow computations using canonical TED representation”. Trans on CAD. 28(9), 1321-1333. 2009

## Slide 81: SAT/SMT
[Zhang-ICCAD'01] Zhang, L., Madigan, C. F., Moskewicz, M. H., and Malik, S. "Efficient conflict driven learning in a boolean satisfiability solver." ICCAD, 2001.
[Biere-2009] Biere, A., Heule, M., and van Maaren, H. “Handbook of satisfiability.” Vol. 185, 2009.
[Aloul-IWLS'02] Aloul, F. A., Mneimneh, M. N., and Sakallah, K. A. "ZBDD-Based Backtrack Search SAT Solver." IWLS. 2002.
[Alizadeh-TCAD'10] Alizadeh, B., and Fujita, M. "Modular datapath optimization and verification based on modular-HED." Trans. on CAD, 29.9 (2010): 1422-1435.
[Mishchenko-2010]. Mishchenko, A. "ABC: A system for sequential synthesis and verification." URL http://www. eecs. berkeley.edu/alanmi/abc
[Sörensson-SAT’09] Sörensson, N., & Eén, N. (2009). MiniSat 2.1 and MiniSat++ 1.0—SAT race 2008 editions. SAT, 31.
[Brummayer-2009] Brummayer, R., & Biere, A. (2009). Boolector: An efficient SMT solver for bit-vectors and arrays. In Tools and Algorithms for the Construction and Analysis of Systems (pp. 174-177).

## Slide 82: SAT/SMT, cont’d
[Barrett-CAV’11] Barrett, C., Conway, C. L., Deters, M., Hadarean, L., Jovanović, D., King, T., ... & Tinelli, C. “CVC4”. CAV, 2011.
[De Moura-2008]De Moura, L., & Bjørner, N. (2008). Z3: An efficient SMT solver. In Tools and Algorithms for the Construction and Analysis of Systems (pp. 337-340).
[Silva-ICCAD’1997] Silva, J. P. M., & Sakallah, K. A. (1997, January). GRASP—a new search algorithm for satisfiability. ICCAD, 1996.
[Biere-2010] Biere, Armin. "Lingeling, plingeling, picosat and precosat at SAT race 2010." FMV Report Series Technical Report 10.1 (2010).