## Slide 1: MDR
Advisor
Professor Pishro-Nik
Evaluators
Professor Jackson & Professor Kundu

## Slide 2: Team AutoTabber
Michaela Shtilman-Minkin (CSE)
Signal Processing & Algorithms
Michael Murphy (EE)
Pickup & MCU
Taryk Alsagoff (CSE)
GUI
Matthew Wojick (EE)
AFE & MCU
Notes: Everybody

## Slide 3: What is AutoTabber?

## Slide 4: System Requirements: Overview
Automatically generate tablature from guitar
  Baseline: single, consecutive notes
  e.g. Mary Had a Little Lamb, Yankee Doodle
Must have GUI
No guitar modifications
  Make a modular, easily installed product
Output from amplifier must be < 1V
MCU must be able to FFT signals close to instantaneously

## Slide 5: PDR Feedback
Wavelet transform
  Typically only used for image processing
  Alternative: time stamp from MCU and/or note onset in software
Displacement
Block diagram
  Fixed!

## Slide 6: Our Previous Block Diagram
Pickup
AFE
MCU
DSP
UI
Guitar
Notes: Mike

## Slide 7: New and Improved Block Diagram

## Slide 8: MDR Deliverables - Summary
Pickup
  Purchase and prototype
  Generate & propagate signal to AFE
Analog Front End (AFE)
  Amplify signal from pickup
Microcontroller
  Hardware that can FFT
Note recognition
  Identify a single note with its corresponding time stamp
Display
  GUI with tabs display
Notes: Michaela
Pickup
  Mike – purchase as well as prototype own. Will generate and propagate signal to Matt (AFE)
Analog Front End
  Matt – will amplify signal from pickup with minimal noise and no clipping to send to microcontroller.
Microcontroller
  Mike and Matt – will have functional hardware FFT to send signals to Michaela (DSP)
Note recognition
  Michaela – able to identify single note with timing and send it to Taryk (GUI)
Display
  Taryk – will have rudimentary GUI to display note packages from Michaela and ugly tab

## Slide 9: Pickups
Must detect vibrations from strings
  Successfully picks up signal from string
  Coil mounts 3D printed spools
  Not affected by adjacent strings
  Fixed high frequency oscillations
Need to compare different size pickups

## Slide 10: Amplifier Stage
Must amplify input from pickups
Need GBW for ~20kHz and ~100 gain
  Two stage TL072 (or TL082) for 10 gain on each stage works up to 100kHz
  Ordered better ones for single stage use

## Slide 11: AGC Amp
Might need automatic gain control in this stage
  Only if ADC ones are not sufficient
  Current one works, but has a problem with slew rate

## Slide 12: ADC
Should take signal from amp and sample at 44.1kHz
PCM1863 from TI
  both SPI and I2S (for audio) interfaces
  192 kHz max sample rate
  Energysense Signal Detection

## Slide 13: Pickups + Amps
PCB created with milling machine

## Slide 14: Demo of Pickup + Amp

## Slide 15: Microcontroller
Should take signal from ADC and perform FFTs
TMDX5535 eZdsp Development Kit
  With C5535 processor

## Slide 17: Signal Processing
Simulated signal processing in Python
Pass in .wav and string name
Use Welch Method for estimating the fundamental
  Estimate power of the signal at different frequencies though periodgram spectrum estimates
Find closest fret to fundamental
  "Evaluating the Online Capabilities of Onset Detection Methods“ by Sebastian Böck, Florian Krebs and Markus Schedl in Proceedings of the 13th International Society for Music Information Retrieval Conference (ISMIR), 2012
  http://ismir2012.ismir.net/event/papers/049_ISMIR_2012.pdf
B string, 7th fret:
  370.59 detected, closest match 369.99 (F#4)

## Slide 18: GUI
Basic GUI
  File I/O
  OO framework
  Defined interfaces
Problems with Qt framework
  Problems with wxWidgets
  Java Swing
  Javascript (web)
    SQL Database

## Slide 19: MDR Deliverables - Summary
Pickup
  Purchase and prototype: Prototype works, no need to buy
  Generate & propagate signal to AFE: YES
Analog Front End (AFE)
  Amplify signal from pickup: YES
  ADC: Received samples
Microcontroller
  Hardware that can FFT: Requested sample for chip/ dev. board
Note recognition
  Identify a single note with its corresponding time stamp: YES
Display
  GUI with tabs display: File I/O is implemented, some bugs

## Slide 20: Team Responsibilities (2014-2015 Schedule)
Mike
Get data for different sized pickups
Configure DSP chip
Interface DSP with software
Prototype fabrication

## Slide 21: Team Responsibilities (2014-2015 Schedule)
Matt
Design single stage amps, continue with AGC, work on ADCs
  Datasheets
  Configuring
  Testing
Interface AFE with DSP

## Slide 22: Team Responsibilities (2014-2015 Schedule)
Michaela
Determine timestamps for onset of all notes (presented in FFT form) in a given stream
Determine fundamental frequency and fret for each note
Package data to be displayed on GUI

## Slide 23: Team Responsibilities (2014-2015 Schedule)
Taryk
User-friendly interface
File I/O
Tablature editing capabilities for the user
Display of data sent from spectrum analyzer

## Slide 24: Proposed CDR Deliverables
Mike
  DSP configuration
  “Hello World”
Matt
  Analog design
Michaela
  Break up note stream into individual notes
  Identify timestamp of note onset, and fundamental frequency
  Output: timestamp, string, fret
Taryk
  GUI display and editing of sample tablature