## Slide 1: Team AutoTabber
Michaela Shtilman-Minkin (CSE)
Michael Murphy (EE)
Taryk Alsagoff (CSE)
Matthew Wojick (EE)
Notes: Everybody

## Slide 2: Our Vision
AutoTabber
A frustration-free system for producing tabs in minutes
Notes: Michaela

## Slide 3: First Things First… …some music education!
Notes: Michaela

## Slide 4: Formal Music Notation
Notes: Taryk

## Slide 5: What makes guitar different?
Tabs!
Notes:   Taryk
  1:1 mapping of where a guitarist needs to place his/her fingers on the neck of the guitar (fretboard) in order to play the right note
  Spend more time clearly explaining how a tab corresponds to the fretboard
Keyword: VISUALLY ANALGOUS

## Slide 6: Tabs vs. Sheet Music
The same notes may map to completely different tabs.
Notes: Michaela

## Slide 7: Why not sheet music?
Sheet music is hard to read, tabs are much easier
Notes: Michaela

## Slide 8: While it is possible to read sheet music…
Requires musical training
Doesn’t specify frets
Isn’t widely available
  When it is, it usually costs $$
Notes: Michaela

## Slide 9: Why Tabs Rock
Precise
Easy to read
Widely distributed
Require no formal musical training to interpret
Can range from simple to complex
Notes: Michaela

## Slide 10: The Status Quo
People currently tab…
  Manually (On paper or typed)
  Using software
    Guitar Pro (De-facto commercial)
    Power Tab (Freeware)
    TuxGuitar (Freeware)
    Aria Maestosa (Freeware)
    Tabular (Commercial)
    More…
Notes: Taryk

## Slide 11: Current Software
Notes: Taryk

## Slide 12: Our Vision
AutoTabber
A frustration-free system for producing tabs in minutes
Notes: Matt

## Slide 13: Our Goal
Combine existing technologies in a novel way
A system that automatically generates tablature WITHOUT permanently modifying or damaging the guitar.
Notes: Matt

## Slide 14: Benefits
Rapid transcription
User-friendliness
More people writing tabs
Increased productivity
Notes: Matt
  Select predictions: notes that it is confident in will choose a note
  Notes that it is not confident in will create a selection of notes for the user to choose from (like smart phone keyboards

## Slide 15: Requirements
GUI
Automatically generate tablature
  Baseline: single, consecutive notes
  e.g. Mary Had a Little Lamb, Yankee Doodle
No guitar modifications
  Make a modular, easily installed product
Notes: Matt
Extension to the project could include trying to detect more complicated signals (like chords), but right now we are just focusing on single notes
Can use on multiple guitars

## Slide 16: I/O
Inputs
  Vibrations from guitar strings
Outputs
  Tabs
  MIDI (for playback)
Notes: Matt

## Slide 17: Block Diagram
Pickup
AFE
MCU
DSP
UI
Guitar
Notes: Mike

## Slide 18: Our team
Michael Murphy
  Pickup & microcontroller
Matthew Wojick
  Analog front end & microcontroller
Michaela Shtilman-Minkin
  DSP Software & Algorithms
Taryk Alsagoff
  UI Software & Algorithms
Notes: Mike

## Slide 19: Block 1: Pickup
Hexaphonic pickup
  Identify individual strings
  Small
  Sensitive and accurate
Notes: Mike

## Slide 20: Block 1: MDR Deliverable
Pickup
  Purchase and prototype
  Generate & propagate signal to AFE
Notes: Mike

## Slide 21: Alternative Pickup Designs
Piezoelectric pickup
  expensive & undesirable modification
Optical pickup
  Has been shown to preform poorly
Notes: Mike

## Slide 22: Block 2: Analog Front-End (AFE)
Pre-amp
  Amplify incoming signal
Analog to Digital Conversion
  Sample at most 20kHz rate
  16 bit ADC
Notes: Matt
Split pickup will give around 1mV, where as normal pickups are around 100mV
16 bit: standard for ADCs, MCU also uses 16 bit, higher not necessary, but lower than 16 might not sample lower sound levels accurately
20kHz for highest note on the highest string to be detected
Lower strings need lower sample rate because there is a smaller gap between different notes

## Slide 23: Block 2: MDR Deliverables
Analog Front End (AFE)
  Purchase chip
  Amplify signal from pickup
Notes: Matt

## Slide 24: Block 3: Microcontroller (MCU)
FFT
  MCU for FFT in hardware
  TI 5000 series has FFT coprocessor
    1,024 bins in hardware
Notes: Mike

## Slide 25: Block 3: MDR Deliverables
Microcontroller
  Research and purchase a chip that can FFT
Notes: Mike

## Slide 26: Block 4: DSP software
Data
  Interpretation
  Analysis
  Packaging
Notes: Michaela

## Slide 27: Block 4: MDR Deliverables
Interpretation: Note recognition
  Identify a single, recorded note with its corresponding time stamp
Notes: Michaela

## Slide 28: Block 5: GUI
Notes: Taryk

## Slide 29: Block 5: MDR Deliverables
Display
  GUI with tabs display
Notes: Taryk

## Slide 30: MDR Deliverables - Summary
Pickup
  Purchase and prototype
  Generate & propagate signal to AFE
Analog Front End (AFE)
  Amplify signal from pickup
Microcontroller
  Hardware that can FFT
Note recognition
  Identify a single note with its corresponding time stamp
Display
  GUI with tabs display
Notes: Michaela
Pickup
  Mike – purchase as well as prototype own. Will generate and propagate signal to Matt (AFE)
Analog Front End
  Matt – will amplify signal from pickup with minimal noise and no clipping to send to microcontroller.
Microcontroller
  Mike and Matt – will have functional hardware FFT to send signals to Michaela (DSP)
Note recognition
  Michaela – able to identify single note with timing and send it to Taryk (GUI)
Display
  Taryk – will have rudimentary GUI to display note packages from Michaela and ugly tab

## Slide 31: Trial by Fire
Q&A