## Slide 1: FPR Presentation Team Frij

## Slide 2: Team FRIJ
Andrew Paisner - EE
Carlton Jones - EE
Adviser: Prof David Irwin
Shravan Nayak -CSE
Amrit Khalsa – CSE

## Slide 3: The Frij – Goals Reiterated
RFID and weight sensors keep status of food items in the Frij
Accurate and easy product identification via interface with UPC (barcode) database
Server/Database stores inventory for easy access and generates shopping list
App displays current inventory and accesses database-generated shopping list

## Slide 4: The Frij – Quantitative Goals
Resolution of scale: 3 ounces
Able to weigh up to 20 lbs of products
Able to track at least 10 items
90% accuracy in detecting items in the fridge
RFID to server latency: <1s
Barcode to server pi latency: <1s
Server to android app latency: <500ms
Overall system latency: <3s

## Slide 5: Block Diagram from PDR
Refrigerator
Barcode scanner
RFID sensor
Raspberry Pi
Food Item
(with RFID Tag)
Server
Product recognition
UPC Database
Pattern recognition
Mobile App
Database
Block 1: Carlton Jones - EE
Block 2: Andrew Paisner - EE
Block 3: Shravan Nayak -CSE
Block 4: Amrit Khalsa - CSE
User Interface
Door Sensor
Scale, Inst. Amp, ADC

## Slide 6: Block 1: Carlton Jones – Hardware
Use postage scales to weigh objects on each shelf
  Voltage across bridge is amplified and converted by ADC, then sent to be read by Pi
  Voltages are converted to weights (in ounces) by software on Pi
Refrigerator houses all hardware and incorporates power supply, isolates RFID scanner from outside tags

## Slide 7: Block 1: Carlton Jones – Hardware
Chose and ordered parts, supplied refrigerator
  Ordered RFID reader: Needed to fit required range, number of tags, power use, size, price, etc.
Designed amplification and ADC circuit
Experimented to test RFID and scale accuracies and create voltage to weight conversion equation
Removed voltage fluctuations in software
Added “Door Open/Closed” sensor to give Pi more information
Designed and built final hardware assembly

## Slide 8: Block 2: Andrew Paisner – Raspberry Pi
Wrote code to mimic RFID reader’s Windows sample program in Linux for Raspberry Pi
  Polls for tags in range of reader multiple times, writes all detected tags to file
Receives barcodes from scanner, weights as digital input from ADC via GPIO Pins
Sends list of tags, current total weight, and any new UPC codes to server as JSON array
  First determines if weights and codes have changed since last posting to server
  Repeats process once the server acknowledges data

## Slide 9: Block 2: Andrew Paisner – Challenges
Data transmission
  Protocol for the formatting of JSON Objects
  Only sending after significant change
  Data is only sent when necessary
      When the door is closed
      When the data is presumed to be corrected
Error handling
  Scale data is checked
  RFID reliability issues fixed in software
    Polling multiple times
    Minimizing delays

## Slide 10
Block 3: Amrit Khalsa – Server
Server links barcode, RFID tag, and weight data together
  Links based on ordering and timing
Tables in database: numbers, items, systeminfo
Server sends shopping list to App based on missing items
Server sends text alerts if item is missing for an amount of time or if the item is low weight. (<.3 of start weight)
  Uses Twilio API
Observed latency for executing queries: 31ms

## Slide 11
Block 3: Amrit Khalsa – Challenges
Determining when an item has actually left the Frij
  Tags data can be unreliable
  Solved by only recording change when weight change detected
Linking tag data with weight data
  Correct for dropped tags
Sending alerts on correct items

## Slide 12: Block 4: Shravan Nayak – App
Unified User Interface(UI)
  Redesigned unified user interface
  Navigation tabs for inventory and shopping list in a single app
Multithreaded architecture
  Main user interface thread
  One network thread for accessing the inventory
  Second network thread for accessing the shopping list
Refresh button
  Refresh button to get the updated data from the server
  The button triggers HTTP GET requests to server to get JSON objects containing inventory and shopping list

## Slide 13: Block 4: Shravan Nayak – Challenges
Unifying the app
  Solution- Navigation tabs user interface
Accessing data simultaneously from server
  Solution- Multithreaded application
  Main user interface thread
  One network thread for accessing the inventory
  Second network thread for accessing the shopping list
Refresh data
  Solution-Refresh button to get the updated data from the server

## Slide 14: Proposed FDP Deliverables
Hardware features clean and perfected
  Second postage scale for bottom shelf
  Power supplies and data cables neatly integrated into refrigerator
Pi begins on refrigerator startup and connects to local Wi-Fi automatically
Server and database with intelligent algorithms to suggest grocery items
Unified UI with refresh button
Incorporating alerts on the android app when item is running low or consumed
Notes: 14
14
14

## Slide 15: Accomplished FDP Deliverables
Hardware features clean and perfected
  Second postage scale for bottom shelf
  Power supplies and data cables neatly integrated into refrigerator
Pi begins on refrigerator startup and connects to local Wi-Fi automatically
Server and database with intelligent algorithms to suggest grocery items
Unified UI with refresh button
Incorporating alerts on the android app when item is running low or consumed
Notes: 15
15
15

## Slide 16: Demonstration – Step 1
Scan barcode on Land O’Lakes butter and insert into Frij
    Notice that the butter has appeared in the app’s inventory
Notes: 16
16
16

## Slide 17: Demonstration – Step 2
Remove butter from Frij
  Butter has moved from app’s inventory to the grocery list
Notes: 17
17
17

## Slide 18: Demonstration – Step 3
Remove three sticks of butter from box and reinsert into Frij
  Butter is back on inventory with lower weight.
Notes: 18
18
18

## Slide 19: Demonstration – Step 3
Remove butter from Frij entirely
  After a short time the server will send an alert to the user that the item has been used up.
Notes: 19
19
19