## Slide 1: Comprehensive Design Review
Team14:
BMW Brainwave Manipulated Wagon

## Slide 2: Team 14 Members
Zijian Chen
CSE
Tiffany Jao
CSE
Man Qin
EE
Xueling Zhao
EE
Faculty Advisor:
Qiangfei Xia

## Slide 3: Outline
System Review
Demo Overview
CDR Demo
FPR Deliverables

## Slide 4: Previous Block Diagram
Computer
Arduino/
C# Application
USB serial Write
Database
XBEE:TX
Signal Processing
Command Algorithm
User Interface
XBEE: RX
Arduino
Motor
Power Supply
Neurosky
headset
Bluetooth v3.0
ThinkGear Packet
Robotic Car
TX Arduino Module
Man Qin
Zijian Chen
Xueling Zhao
Tiffany Jao

## Slide 5: Revised Block Diagram
Computer
C# Application
command
Database
(Training Data)
Signal Processing
Bayesian
Classifier
User Interface
Bluetooth HC05
Arduino
Emotiv EPOC
headset
Proprietary wireless 2.4GHz
Robotic Car
Man Qin
Zijian Chen
Xueling Zhao
Tiffany Jao
EEG data
(real time) Alpha, beta power
(training)Alpha, beta power
(training)Alpha, beta power
Notes: Input/out of each block

## Slide 6: Current Control
Control using eye open/close
  Alpha and beta power
  Alpha power increases when close eyes
Use sensor around occipital lobe- visionary processing
  O1

## Slide 7: Signal Processing: FFT
Input: Raw EEG data from headset
C# library
Visualize raw EEG data in frequency domain
1 second frame － 128 samples
0.5 second overlapping window
Output: calculated alpha and beta total power
  Alpha wave : 8 – 12 Hz
  Beta wave: 13-30 Hz

## Slide 8: Before FFT: Raw EEG Data Voltage vs Time
Voltage (uV)
Time(Sec)
Fig1. (a)
Voltage (uV)
Time(Sec)
Fig1. (b)
Eye-Open
Voltage vs Time
Eye-Closed
Voltage vs Time
These two graphs are not meaningful as they are not indicting any information.

## Slide 9: After FFT: Power vs Frequency
Power(Watt)
Frequency(Hz)
Fig2. (a)
Power(Watt)
Frequency(Hz)
Fig2. (b)
Eye-Open
Power vs Frequency
Eye-Closed
Power vs Frequency
A dominant spike is observed in Fig2. (b) Eye-Closed.
Spike within alpha range

## Slide 10: FFT: Alpha and Beta Power Comparison
Alpha
Beta
Power Level
Eye-Open vs Eye-Closed
Open
Closed
Open
Closed
Fig3. Alpha power increases obviously, while Beta power stays in similar level
Fig3.

## Slide 11: Naïve Bayes Classifier
Probabilistic classifier based on applying Bayes’ theorem.
Bayes Theorem:
Why Naive Bayes Classifier :
  Provide strong machine learning ability to adapt patterns
  Run faster that other classifier, Need O(1) run time.
  High accuracy for classification with small size of training set.

## Slide 12: Naïve Bayes Classifier
How to Use ?
Real Time Data
AnalysisTrainingSet()
classify()
FindReference Point()
Database
(Training)
output
(Alpha,Beta,Trigger)
average of closed-eye alpha, beta
Update probability
(true/false)
(alpha, beta)
compare probability
of trigger on and off
Notes: What is Baye’s theorem. You should at least give a few word to explain it or an equation that helps the evaluators to understand. – Xueling Zhao

## Slide 13: Remote Robotic Car
HC-5 Bluetooth Module
Arduino Uno

## Slide 14: Remote Robotic Car
L298N Motor Driver Board
Power Supply
Powered by 6 AA batteries which have
total voltage of 9v.
Digital Input
From Arduino
Power
Output to motor

## Slide 15: Remote Robotic Car
HC-5
bluetooth module
Arduino
L298N Motor Driver Board
2 Motors
6 AA Batteries power

## Slide 16: Graphical User Interface - Training

## Slide 17: Graphical User Interface - Control

## Slide 18: Outline
System Review
Demo Overview
CDR Demo
FPR Deliverables

## Slide 19: Demo Overview
Utilize the brainwave to control the robotic car
  forward/stop
What’s working | Issues
Data retrieval from Emotiv real time signal processing Bayesian classifier distinguished eye open/close state Software interfacing with robotic car | 1 second delay between car and the software Wireless interference misclassified result

## Slide 20: Outline
System Review
Demo Overview
CDR Demo
FPR Deliverables

## Slide 21: Outline
System Review
Demo Overview
CDR Demo
FPR Deliverables

## Slide 22: Proposed FPR Deliverables
  Minimize the amount of misclassified command
    filter outlier in training set
  Ability to classify another command
    Turning
    Minimize delay

## Slide 23: Thank you
Questions?

## Slide 24: Backup Slide

## Slide 25: Naïve Bayes Classifier
Find Reference Point
  Get the average alpha and beta from training set
  Remove unusual-high alpha or beta data
  Use to determine if alpha or beta is high or low
Notes: What is Baye’s theorem. You should at least give a few word to explain it or an equation that helps the evaluators to understand. – Xueling Zhao

## Slide 26: Naïve Bayes Classifier
AnalysisTranningSet()
  Update Probability Table base on Training Set
P(H_Alpha¦Trigger) | P(H_Alpha¦NO_Trigger)
P(L_Alpha¦Trigger) | P(L_Alpha¦NO_Trigger)
P(H_Beta¦Trigger) | P(H_Beta¦NO_Trigger)
P(L_Beta¦Trigger) | P(L_Beta¦NO_Trigger)

## Slide 27: Naïve Bayes Classifier
Classify
  Calculate probability of trigger on
    on ← argmax P(Y = t)∏P(Xi|Y = t)
  Calculate probability of trigger off
    off ← argmax P(Y = NO_t)∏P(Xi|Y = NO_t)
  Compare on and off
  return classified result

## Slide 28: Why changes the headset?
It is needed to have more than 1 sensor for accurate measurement
2 references sensor

## Slide 29: FFT 1-sec frame vs 2-sec frame