## Slide 1: Team E-μ
Advised by Professor Baird Soules
Preliminary Design Review – October 2014
Notes: 30 seconds

## Slide 2: Team members
Professor Baird Soules
Advisor
Christopher Allum
CSE and EE
Shehzeen Hussain
EE
Jeffrey Maloney
EE
Notes: 30 seconds

## Slide 3
People guiding vehicles through tight or crowded spaces are unable
to reliably communicate with the driver.
Visual cues are not always enough because:
The driver may become distracted
Low light levels impair vision
Noisy environments
The spotter on ground isn’t visible
Land profiles that obstruct vision
Jeff
The Problem
Fig 1: A guide is often deployed on the ground to assist vehicle operators [1]
Notes: 1 minute no evidence of the process we went through to get to the problem.

## Slide 4: The Problem
Failure to safely maneuver vehicles can result in
Damage to vehicles and other equipment
Injuries to trained personnel
In extreme cases - death
Jeff
Fig 2: Vehicles in motor pools and shipping warehouses often squeeze into very tight spots. [2]
Notes: 1 minute
Damage to equipment and damage to people

## Slide 5: Effects on Individuals Effect on Groups
Injuries can mean
Incurred medical expenses
Impaired mobility
Loss of job
Loss of life
Unsafe work environments can lead to lower levels of morale
Retention rates are lower for dangerous jobs
Expensive for the workplace
Jeff
The Problem
Notes: 1 minute
remo

## Slide 6: Requirements
Such a system should:
Be portable and weigh under 5 pounds
Wireless communication within at least 10 meters
Work in low light levels
Work in high noise areas
Implement existing hand signals
Be intuitive and easy to use
Christopher
10 meters
Guide
Large Vehicle
Night Time
Loud Noises
Loud Noises
Obstacle
Fig 3: Worst case scenario depicting loud noises and low light (figure not to scale)
Notes: 2 min

## Slide 7: Our Solution
A wearable device to detect hand signals and relay information to a vehicle operator via recognizable pre-recorded voice commands
No need to change existing hand gestures
Easy for both vehicle operator and guide to use
Shehzeen
Fig 4: Wearable Armband [3]
Notes: 2 min

## Slide 8: Input and Output
Input
Existing hand signals can be
detected using a combination of
EMG and IMU sensors
Output
An audio signal delivered by
wireless speakers inside the cab and to the guide on the ground.
Shehzeen
EMG – Electromyography
IMU – Inertial Measurement Unit
Fig 5: Wireless Speaker [4]
Fig 4: Armband [3]
Notes: 1 min

## Slide 9: Design Alternatives
Sensing Alternative:
  External vehicle-mounted sensor: Proximity sensors
Output Alternatives:
  Visual output interface with device like Google Glass
  Car radio interface
  Phone application
System Alternatives:
  Hand-held radio
  Rearview camera
Shehzeen
Notes: 1 min add specs

## Slide 10: System Level Block Diagram
Output Devices
Bluetooth TX/RX
Speaker
Armband
Bluetooth TX/RX
EMG Sensor
IMU Sensor
10V Rechargeable Battery
Signal Conditioning Circuitry
SD Card Module
3.3V Regulator
MCU
Controller
Pattern Recognition
IMU Digital Processing
Power
Data Signal
Bluetooth
Control
Hardware Block
Software Block
Jeff
Standby Mode Flip Switch
Notes: >4 minutes differentiate btwn software and hardware verbally (if not in block diagram)
Need a d/a to give to speaker ex. Mp3 decoder or high speed pwm for audio. Look up teensy dac
Possibly have black arrow from mcu instead of controller

## Slide 11
First Subsystem: EMG Sensor & Conditioning
Output Devices
Bluetooth TX/RX
Speaker
Armband
Bluetooth TX/RX
EMG Sensor
IMU Sensor
10V Rechargeable Battery
Signal Conditioning Circuitry
SD Card Module
3.3V Regulator
MCU
Controller
Pattern Recognition
IMU Digital Processing
Power
Data Signal
Bluetooth
Control
Hardware Block
Software Block
Standby Mode Flip Switch
Shehzeen

## Slide 12: First Subsystem: EMG Sensor & Conditioning
Summary: Electromyography (EMG) measures electrical activity produced by skeletal muscles.
Requirements:
Must sense muscle activity reliably.
Ability to setup within two minutes.
Input
Two sets of surface electrodes on two main forearm muscles.
±5V from rechargeable battery
Output
Rectified waveform envelope ranging from 0-5VDC.
Shehzeen
Figure 6: Basic physiology of the forearm.
Fig 7: Arm with electrodes [5]
Notes: 2 min
Figuring out what the wrist is doing is impossible from the tricep/bicep. Want to use grip as one of the gestures.

## Slide 13: First Subsystem: EMG Sensor & Conditioning
Jeff
EMG Electrodes
LPF
Full Wave Rectifier
Differential
Amplifier
LPF
MCU
A/D
Fig 8: A waveform captured using Polulu muscle sensor v3. This is the expected output of our differential amplifier.
Pre-Amp
Fig 7: Surface Electrodes [5]
Notes: 1 minute
Specify the word differential
Pre-amp say & or with
Full wave may be one word
Check block contents
10 bit resolution on a/d

## Slide 14: Second Subsystem: IMU Sensor & IMU Digital Processing
Output Devices
Bluetooth TX/RX
Speaker
Armband
Bluetooth TX/RX
EMG Sensor
IMU Sensor
10V Rechargeable Battery
Signal Conditioning Circuitry
SD Card Module
3.3V Regulator
MCU
Controller
Pattern Recognition
IMU Digital Processing
Power
Data Signal
Bluetooth
Control
Hardware Block
Software Block
Standby Mode Flip Switch
Christopher

## Slide 15: Second Subsystem: IMU Sensor & IMU Digital Processing
Requirements of Sensor:
Inertial Measurement Unit (IMU) must contain:
  Accelerometer: Measures the direction and magnitude of acceleration
  Gyroscope: Measures angular velocity to help determine orientation
  Magnetometer: Measures the current orientation relative to Magnetic North
I²C serial host interface for communication with microcontroller
Input to IMU Digital Processing System:
Acceleration including gravity
Angular velocity
Magnetic field strength
Output to Pattern Recognition System:
Velocity, Orientation
Gravity-free data
Christopher
Fig 9: IMU MPU-9050 [5]
Notes: 2 min
Know how to calibrate it

## Slide 16: Third Subsystem: Pattern Recognition & Controller
Output Devices
Bluetooth TX/RX
Speaker
Armband
Bluetooth TX/RX
EMG Sensor
IMU Sensor
10V Rechargeable Battery
Signal Conditioning Circuitry
SD Card Module
3.3V Regulator
MCU
Controller
Pattern Recognition
IMU Digital Processing
Power
Data Signal
Bluetooth
Control
Hardware Block
Software Block
Standby Mode Flip Switch
Christopher

## Slide 17: Third Subsystem: Pattern Recognition & Controller
Christopher
Summary: The pattern recognition system translates gestures to audio output by comparing inputs to stored patterns using KNN (k-nearest neighbors) algorithm. The result of the pattern recognition determines which audio message is sent via Bluetooth.
Requirements:
Differentiates between six distinct hand gestures to indicate signals: left, right, forward, backward, slow down, stop.
Interface with peripherals: sensors and Bluetooth module.
Interface with SD card containing speech library corresponding to gestures
Inputs:
Conditioned EMG Analog Signal
Position vector from IMU Digital Processing stage
Outputs:
Audio signal sent via Bluetooth module
Fig 10: Teensy 3.1 [6]
Notes: 2 min

## Slide 18: Tasks
Shehzeen & Jeff
Design EMG signal conditioning circuitry
Determine optimum position for EMG electrodes for detecting electrical signals from muscles
Filter and amplify EMG signals
Calibrate sensor circuit design
Design envelope detector for EMG waveshaping
Sensor interface with microcontroller
Christopher
Program a KNN pattern recognition system in C++ for the microcontroller
Analyse the IMU data to determine orientation and a velocity vector
Shehzeen
Manage Bluetooth link between microcontroller and speakers
Jeff
Design voltage regulation circuitry

## Slide 19: MDR Deliverables - November
Working analog circuit implementation for measuring muscle activity data
Program to show waveform of EMG signals using the processor
Program to show simplified digital data from the IMU for different gestures
Basic pattern recognition program
Shehzeen
Circuitry
“Left”
Fig 11: Deliverable Components

## Slide 20: Questions?
Thank μ!

## Slide 21: References
De Luca, Carlo J. "The Use of Surface Electromyography in Biomechanics."Journal of Applied Biomechanics (1997): 135-63. Human Kinetics Publisher Inc. Web. 5 Sept. 2014.
Artemiadis, P.K., and K.J. Kyriakopoulos. “EMG-Based Control Of a Robot Arm Using Low-Dimensional Embeddings.” Robotics, IEEE Transactions On 26.2 (2010) : 393-398. © 2010 IEEE
Veresano, Fabio. “A Guide to Using IMU (Accelerometer and Gyroscope Devices) in Embedded Applications.” Starlino Electronics. N.p., n.d. Web.
Sachs, David. "Sensor Fusion on Android Devices: A Revolution in Motion Processing." YouTube. YouTube, n.d. Web. 01 Oct. 2014.
Notes: http://x.couver.us/index.php?main_page=product_info&products_id=1129