## Slide 1: Shush! SDP Group 14:
Ryan Coleman
Christos Lemonias
Tim Reardon
Shaaz Salim
Notes: Ryan: Just intro

## Slide 2: This is Shush! Christos Lemonias Tim Reardon Shaaz Salim Ryan Coleman
Notes: Ryan

## Slide 3: Problem Statement
Difficulty sleeping when your roommate's alarm goes off
Feeling bad when you keep your roommate awake
Enjoy listening to white noise before bed
Alarm that wake you up without waking anyone else
Robust and easy to use system which enhances the user's experience
Notes: Ryan

## Slide 4: Specifications
Array
  Works properly within a meter from pillow
  Has it’s own dedicated Bluetooth link
  Sound covers approximate size of pillow (20x28 in)
  Volume at pillow between 70 and 90 dB
App
  The app will be designed and available for android
  Functions such as snooze, alarm time, and tone select
Notes: Christos

## Slide 5: Cost Analysis
Past | QTY | Unit Price | Description | Total
 | 1 | $31.25 | Teensy 3.5 | $31.25
 | 10 | $4.46 | Ultrasonic Transducer | $44.60
 | 2 | $0.96 | Logic Output | $1.92
 | 4 | $1.30 | Half Bridge Driver | $5.20
 | 2 | $0.95 | Voltage Regulator | $1.90
 | 4 | $0.92 | MOSFET PT8N | $3.68
 | 1 | $8.50 | HC-05 Bluetooth Serial Module | $8.50
 | 2 | $8 | Shipping | $16
 |  |  | Total | $113.05
Future | 1 | $8.00 | MicroSd and Adapter | $8.00
 | 1 | $22.00 | Audio Shield | $22.00
 | 1 | $17.45 | WALL MOUNT ADAPTER 24V 24W | $17.45
Notes: Tim

## Slide 6: Gantt Chart
Notes: Shaaz

## Slide 7
Block Diagram (Original)
Alarm Box
Micro Controller
Parametric Circuitry
Bluetooth
Display
Memory
Power
Parametric Array
Bluetooth
Transducers
Battery
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Notes: Tim

## Slide 8: PDR Recommendations (1)
Simplify Design/Combine array with alarm box
  Keeps design from getting too complicated
  Less spots for errors to occur
  Only need one Bluetooth connection as opposed to two
  Gets rid of battery
We took this into account moving forward and...
Notes: Tim

## Slide 9
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Block Diagram (Updated)
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Tim

## Slide 10: Transducers
16mm piezoelectric transducers
  Parallel honeycomb setup
  Current setup uses 10
Not currently at optimal distances
  Breadboard pin spacing isn’t great
  Future PCD design needed
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Ryan

## Slide 11: Parametric Circuitry
Opto isolator
  protects our microcontroller from harmful currents
H-bridge Amplifier
  Microcontroller outputs 3.3V but transducers need 20V
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Ryan

## Slide 12: Microcontroller
Teensy 3.5
  Up to 120 MHz ARM® Cortex
Supply voltage: 3.3V
SPI communication pins (for SDHC external memory interface)
PWM capabilities
  many PWM output pin options
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Christos

## Slide 13: Memory
External memory card will be used
  SanDisk microSDHC card
  16 GB of space
What is being stored?
  WAV files for music/tones
  Alarm clock settings
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Shaaz

## Slide 14: Bluetooth
HC-05
  Maintains connection up to 30 feet
  Voltage levels line up with Teensy
Software will allow for easy manipulation of received information
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Shaaz

## Slide 15: Voltage Supply
Parametric circuitry needs a 20V supply
Teensy needs 3.3V
24V wall adapter will be used
  Voltage regulator circuits to provide both voltage supplies
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Christos

## Slide 16: App
Developed in Android Studio for Android Apps
User controls
  Pick time and day of alarms
  Choose repeating alarms
  Choose alarm tones
Will send all information to the Teensy
Parametric Array
Bluetooth
Power
App
Interface
Phone Systems
Bluetooth
Accelero- meter
Memory
Speaker
Micro Controller
Memory
Parametric Circuitry
Transducers
Notes: Tim

## Slide 17: PDR Recommendations (2)
Add Bluetooth connection between microcontroller and phone to MDR Deliverables
  Important for the eventual combination of our deliverables
  Didn’t want to leave this for later and possibly delay ourselves
We took this into account moving forward and...
Notes: Shaaz

## Slide 18: MDR Deliverables
Bluetooth Connectivity Demonstration
  Developed By Shaaz Salim
App Framework Presentation
  Developed by Timothy Reardon
Parametric Circuitry with Array
  Developed by Ryan Coleman and Christos Lemonias
Notes: Shaaz

## Slide 19: Bluetooth Presentation
Mobile app code sends ‘high’ signal
while button is pressed.
Teensy constantly checks for change
in signal from Bluetooth.
Notes: Shaaz

## Slide 20: Framework Presentation
Notes: Tim

## Slide 21: Parametric Schematic
Optoisolator 1
Optoisolator 2
H-bridge
Speaker
Notes: Ryan

## Slide 22: Parametric Array Spread
Notes: Christos

## Slide 23: Parametric Presentation
Notes: Ryan “We have taken to also referring to this system as the brain of our project.

## Slide 24: CDR Deliverables
Functional prototype (All Members)
  Fully functional App
  System control via App
Power supply / regulation implementation (Tim and Shaaz)
PCB design (Ryan and Christos)
Notes: Ryan

## Slide 25: Questions?
Notes: comparable Processors? Limited processing in the box, mostly non continuous
Estimate battery life? power usage of bluetooth and transducer

## Slide 26: Weight
Current Speaker/board set up is only 0.28lbs
Future PCB weight should be similar to our breadboard
Components should not add much to the overall weight
Notes: comparable Processors? Limited processing in the box, mostly non continuous
Estimate battery life? power usage of bluetooth and transducer

## Slide 27: Power Consumption
Teensy MC: maximum of .33W at operating voltage of 3.3 V
  Output high current total for all ports: 100mA
  Output high voltage: 3.3V
  relatively low power; regulated by power supply
Transducers: 2.1 uW of power at 20V
  Each 40KHz piezo transducer dissipates .21 uW
  10 piezo transducers