## Slide 1
Weather Box
Team 3/LH 6
SDP 20
CDR
March 9, 2020

## Slide 2: Introduction
Professor Zink
Advisor
Anthony Mendez
CompE
Software Lead
Tina Maurer
EE
Hardware Lead
Stephan Kim
CompE
Christian Norton
CompE
Notes: Introduce Ourselves

## Slide 3: Problem Statement
Commercial weather stations can effectively collect data for a specified area at the macroscale. However, weather conditions in these area can vary greatly at the microscale.
These micro-weather conditions can impact various situations, such as the effective use of a wind farm, the flow of pollutants and waste through an area, and a drone’s ability to fly for emergency services.
Notes: Christian

## Slide 4: System Specifications
Each sensor package will take measurement at its location and the web server must create a map of at least 75x50 m2 based on data from sensor packages
Each sensor package must be mountable and weighs less than one pound
Each sensor package must measure wind, temperature, barometric pressure, humidity, dust, and air quality with 95% confidence
Each sensor package must have a battery life of at least 24 hours
Sensor package must be operable in the range of 20 degrees Fahrenheit to 100 degrees Fahrenheit
Each sensor package should be able to transmit sensor data to a web server via WiFi
Each sensor package must be manufacturable for at most $120
Notes: Tina

## Slide 5: Our MDR Solution
Notes: Stephan

## Slide 6: Our CDR Solution
Notes: Stephan

## Slide 7: CDR Prototype - Software
Notes: Anthony
Three major components to the software
  Firmware
    Handles reading sensor data, and sending to the web server
  Web Server
    Handles receiving data from the Weather Boxes, storing the data, and sending to the client websites
  Website
    Handles requesting data from the web server and handles placing data onto the map.

## Slide 8: CDR Deliverables
A first revision custom PCB containing the sensor suite and power circuitry
Firmware written and tested for remaining sensors
  ams CCS811B-JOPD500 Air Quality Sensor
  SHARP GP2Y1010AU0F Dust Sensor
Preliminary interpolation algorithm implemented on the map
Prototype physical enclosure for the sensor package
Notes: Anthony
Promised:
First revision of a custom PCB with sensors and power circuitry
Firmware written and tested for the Air Quality and Dust Sensor
Preliminary interpolation algorithm on the map
Preliminary physical enclosure

## Slide 9: CDR Team Responsibilities
Tina
  Hardware Lead
  PCB, Enclosure
Anthony
  Software Lead
  Firmware - Air Quality Sensor
  Website/Server - Google Sign-In, Systems Management
Stephan
  Firmware - Dust Sensor, WiFi
Christian
  Website - UI Overhaul, Interpolation
Notes: Our Responsibilities
Anthony
Oversaw and managed communications between firmware, server, and client side.
Programmed the Air Quality Sensor
Implemented Google Sign In and Systems Management

## Slide 10: PCB Design: Tina
Created schematic and completed layout for printed circuit board using KiCAD software
Main and sensor board are both four layers with a ground plane on the second layer
Power circuit has been adjusted from LDO regulators to switching regulators for power rails
Boards were hand soldered and tested against prototype measurements
Notes: Tina

## Slide 11: System Enclosures: Tina
Designed robust housings for each board using TinkerCAD, then 3D-printed with PLA filament
The interlocking joints between the lid and box create a seal for each enclosure
Along with cable openings, a small window was created in the sensor housing to allow the sensors to be exposed to weather conditions
Notes: Tina

## Slide 12: Firmware: Stephan, Anthony
MCP3008 10-bit ADC
  Removed in favor of STM32’s built-in ADC
STM32 Internal ADC
  12-bit, simplified circuit by removal of other ADC
  Programmed using STM’s HAL API in C
Sharp GP2Y1010AUF Dust Sensor
  Analog Dust Sensor
  Utilizes GPIO for LED and ADC for output reading
Notes: Stephan

## Slide 13: Firmware: Stephan, Anthony
ESP8266 WiFi Module
  Wrote C driver in order to interface between STM32
and ESP8266
  C drivers send AT commands through STM32
and UART serial protocol to program our module
ams CCS811 Air Quality Sensor
  Wrote C library to handle sensor operations
  Library mimicked Bosch driver format
  Utilizes I2C communication protocol
Notes: Stephan
Anthony
Wrote a C library to handle sensor operations
Library mimicked format of the Bosch sensor, changed functions to reflect AQ sensor operations
I2C to request and retrieve data

## Slide 14: Google Sign-In API: Anthony
Needed to ensure Integrity and Availability
UMass utilizes Google Mail
Easy to implement
Created Public Client ID in Google Cloud
  Once signed in, JavaScript function is called
  Sends user token to server
  Server checks if user is an admin
  If so, server assigns the client a session variable “admin”
Notes: Anthony
Needed an Authentication API to let us and only us edit the systems database on the website
UMass uses Google Mail
Google provides a Sign-In API that’s easy to use
The setup and adding to our website was easy
Client signs in with Google, website receives a token, sent to our web server, and checks if the user is an admin.

## Slide 15: Systems Management: Anthony
Once authenticated, admin can:
  Add a system to the database
  Remove a system from the database
  Edit a system’s location
Website does front-end and back-end data validation
Operations only proceed if session variable “admin” exists and is set to “true”
Notes: Anthony
If user is an admin, they can manipulate the systems database without writing SQL queries
  Adding, removing, and editing systems
Website and Server does data validation
If user is not an admin but still tries to send changes to web server, web server will reject those changes

## Slide 16: Interpolation: Christian
Current implementation uses a linear interpolation
  Calculate an average latitude, longitude, and weight for every combination of two points
  Populate the heatmap with these points
  The function can be called repeatedly to generate a more flushed out heatmap
Next implementation will use Inverse Distance Weighting
  Allows for calculation of points outside of the bounds of systems
Notes: Christian

## Slide 17: UI Overhaul: Christian
Improved dynamic transition between desktop and mobile layout
  Column scaling is done under a set of defined CSS classes
  Classes can be applied to any section allowing for easier separation
Enlarged buttons for better use on mobile layout
Improved colors for better readability
Reserved space for system management
Notes: Christian

## Slide 18: CDR Result
A first revision custom PCB containing the sensor suite and power circuitry
Designed, laid out, and tested PCB set
Firmware written and tested sensors
  ams CCS811B-JOPD500 Air Quality Sensor
  SHARP GP2Y1010AU0F Dust Sensor
Preliminary interpolation algorithm implemented on the map
Designed and printed prototype enclosure for the PCB set
Notes: Tina

## Slide 19: Gantt Chart
Notes: Christian

## Slide 20
Notes: Questions?

## Slide 21: Systems Management Diagram: Anthony
Notes: Anthony

## Slide 22: Website