## Slide 1: ECE 671 – Lecture 19
Available Bit Rate Streaming

## Slide 2: Video on Demand
VoD: dominate factor of today’s Internet
  VoD: 67% of peak hour downstream Internet traffic in US [1]
VoD challenges
  Various end user devices
    TV, laptop, tablet, cell phone
  Variety of access networks
    Ethernet, Wifi, Cellular networks
[1] Sandvine. Global Internet phenomena report 2015

## Slide 3: Introduction
Video streaming has moved from fixed bit rate to adaptive bit rate streaming (ABR).
Example, Netflix creates up to 120 different quality versions to support ABR streaming.
http://www.streamingmedia.com/Articles/Editorial/What-Is-.../What-is-Adaptive-Streaming-75195.aspx

## Slide 4: Adaptive Streaming Solutions
Microsoft SmoothStream
Apple HTTP Live Streaming (HLS)
Adobe HTTP Dynamic Streaming (HDS)
MPEG – Dynamic Adaptive Streaming over HTTP (DASH)

## Slide 5: Adaptive Bit Rate (ABR) Streaming
Single video split into segments – 2s, 4s, 10s…
Each segment in different qualities
Based on Advanced Video Codec (AVC)
Client decides next requested quality based on download rate or buffer level
  Avoid playback freezing
* Picture source: https://bitmovin.com/bitdash-mpeg-dash-player/

## Slide 6: DASH – Playback without Pauses
Split video into segments
Different qualities for each segment
HTTP based
  Can be hosted on regular HTTP server
  Easy firewall penetration
Client driven segment retrieval
  No HTTP server logic needed

## Slide 7: Timeliness
Start presenting data (e.g., video playout) at t1
Consumed bytes (offset)
  variable rate
  constant rate
Must start retrieving data earlier
  Data must arrive before consumption time
  Data must be sent before arrival time
  Data must be read from disk before sending time
time
data offset
consume function
arrive function
send function
read function

## Slide 8: Quality Adaptation Issues
Identify existing issues with current rate estimation approaches
Improve QoE
  Prevent re-buffering
  Reduce quality changes
  Keep average quality as high as possible
No server modifications  work with any web server
Evaluate new approach in testbed and real-world scenario

## Slide 9: Critical Observation I
User space rate estimation
Impact of NIC segment offloading
DASH in User Space: Inaccurate Rate Estimation
More accurate for longer segments

## Slide 10: Critical Observation II
Segment Size Impacts Download Rate
Download rate for each segment
  With segment length 2s & 10s
  With persistent & non-persistent HTTP connection
Higher rate for longer segments (10 seconds)
Higher rate for persistent HTTP connection

## Slide 11: Critical Observation III
DASH is TCP submissive
DASH with 2 sec segments
DASH with 10 sec segments
Cross-traffic off
DASH with competing TCP flow
  Butterfly topology
  One competing TCP flow
DASH behaves as ON/OFF source on top of TCP
  2s segment: 1.5 Mbps
  10s segment: 3.8 Mbp
10 Mbps

## Slide 12: Segment Size Impacts TCP CW
Congestion window size
  Much larger cwnd size for longer segments
Inter-GET times
  Silence time between two segment requests
  Longer segments have shorter inter-GET time
CDF of inter-GET times
Congestion window comparison