## Slide 1: ECE 671 – Lecture 3
Review of Internet Protocols Network Layer

## Slide 2: Interface-to-interface connectivity
We now have links. How to get across the network?

## Slide 3: Virtual circuits
Static allocation of path

## Slide 4: Datagrams
Datagrams are forwarded independently

## Slide 5: Datagrams vs Virtual Circuits
 | Datagrams | Virtual Circuits
Setup Phase | Not needed | Required
Router State | Per destination | Per connection
Addresses | Carries full address | Carries short label
Routing | Per packet | Per circuit
Failures | Easier to mask | Difficult to mask
Quality of Service | Difficult to add | Easier to add

## Slide 6: Internet Protocol
IP header
  Source and destination address
  Datagram length
    Header + data
  Upper layer protocol
    Identifies TCP, UDP, etc.
  Time to live
    Protection against accidental loops
  Header checksum
    Protection against bit errors
  Fragmentation possible
    Link layer limited to some datagram size (min. MTU is 576 bytes)

## Slide 7: IP addresses
IP address is 32-bit field
  Uses dotted decimal notation:
How should addresses be allocated?

## Slide 8: Address aggregation
IP addresses aggregated into subnets
  Each subnet represented by “prefix”
  Notation indicates length of prefix
Example:

## Slide 9: Address aggregation
What are potential problems?

## Slide 10: Address aggregation
IP addresses may “move”
Routers perform “longest prefix match”
  Most specific information

## Slide 11: Other IP aspects
Routing
  Determines forwarding
ICMP
  Error handling
Link layer
  Address resolution (ARP)
  Dynamic IP addresses (DHCP)
Application layer
  Domain names (DNS)
Transport layer
  Network address translation (NAT)
New IP version: IPv6