## Slide 1: ECE 671 – Lecture 7
Interconnects and Switching Fabrics

## Slide 2: Network systems
How to interconnect ports of the network system?

## Slide 3: Interconnect designs
What are possible designs for an interconnect?
  Need to get data from any input to any output

## Slide 4: Interconnect designs
Shared bus
Shared memory
Crossbar
Multistage switching fabric
Scalability is important
  Assume N ports with C bandwidth each
  What is the speed requirement for each component?
  In practice: 1xC to 2xC is reasonable, more is not feasibles

## Slide 5: Scalability evaluation
Shared bus
Shared memory
Crossbar

## Slide 6: Multistage switching fabric
Switching element
  Two states: cross-over or straight
  Very simple implementation
Switch fabric assembled from multiple switching elements:

## Slide 7: Switching fabric topologies
Topologies determine properties
  E.g., blocking probability, self-routing property, etc.
Delta network
Omega network

## Slide 8: Contention in interconnects
Any traffic pattern should be handled
  Focus on “permissible traffic load”
  Over “long” term, each port receives and sends C
Short-term variation in traffic can lead to contention
  Switching system needs to deal with contention
What are possible solutions

## Slide 9: Queuing techniques
Input queuing

## Slide 10: Queuing techniques
Output queuing

## Slide 11: Queuing techniques
Virtual output queuing

## Slide 12: Queuing techniques
Combined input-output queuing

## Slide 13: Queuing techniques
Input queuing
  Head-of-line blocking
  Theoretical throughput limit 58.6%
Output queuing
  Requires speedup of N
Virtual output queuing
  N2 queues
VOQ and CIOQ require scheduling algorithm

## Slide 14: Switch scheduling
Model of scheduling problem
  Request matrix or bipartite graph
  Goal: find match in graph

## Slide 15: Switch scheduling
Goals for scheduler
  High throughput
  Low latency
  Fairness
  Low-cost implementation
Comparison
  iSlip, FIRM, MP
  Output queuing is optimum