## Slide 1: ECE 671 – Lecture 10
Routers
Data plane and control plane

## Slide 2: Routers

## Slide 3: Physical view
Input and output “folded” onto same line card

## Slide 4: Data plane vs. control plane
Data plane:
  Regular traffic
Control plane:
  Routing updates
  Error handling
  Etc.

## Slide 5: Prefix matching
Data plane needs to perform prefix matches
  Determine longest matching prefix for destination address
Prefixes stored in forwarding information base (FIB)
Where do FIB entries come from?

## Slide 6: Routing
Shortest path routing
Centralized approach
  Each node has full “view” of network
  Each node calculates shortest path using routing algorithm
  “Link state algorithm”
  (Exchange of link information always decentralized)
Distributed approach
  Each node computes best path without full view
  Shortest path computed as link information is exchanged
  “Distance vector algorithm”

## Slide 7: Link state algorithm
Link cost of all links is broadcast to all nodes
Dijkstra’s algorithm to find shortest path to all nodes
  Each node calculates its own tree
Notation:
  D(v) is least cost to v in current iteration
  p(v) is previous node along least cost path
  N’ is subset of nodes with guaranteed least cost paths
Algorithm
  Initialization:
    N’={u}
    For all nodes v: if neighbor of u then D(v)=c(u,v), else D(v)=∞
  Loop until N’=N:
    Find wN’ with minimum D(w) and add w to N’
    For each neighbor v of w (vN’): D(v)=min(D(v),D(w)+c(w,v))

## Slide 8: Link state algorithm
Example
Iterations
step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f)
0 |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 

## Slide 9: Link state algorithm
Example
Iterations
step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f)
0 | {a} | 1,a | ∞ | 3,a | ∞ | ∞
1 | {a,b} |  | 6,b | 2,b | 5,b | ∞
2 | {a,b,d} |  | 6,b |  | 4,d | 9,d
3 | {a,b,d,e} |  | 5,e |  |  | 8,e
4 | {a,b,c,d,e} |  |  |  |  | 7,c
5 | {a,b,c,d,e,f} |  |  |  |  | 

## Slide 11: Link state algorithm
Can we adjust link weights based on traffic?
  Could avoid congestion
What is the problem?

## Slide 12: Link state algorithm
Traffic-based link weights may cause instability: