## Slide 1: ECE 671 – Lecture 11
Routers
Routing algorithms

## Slide 2: Routing
Shortest path routing
Centralized approach
  Each node has full “view” of network
  Each node calculates shortest path using routing algorithm
  “Link state algorithm”
  (Exchange of link information always decentralized)
Distributed approach
  Each node computes best path without full view
  Shortest path computed as link information is exchanged
  “Distance vector algorithm”

## Slide 3: Distance vector algorithm
Features
  Distributed
  Iterative
  Asynchronous
Each node reports local view
  Cost to neighbors
  Routes to others via neighbors
Each node picks the best option
  Bellman-Ford equation: dx(y) = minv{c(x,v)+dv(y)}
Information is exchanged as “distance vector”
  Shortest distance to all nodes as seen locally
With enough exchanges, routing converges

## Slide 4: Bellman-Ford Equation
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 5: Example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:
Slide from Kurose & Ross “Computer Networking A Top Down Approach

## Slide 6: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Slide from Kurose & Ross “Computer Networking A Top Down Approach

## Slide 7: Distance Vector Algorithm
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Slide from Kurose & Ross “Computer Networking A Top Down Approach

## Slide 8: Distance Vector Algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:
Slide from Kurose & Ross “Computer Networking A Top Down Approach

## Slide 9
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
Slide from Kurose & Ross “Computer Networking A Top Down Approach

## Slide 10
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
Slide from Kurose & Ross “Computer Networking A Top Down Approach

## Slide 11: Distance vector example
Example:
  Two updates:
    First, node 2
    Then, node 3

## Slide 12: Routing in the Internet
How many nodes do we have in the Internet?
How many links do we have in the Internet?
Scalability becomes a problem
  Number of nodes/links in algorithm
  Adding/removing machine could cause global routing update

## Slide 13: Autonomous Systems
Internet is clustered into autonomous systems (AS)
  Single administrative entity (e.g., company, university)
Inside an AS (“local” routing):
  Intra-AS routing protocol
Between ASs (“global” routing):
  Gateway routers connect ASs
  Inter-AS routing protocol
Combination of routing algorithm determines forwarding table

## Slide 14: Intra-AS routing: RIP
Routing Information Protocol
  Originally distributed in 1982 BSD UNIX
  RFC 2453
Distance vector protocol
  “Hop” count as metric
  Maximum hop count is 15
Routing updates
  Every 30 seconds as UDP packets
  “RIP advertisement”
  Up to 25 destination subnets
Link considered down if no update in 180 seconds

## Slide 15: Intra-AS routing: OSPF
Open Shortest Path First
  “Open” as in “not proprietary”
  RFC 2328
  Designed as successor to RIP
Link-state protocol
  Routers have full graph of network
  Dijkstra’s algorithm for shortest path
  Link weights set by administrator
    Difficult to achieve operational goals
Routing updates
  HELLO messages every 10 seconds (check if link is alive)
  Flooding of link-state information
    Routers send link-state info to all other routers
  Route update at least once every 30 minutes

## Slide 16: Inter-AS routing: BGP
Border Gateway Protocol
  De-facto standard for inter-AS routing in Internet
  RFC 1771
Advertisement of reachability
  From Kurose& Ross: “A subnet screams ‘I exist and I am here,’ and BGP makes sure that all the ASs in the Internet know about the subnet and how to get there. If it weren’t for BGP, each subnet would be isolated – alone and unknown by the rest of the Internet.”
BGP provides
  Information on subnet reachability from neighboring ASs
    Propagated to each internal router of AS
  Means to determine “good” routes to subnets
    Based on reachability and AS policy

## Slide 17: Inter-AS routing: BGP
BGP sessions
  Connection between routers to exchange BGP information
  External BGP (eBGP) session
    Session spanning two ASs
  Internal BGP (iBGP) session
    Session within one AS
Reachability information
  Reachable subnet (CIDR prefix)
  BGP attributes
    AS-PATH: path to subnet (ASs traversed)
    Next-HOP: IP address of advertising router
Path vector protocol
  Information to avoid loop or other ASs (import policy)

## Slide 18: Inter-AS routing: BGP
Route selection:
  Often multiple routes available
  Elimination procedure:
    Local preference value set by administrator
    Shortest AS-PATH (=DV with AS hop metric)
    Closest NEXT-HOP router (determined by intra-AS routing)
      “Hot potato routing”
    BGP identifiers
Example
  Y is “stub” network
  X is “multihomed” network
    X is customer network
    X should not forward data between B and C
    X advertise as if stub domain (e.g., not XCY to B)
  B might not want to advertise path to A or W to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 19: Inter-AS routing: BGP
Peering agreements between ASs often confidential
  Administrators are careful what to advertise
  Avoid free riding of traffic from other ISPs
BGP issues
  BGP not always stable
  Route flapping can cause further instability
    Router might get overloaded by BGP messages
    If router can’t keep up, it might be considered down
  Various heuristic fixes
    Route dampening