## Slide 1: ECE 671 – Lecture 14
Transport Layer Systems Firewalls and NAT

## Slide 2: Transport layer systems
Traffic handling at level of connections or flows
  Firewall
  Network Address Translator

## Slide 3: Firewall
Firewall distinguishes between traffic sources
  “Inside” traffic is let through
  “Outside” traffic is blocked
How to achieve duplex communication?

## Slide 4: Firewall
Firewall keeps record of connections from inside
  Traffic with reverse 5-tuple is let through from outside
Additional feature
  Rules to allow or block traffic
How can a firewall be circumvented?

## Slide 5: Network Address Translation
Limited IP address space
  Use reserved space for home/corporate networks: 192.168/16 or 10/8
  Use only one IP address toward Internet
NAT translates between outside and inside addresses
  How can multiplexing/demultiplexing be achieved?

## Slide 6: Network Address Translation

## Slide 7: Network Address Translation
NAT box tracks connections
  Port number identifies connection
  NAT box overwrites layer 3/4 headers

## Slide 8: Transport layer systems
Firewall and NAT keep track of similar information
  Functionality often combined in same system
  Home gateways typically implement firewalls, NAT, DHCP
More sophisticated firewalls also use content filter
  Requires application layer system