## Slide 1: ECE 671 – Lecture 15
MultiPath TCP
Material from http://multipath-tcp.org/

## Slide 2: Motivation
Mobile, wireless clients
ECMP
Data Centers

## Slide 3: Traditional Wireless
3G celltower
IP 1.2.3.4

## Slide 4: Traditional Wireless
3G celltower
IP 1.2.3.4
IP 5.6.7.8

## Slide 5: Traditional Wireless
3G celltower
When IP addresses change TCP connections have to be re-established !
IP 1.2.3.4
IP 5.6.7.8

## Slide 6: Equal Cost Multipath
Packets from one TCP connection (same 5-tupel) follow same path
Different flows might follow different paths
ECMP implementation
Packet arrival :
Hash(IPsrc, IPdst, Prot, Portsrc, Portdst) mod #oif
Notes: ECMP – Equal Cost Multi-Path Routing

## Slide 7: CLOS Data Center Network

## Slide 8: Design Objectives
Evolution of TCP
Does not require modification of applications
Works in the current Internet
Works everywhere were regular TCP works!

## Slide 9: TCP Connection Establishment
Three-way handshake
SYN,seq=1234,Options
SYN+ACK,ack=1235,seq=5678,Options
ACK,seq=1235,ack=5679

## Slide 10: Data Transfer
seq=1234,"abcd"
ACK,ack=1238,win=4
seq=1238,"efgh"
ACK,ack=1242,win=0

## Slide 11: Connection Release
seq=1234,"abcd"
RST

## Slide 12: Connection Release
seq=1234,"abcd"
ACK,ack=1239
FIN,ack=350
seq=345,"ijkl"
FIN, seq=1238
FIN,seq=349

## Slide 13: Identification of TCP Connection
  Four tuple
  IPsource
  IPdest
  Portsource
  Portdest
  All TCP segments contain the four tuple
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP

## Slide 14: New Bytestream Model
Client
Server
ABCDEF...111232
0988989 ... XYZZ
IP:1.2.3.4
IP:4.5.6.7
IP:2.3.4.5
IP:6.7.8.9
B
C
D
A

## Slide 15: MultiPath TCP Protocol
Control Plane
  How to manage TCP connection that uses several paths?
Data Plane
  How to transport data?
Congestion Control
  How to perform congestion control over multiple paths?

## Slide 16: MultiPath TCP Protocol
Control Plane
  How to manage TCP connection that uses several paths?
Data Plane
  How to transport data?
Congestion Control
  How to perform congestion control over multiple paths?

## Slide 17: A naïve Approach
SYN+ACK+Option
ACK
seq=123, "abc"
seq=126, "def"

## Slide 18: Not Working!
SYN+Option
SYN+ACK+Option
ACK
seq=123, "abc"
seq=126, "def"
There is no corresponding TCP connection

## Slide 19: Design Decisions
A multipath TCP connection is composed of one or more regular, combined TCP subflows
Host maintains state that glues TCP subflows that compose a TCP multipath connection together
    Each TCP subflow is sent over a single path and appears like a regular TCP connection along this path

## Slide 20: Multipath TCP Architecture
Physical
Datalink
Network
Transport
Application
Multipath TCP
TCP1
socket
TCP2
TCPn
...
Application
A. Ford, C. Raiciu, M. Handley, S. Barre, and J. Iyengar, “Architectural guidelines for multipath TCP development", RFC6182 2011.

## Slide 21: Two Subflow Example
SYN+Option
SYN+ACK+Option
ACK
SYN+OtherOption
SYN+ACK+OtherOption
ACK

## Slide 22: How to combine subflows?
SYN+Option
SYN+ACK+Option
ACK
SYN+OtherOption
SYN+ACK+OtherOption
ACK
How to link with
blue subflow ?

## Slide 23: How to link subflows?
SYN, Portsrc=1234,Portdst=80+Option
SYN+ACK[...]
ACK
SYN, Portsrc=1235,Portdst=80
+Option[link Portsrc=1234,Portdst=80]
A NAT could change addresses and port numbers

## Slide 24: How to link subflows?
SYN, Portsrc=1234,Portdst=80 +Option[Token=5678]
SYN+ACK+Option[Token=6543]
ACK
SYN, Portsrc=1235,Portdst=80
+Option[Token=6543]
MyToken=5678
YourToken=6543
MyToken=6543
YourToken=5678

## Slide 25: Subflow Agility
Multipath TCP supports
  Addition of subflows
  Removal of subflows

## Slide 26: TCP Subflows
Which subflows can be associated to a Multipath TCP connection ?
  At least one of the elements of the four-tuple needs to differ between two subflows
    Local IP address
    Remote IP address
    Local port
    Remote port

## Slide 27: MultiPath TCP Protocol
Control Plane
  How to manage TCP connection that uses several paths?
Data Plane
  How to transport data?
Congestion Control
  How to perform congestion control over multiple paths?

## Slide 28: How to Transfer Data?
seq=123,"a"
seq=124,"b"
seq=125,"c"
seq=126,"d"
ack=124
ack=126
ack=125
ack=127

## Slide 29: In today’s Internet
seq=123,"a"
seq=124,"b"
seq=125,"c"
ack=124
ack=126
ack=125
Gap in sequence numbering space
Some DPI will not allow this !

## Slide 30: Multipath Data Transfer
Two levels of sequence numbers
Multipath TCP
TCP1
socket
TCP2
Multipath TCP
TCP1
socket
TCP2
ABCDEF
Data sequence #
TCP1 sequence #
TCP2 sequence #

## Slide 31: Multipath Data Transfer
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=2, seq=124,"c"
DAck=1,ack=124
DAck=3, ack=125
DAck=2,ack=457

## Slide 32: How to deal with losses?
Data losses over one TCP subflow
  Fast retransmit and timeout as in regular TCP
Dseq=0,seq=123,"a"
DAck=1,ack=124
Dseq=0,seq=123,"a"
DAck=1,ack=124

## Slide 33: Subflow failure
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=0,ack=457
Dseq=0,seq=457,"a"
DAck=2,ack=458

## Slide 34: Retransmission heuristics
Fast retransmit is performed on the same subflow as the original transmission
Upon timeout expiration, reevaluate whether the segment could be retransmitted over another subflow
Upon loss of a subflow, all the unacknowledged data are retransmitted on other subflows

## Slide 35: Flow Control
How should the window-based flow control be performed ?
  Independent windows on each TCP subflow
  A single window that is shared among all TCP subflows

## Slide 36: Independent Windows
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=100
Dseq=2,seq=457,"c"
DAck=3,ack=458,win=100
DAck=1,ack=124,win=0

## Slide 37: Independent Windows Problem
Impossible to retransmit, window is already full on green subflow
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=0

## Slide 38: Single window approach
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=10
Dseq=2,seq=457,"c"
DAck=3,ack=458,win=10
DAck=1,ack=124,win=10

## Slide 39: Middle box impact
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=100
DAck=1,ack=124,win=100
DAck=2,ack=457,win=5

## Slide 40: Multipath TCP Windows
Multipath TCP maintains one window per Multipath TCP connection
  Window is relative to the last acked data (Data Ack)
  Window is shared among all subflows
    It's up to the implementation to decide how the window is shared
  Window is transmitted inside the window field of the regular TCP header
  If middleboxes change window field,
    use largest window received at MPTCP-level
    use received window over each subflow to cope with the flow control imposed by the middlebox

## Slide 41: This is not fiction

## Slide 42: Comparison with QUIC
HOL blocking
FEC
Middle boxes?