## Slide 1: ECE 671 – Lecture 2
Review of Internet Protocols Link Layer

## Slide 2: Structuring networks and protocols
Goal of network:
  Provide communication for distributed applications
How to organize networks in such a way that they
  Work correctly?
  Are scalable to large number of nodes?
  Can achieve high performance?
  Are interoperable across different technologies and uses?

## Slide 3: Example network
How to achieve end-to-end data exchange?

## Slide 4: Internet architecture
Designing the structure of the Internet was a difficult problem
  Many contributions
  One example: TCP/IP

## Slide 5: Internet architecture
“Hourglass architecture”
Achieves interoperability
  Single, common network layer protocol: Internet Protocol (IP)
  All network nodes need to support this protocol
Supports diversity
  Different link/physical layer protocols below
  Different transport/application layer protocols above

## Slide 6: Next Gen. Internet Architecture
Information Centric Networking (ICN):
Move from host-centric to content/information-centric paradigm

## Slide 7: Services provided by layers
Each layer in protocol stack provides a “service”
  Uses service from lower layers
Benefits of layering
  Isolates complexity
  Clearly defined interfaces
Protocols implement functionality within layer

## Slide 8: Protocols
Protocols define communication between entities
  Format and order of messages
  Actions taken on transmission and/or receipt of message or other event
Protocols use headers (and trailers) for control information
  Naming depends on layer

## Slide 9: Network devices
Network devices differ by highest layer processed
  Devices can process/modify headers up to that layer
  Switches and routers are most common

## Slide 10: Review of specific protocols
We will briefly review three protocols
  Link layer: Ethernet
  Network layer: Internet Protocol (IP)
  Transport layer: Transmission Control Protocol (TCP)
For full details
  Networking textbooks
  RFCs

## Slide 11: Link layer
Communication between “neighboring” interfaces
What are the challenges?

## Slide 12: Link layer
Point-to-point guided medium is straightforward
  One side sends, other side receives (coding, timing, etc. is handled by physical layer)
  Duplex operation by duplicating medium
Multiple access case is more interesting
  Multiple nodes share guided or unguided medium
  Need to consider:
    Naming
    Medium access protocol
    “Strange” cases (e.g., hidden terminal problem)

## Slide 13: Medium access principles
How should nodes share a medium?

## Slide 14: Medium access principles
How should nodes share a medium?
  Do not interrupt ongoing transmissions
  When transmitting, stop after a while
  Allow for fair sharing among all nodes
  Allow efficient use of medium
  Do not require central control
  Etc.

## Slide 15: Side note: delays in networking
What delays are encountered in networks?
What is a typical range of each delay?

## Slide 16: Side note: delays in networking
What delays are encountered in networks?
  Transmission delay
  Propagation delay
  Processing delay
  Queuing delay
What is a typical range of each delay?
  Assumption: 1Gbps, 1250-byte packet, 1000km, 200000km/s
  Transmission delay: 10 microseconds
  Propagation delay: 5 milliseconds
  Processing delay: low microseconds
  Queuing delay: transmission delay of queued packets

## Slide 17: Signal propagation
At link layer, signal propagation delay matters
  Space-time diagram illustrates events
  Slope of lines determined by propagation speed
    Typically: 2/3 speed of light of light (~200,000 km/s)

## Slide 18: ALOHA protocol
Propagation delay may cause collisions on medium
  Even if all stations check to see if medium is available
Slotted ALOHA protocol
  Discrete time slots
  Each node makes random choice to transmit in slot or not
Pure ALOHA
  No time slots
  Each note makes random choice to transmit at any time

## Slide 19: Slotted ALOHA
Assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only at slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
Operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 20: Slotted Aloha
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 21: Slotted ALOHA Efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel
used for useful
transmissions 37%
of time!
!

## Slide 22: Analysis of ALOHA
Slotted ALOHA analysis
  Probability that k frames are generated during interval
    Poisson distribution: Pr[k]=Gke-G/k!
    G is rate of frame generation (new and retransmission)
  Probability of successful transmission
    Success if no other frame generated (P0): S=GP0=Ge-G
ALOHA analysis
  Frame overlaps two slots
  Probability that no other frame is generated during two slots:
    P0=e-2G
    Success S=GP0=Ge-2G
Max throughput:
  37%@G=1.0 (slotted ALOHA)
  18%@G=0.5 (ALOHA)

## Slide 23: CSMA/CD protocol
How can we improve ALOHA?
  Don’t send when somebody else has already started
  Stop when interference is already happening
    Why do we need to do that if we don’t start sending when somebody else sends?
Carrier Sensing (CS)
  Listen on channel
  Only send when nobody else is transmitting
Collision Detection (CD)
  Listen to own transmission on channel
  If garbled then stop transmitting

## Slide 24: CSMA/CD Collision
Collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
Collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 25: CSMA/CD example
A

## Slide 26: Ethernet
IEEE 802.3 protocol
Medium access with CSMA/CD
Truncated exponential backoff
  Wait for random number of 512 bit-times
  After c collisions: uniform distribution over [0…2min{c,10}-1]
  After 16 collisions: transmission aborted
Limitations
  Max 2.5km of cable, thus RTT limited to 51.2µs
  Corresponds to 64 bytes @ 10Mbps

## Slide 27: Ethernet Switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 28: Simultaneous Transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 29: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 30: Self-learning Switch
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 31: VLANs
Port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
Switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 32: Port-based VLAN
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
router

## Slide 33: Spanning Multiple Switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 34: 802.1Q VLAN Frame Format
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 35: Related topics
Next: network layer
  Combining links to a network
Later: switches and bridges
  Organization of layer 2 links into local area networks (LAN)
  Algorithms for reaching particular nodes in a LAN